F/W Upgrade Procedure:

Please download the latest official firmware file archive from the following link:

- 16CH F/W：ftp://211.75.84.102/Firmware/16CH_0050.rar

- 8CH F/W：ftp://211.75.84.102/Firmware/8CH_1167.rar

Unzip the archive (5 files in total) onto the root directory of a USB disk and follow the following steps to perform the update:

- Insert the USB disk to the USB slot. DVR will suggest that USB disk is now connected. Go into the DVR OSD. Select “MENU” -> “SYSTEM INFO” -> “Upgrade” to start the process.

- The DVR will now start the 1st stage of the update and automatically reboot after 2 minutes. After the reboot, the system will prompt “Upgrade Device Firmware, are you sure?”. Press “YES” to continue to the 2nd stage.

- After the 2nd stage of the update process, the system will again automatically reboot after 1 minute. After the final reboot, the update process is now completed.

- Verify the update by going to the OSD. Select “MENU”->”SYSTEM INFO”. The version number is shown on the bottom of the menu.For 16 channels, the version number should be 0050-1049-1017-1035-02-1212.For 8 channels, the version number should be 1167-1049-1017-1035-02-1212

WARNING: PLEASE DO NOT REMOVE THE USB DISK FROM THE USB SLOT OR UNPLUG THE POWER UNDER ANY CIRCUMSTANCE DURING THE UPDATE PROCESS.