MyKEY  Instructions for use and warnings

WARNINGS

This manual contains important information, read it carefully and store it safely for future programming and maintenance operations.

Caution: Keep the transmitter out of reach of children.

For the product cleaning use a cloth slightly damped with water. Seepage of waters of use of corrosive substances and solvents could damage the product.

Perform cleaning and maintenance operation out of the range of radio receiver to avoid the automation accidentally activates.

Do not pollute the environment. Ensure the product is passed to the authorised collection centres for safe disposal.

PRODUCT DESCRIPTION and INTENDED USE

| 3-Channel Radio Transmitter |
| --- |
| Frequency | 433,92 MHz |
| Power supply (battery) | 12Vdc – 23A |

MyKEY transmitters are exclusively designed to control electric gates, doors, rolling shutters or similar products of MYGATE brand.

Any other use than above described has to be considered as inappropriate and strictly prohibited.

MyKEY is a 3 channel radio transmitter: each button A, B or C of the transmitter can activate different function on the same automation or control 3 distinct automations.

PROGRAMMING

The transmitters MyKEY are ready to be saved on the receiver card. Please follow the installation manual of the control panel (paragraph “programming of radio transmitters”) or of the external receiver card for radio saving procedure.

CHANGING THE RADIO CODE

MyKEY transmitters have a preset radio code, random generated. You can replace this radio code with a new one, also random generated, at any time by following this procedure:

1) Simultaneously press buttons B and C (about 4-5 seconds) till the red light of the remote control illuminates.

2) Hold button B pressed and at the same time release button C and press it again twice. The two lights, red and green, should alternating blink to show that the generation of a new random code succeeded.

3) Now you can release button B also. The remote control is ready to transmit with a new radio code. N.B. – if you had previously stored the remote control on any receiver card you should repeat the storing procedure once you change the code of the remote control.

BATTERY REPLACEMENT

A progressive reduction in the radio range and in light brightness can be due to a low battery. Please proceed as follows to replace it:

1) Remove the battery cover under the transmitter by levering it on the upper edge (fig.3).

2) Replace the battery with a new one paying attention to the specified polarity (fig.4) and close back the cover.

CONFORMITY DECLARATION

MyGATE is a trademark by PROTECO Srl

PROTECO Srl declare that all radio transmitters MyKEY, model PTX3UBI, PTX3UGI and PTEX3UVI, comply to the essential requirements of R&TTE 99/5/CE Directive for the use the products have been designed for.

Castagnito, 3 ottobre 2011                                   Angela Gallo

Managing Director