TX312  433.92Mhz – Instructions for use

DESCRIPTION and TECHNICAL SPECIFICATIONS

| 3-Channel Radio Transmitter |
| --- |
| Frequency | 433,92 MHz |
| Power supply (battery) | 12Vdc – 23° |

TX312 transmitters are exclusively designed to control electric gates, doors, rolling shutters or similar products.

PROGRAMMING

The transmitter TX312 is ready to be saved on the receiver card. Please follow the installation manual of the control panel (paragraph “Programming of radio transmitters”) or of the external receiver card for radio saving procedure.

CHANGING THE RADIO CODE

TX312 have a preset radio code random generated. You can replace this radio code with a new one, also random generated, at any time by following this procedure:

1) Simultaneously press buttons B and C (about 4-5 seconds) till the red light of the remote control illuminates.

2) Hold button B pressed and at the same time release button C and press it again twice. The two lights, red and green, should alternating blink to show that the generation of a new random code succeeded.

3) Now you can release button B also. The remote control is ready to transmit with a new radio code. N.B. – if you had previously stored the remote control on any receiver card you should repeat the storing procedure once you change the code of the remote control.

HOW TO DUPLICATE A RADIO CODE

It’s possible to duplicate the code of a “master” remote control TX312 on a “slave” remote control TX312:

1) Simultaneously press buttons B and C of the “slave” transmitter, until the red light illuminates (N.B: do not over-press the button to avoid the transmitter to enter into the new code generation mode).

2) As soon as the red light blinks release buttons B and C. (you can check that the “slave” transmitter has entered the radio learning mode by pressing any button”: the red light only should illuminate).

3) Put the “slave” and the “master” transmitter back to back (fig.2). Hold a button of the “slave” transmitter pressed and at the same time press once the button on the “master” transmitter. The green and red lights on the “slave” transmitter should alternate blink.

4) Release the button on the “slave” transmitter. The radio code has been duplicated.

CONFORMITY DECLARATION

PROTECO Srl declare that all radio transmitters TX312, model PT3P1I, comply to the essential requirements of R&TTE 99/5/CE Directive for the use the products have designed for.

Castagnito, 3 ottobre 2011                                   Angela Gallo

Managing Director