# PRODUCTS

# Swing Gates

myAster

Double swing gate automation kit, for gate leafs up to 3,5 m.

Powerful ad easy-to install it’s the perfect solution to suits most of residential and commercial swing gates. Electromechanical blocked rams (no extra electric lock is needed), completely in aluminium.

Download product datasheet

myHook

Double swing gate automation with articulated arms, for leafs up to 2m.

Ideal for large pillars, very light gates or outwards opening. Built-in electric limit-switches and embedded control panel.

Download product datasheet

myFlow

Double swing gate automation, wheel-driven system.

Unlimited opening angle and easy installation. Suitable for gates with long and light leafs, invar or outward opening, it can overcome slight sloping driveways and uneven ground. Maximum leaf’s weight 150Kg. Compact ground surface with adequate grip is needed.

Download product datasheet

Swing Gate Accessories

MEL03

Interface module to connect a pre-existing electric lock to the control panel (for Q71A, Q71B, Q56 control panels).

RT18

Vertical Electric-lock 12V, double cylinder with ground clutch. Suitable for double swing gate.

# Sliding Gates

myStrike

Sliding gate automation for rack-driven gates up to 800Kg.

Powerful, quiet, with a compact design. Perfect for either wrought iron or solid timber sliding gates. Embedded pre-wired control panel with anti-crushing system and self-learning function of the working times.

Download product datasheet

Sliding Gate Accessories

B117

Nylon toothed M4 rack with inner iron frame. Snap-fit bars 0.5m.

Package for 2m (4 bars).

RC21

Sliding gate safety edge. Electromechanical edge with iron frame and rubber 60mm profile.

Supplied with sensor and wire (2m).

# Garage Doors

myLibra

Garage door opener for sectional doors up to 12m² wide and 100Kg of weight.

Programming display, courtesy light and alert in case of door left open.

Smooth and precise movement. Anti-crushing system with obstacle detection.

Download product datasheet

Garage Door Accessories

PARC01

Adapter bracket for counterweights balanced doors.

MLIRO7

Release kit for emergency opening from outside the garage. For Libra garage door automation.

# Accessories

myKEY

3-button radio-transmitter, frequency 433.92MHz. Random generated transmitting codes. Each remote controller can operate up to 3 sets of gate/garage door systems. Available in lime, dark grey or purple colour.

myRS

Key-switch with one micro. Suitable for surface or semi-recessed mounting.

myRT

Surface mounted digital keypad, 60 user codes. Power supply 12V-24Vac/dc.

myRL

Flashing light 24V-10W.

Suitable for wall mounting or pillar mounting.

myRF

Set of safety photocells, they can be mounted on the wall, on the pillar or on PRF10 photocells post.

12-24V power supply.

RF10

Post for myRF photocell, 55cm high, in painted iron.

PANT01

Radio external aerial 433.92MHZ, complete with mounting bracket and 3.5m coaxial wire.

It can increase the receiving range in case of low radio signal.