SPW-100

spw-100_int 02/09

# INDOOR SIREN

The SPW-100 indoor siren is dedicated to operation in intruder alarm systems. It can be used with any source of alarm signal in which 12V voltage occurs at the signal output under emergency situation. The modulated audible signal is generated by means of a piezoelectric transducer. There are three different types of acoustic signaling to choose from.

The EC declaration of conformity and certificates in current wording can be downloaded from www.satel.pl.

# FIGURE 1:

1 -	terminals:

+SA- – acoustic signaling

TMP – tamper contact

2 -	tamper contact which reacts to cover opening

3 -	piezoelectric transducer leads

4 -	audible signal setting pins

5 -	description of jumper settings for corresponding audible signal.

# FIGURE 2

1 -	cable inlets

2 -	mark which is to be aligned with cover mark when closing the siren housing

3 -	fixing screw holes

4 -	piezoelectric transducer

5 -	electronics PC board (see Fig. 1).

# INSTALLATION

The SPW-100 siren is to be installed on a flat surface at a hard-to-reach place so as to minimize the risk of tampering. The siren should be secured to the surface by using screws and expansion plugs (the screws and expansion plugs are included in the siren delivery set).

- Open the siren housing – press the cover slightly and turn it firmly clockwise.

- Pass the cable through the corresponding inlet.

- Attach the rear panel of the housing to the wall.

- Connect the + SA – terminals to the corresponding output of the control panel.

- Connect the TMP terminals to the tamper circuit of the control panel.

- Using the JP1-JP5 pins, set the type of audible signal according to the description on the electronics board.

- Close the siren housing, remembering that the marks on the cover and on the rear panel of the housing must be aligned.

- Carry out functional test of the siren.

# TECHNICAL DATA

Supply voltage	12 V DC 15%

Maximum current consumption	240 mA

Sound intensity (at a distance of 3 m)	100 dB

Environmental class	I

Working temperature range	+5...+40° C

Dimensions	130 x 130 x 30 mm

Weight	146 g

SATEL

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl