SPW-210

spw-210_int 06/09

# INDOOR SIREN

The SPW-210 indoor siren is designed for operation in the intruder alarm systems.

# FEATURES

Acoustic alarm generated by means of piezoelectric transducer.

3 selectable tones.

Tamper protection in 2 ways – cover opening or tearing housing from the wall.

Housing made of PC LEXAN high-impact polycarbonate, featuring a very high mechanical strength.

The latest EC declaration of conformity and product approval certificates are available for downloading on website www.satel.pl

FIGURE 1: View of the siren

1	-	housing base

2	-	screws securing the siren to its mounting surface

3	-	piezoelectric transducer

4	-	tamper contact

5	-	electronics board (see: Fig. 2)

6	-	screws locking the cover

7	-	screw fixing the housing tamper element to mounting surface

8	-	cover

FIGURE 2: View of the electronics board

1	–	pins for tone selection

2	–	description of setting jumpers for respective acoustic signals

3	–	wires to piezoelectric transducer

4	–	wires to tamper contact

5	–	terminals:

TMP – tamper contact (NC)

+SA- – acoustic signaling

FIGURE 3: Selection of acoustic signal type

A – tone 1; B – tone 2; C – tone 3 ( - pins shorted;  - pins open).

# INSTALLATION AND CONNECTION

The siren may only be used indoor.

The siren should be installed on a flat surface by means of screws and expansion bolts.

All connections should only be made after the alarm system power supply has been disconnected.

FIGURE 4: Method of connecting the siren to high-current outputs of INTEGRA 32 control panel

Output OUT1 triggers acoustic signaling (the high-current output with normal polarity – activation means that +12 V voltage is supplied). Zone Z1 should be programmed as 24 h tamper.

FIGURE 5. Siren dimensions.

# SPECIFICATIONS

Power supply voltage	12 V DC 15%

Maximum current consumption	110 mA

Sound pressure level (at 1 m distance)	up to 120 dB

Environmental class	II (EN50130-5)

Operating temperature range	-10…+55°C

Dimensions	87 x 134 x 37 mm

Weight	159 g

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl