# General

The DB-100 base (Fig. 1) allows you to install and connect the DMP-100, DRP-100 and DCP-100 conventional detectors to the fire alarm control panel. The wires to be connected to the base can be either concealed or surface mounted.

The DB-100 base can be installed by means of the intermediate PDB-100 industrial spacer (Fig. 2). The use of the industrial spacer is recommended for installing detectors in spaces where the phenomenon of water vapor condensation may occur on the ceiling.

# DB-100 base wiring

Disconnect power before making any electrical connections.

Connect wires to the screw terminals marked with the following numbers:

1 – terminal „-”;

2 – terminal "-", dedicated for remote alarm indicator;

3 – terminal „+”;

4 – terminal „+”;

5 – terminal dedicated for screen connection.

Fig. 4 shows a typical connection.

# Specifications

## DB-100 detector base

Dimensions	ø106 x 26 mm

Weight	52 g

## PDB-100 industrial spacer

Dimensions	131 x 131 x 35 mm

Weight	76 g

DETECTOR BASE

DB-100

INDUSTRIAL SPACER

PDB-100

db-100_en 07/13

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. 58 320 94 00

info@satel.pl

www.satel.eu

druk (4 na 1)

3,4,3,4,1,2,1,2