CONTENTS

1	Main menu	3

2	VERSA - Structure	4

2.1	System	4

2.1.1	Partitions	5

2.2	Hardware	6

2.2.1	Main board	6

2.2.2	Built-in modules	6

2.2.2.1	INT-VG	7

2.2.2.2	VERSA-ETH	7

2.2.2.2.1	ETHM	8

2.2.2.2.2	GSM	9

2.2.2.2.3	Messaging	11

2.2.2.2.4	Starting the e-mail messaging	12

2.2.2.2.5	Starting the SMS messaging	13

2.2.2.2.6	Remote firmware update	13

2.2.3	Expansion modules	14

2.2.3.1	Addresses	15

2.2.3.2	Identification	16

2.2.3.3	VERSA-LCD	16

2.2.3.3.1	Volume [VERSA-LCDM]	17

2.2.3.4	VERSA-LCDR	18

2.2.3.4.1	Volume	19

2.2.3.4.2	Proximity cards	20

2.2.3.5	VERSA-LED	20

2.2.3.6	VERSA-LCDM-WRL	21

2.2.3.6.1	Volume	23

2.2.3.6.2	Proximity cards	23

2.2.3.7	INT-TSG	24

2.2.3.7.1	Status screen	26

2.2.3.8	INT-TSH	27

2.2.3.8.1	Status screen	29

2.2.3.9	INT-RX	30

2.2.3.9.1	Adding 433 MHz keyfob	31

2.2.3.9.2	Removing 433 MHz keyfob	32

2.2.3.10	VERSA-MCU	32

2.2.3.10.1	Adding 433 MHz wireless detector	33

2.2.3.10.2	Removing 433 MHz wireless detector	33

2.2.3.11	ACU-100	33

2.2.3.11.1	Adding ABAX wireless device	36

2.2.3.11.2	Removing ABAX wireless device	37

2.2.3.11.3	Adding ABAX keyfob	37

2.2.3.11.4	Removing ABAX keyfob	38

2.2.3.11.5	Adding the wireless keypad	38

2.2.3.11.6	Removing the wireless keypad	38

2.2.3.11.7	Configuring the ABAX wireless devices	38

2.2.3.12	Zone expander	40

2.2.3.13	Output expander	41

2.2.3.14	INT-IT	41

3	Global parameters	42

3.1	Options	42

3.2	Times	45

4	Zones	46

4.1	Zone types	50

5	VERSA - Outputs	52

5.1	Outputs	52

5.1.1	Output functions	54

5.2	Quick control	55

6	VERSA - Timers	55

7	VERSA - Reporting	55

7.1	Monitoring Stations	56

7.2	GSM/ETHM reporting	58

7.3	SIA-IP	59

7.4	Event codes	59

7.5	Starting the reporting	60

7.5.1	Reporting via analog telephone line	60

7.5.2	Reporting via Ethernet network	61

7.5.3	Reporting with the use of GPRS technology	61

7.5.4	Reporting with the use of CSD technology	62

7.5.5	Reporting by means of SMS messages	62

7.5.6	Reporting via GSM voice channel	62

8	VERSA - Tel. messaging	62

8.1	Telephone no.	62

8.2	Event assignment	63

8.3	SMS/Pager messages	63

8.4	Starting the telephone messaging	63

8.4.1	PAGER messaging	64

8.4.2	Voice messaging	64

8.4.3	SMS messaging	65

9	SMS control	65

10	VERSA - Users	65

10.1	Users	65

10.1.1	Adding a user	66

10.1.2	Removing a user	66

10.1.3	Adding proximity card	66

10.1.4	Removing proximity card	67

10.2	User schedules	67

10.2.1	Rights	67

11	Data comparison	68

12	VERSA Event log	68

12.1	Choose	69

12.2	Print	70

12.3	Grade2 events	70

13	System state	71

13.1	Keypad	71

13.2	VERSA - Partitions state	71

13.3	VERSA - Zones state	71

13.4	Outputs and modules state	71

13.5	VERSA - Troubles	71

13.6	Module power supply	71

13.7	VERSA - Wireless devices	71

14	Configuration	72

14.1	Port RS-232	72

14.2	Modem	72

14.2.1	Configuring the modem connected to computer	73

14.3	Data	73

15	Connection	73

15.1	Port USB - VERSA Plus	74

15.2	Modem 300bps	75

15.3	VERSA Plus - GSM modem	77

15.4	TCP/IP: DLOADX -> ETHM	80

15.5	TCP/IP: DLOADX <- ETHM/GPRS	81

15.6	TCP/IP: SATEL server	83

15.7	Communication identifiers and establishing connection	84

16	Connection settings	85

17	Programming telephone numbers	86

18	Changing the DLOADX program access code	86

# Main menu

1 - type of alarm control panel.

2 - name of alarm system / data file.

3 - information on data writing/reading progress.

4 - information on the way of communication with the alarm control panel:

USB-HID - communication via the USB port,

Modem - communication via the modem,

TCP/IP - communication via the Ethernet / GPRS network.

###### Buttons

- click to open the VERSA - Structure window.

- click to open the Global parameters window.

- click to open the VERSA - Zones window.

- click to open the VERSA - Outputs window.

- click to open the VERSA - Timers window.

- click to open the VERSA - Reporting window.

- click to open the VERSA - Tel. messaging window.

- click to open the SMS control window.

- click to open the VERSA - Users window.

- click to open the window with information on errors made when configuring the alarm system (e.g. nonconformity with requirements of EN 50131 for Grade 2, when Grade 2 option is enabled).

- click to open the Data comparison window.

- click to read data from the control panel.

- click to write data to the control panel.

- click to open the event log window.

- click to terminate data reading/writing.

- click to write computer clock time to the control panel.

- click to display virtual keypad (see: Keypad).

- click to display the drop-down menu, in which the system supervisory tools are available (see: System state).

- click to open the Configuration window. The Configuration window will not open, when the DLOADX program is connected to the control panel via modem, Ethernet or GPRS. Instead, a window with the connection information will open. Opening the Configuration window will only be possible after the connection is ended.

- click to display the drop-down menu, where you can select the way of communication with the alarm control panel (see: Connection).

- click to:

- interrupt / resume connection via USB port,

- open the connection information window (remote programming).

Color of the button icon has the following meanings:

green - connection OK,

alternating green and yellow - data transfer going on,

gray - no connection.

# VERSA - Structure

System

Hardware

## System

The logical structure of the system, i.e. the partitions and the zones belonging to them, is presented in the tree form. You can click on any of the elements of the tree to proceed to its programming.

Presented in tabulated form is a list of all zones, showing the partitions to which they are assigned, as well as the zones that will be armed after the day or night armed mode is activated. Double click to make changes to individual fields of the table. The X symbol means that the zone is assigned to a partition / is armed in case of a given armed mode.

Partitions

Zones

### Partitions

The partition is a separated area within the premises protected by the security alarm system. The subdivision into partitions enables arming/disarming the system only in part of the protected area, as well as limiting access to some portion of the premises to selected users. You can create 2 partitions.

###### Partition parameters

Name - individual name of the partition (up to 16 characters).

Partition’s zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - the zone does not belong to the partition,

orange - the zone belongs to the partition,

brown - the zone belongs to both partitions.

Double-click on the field to add the zone to the partition / remove the zone from the partition.

Partition exit delay - the time counted from the moment of starting the partition arming procedure which enables the protected area to be left without triggering an alarm. Violation of the 0. Entry/Exit, 1. Entry/Exit final, 2. Entry/Exit route or 4. Double knock type zones during the exit delay time will trigger no alarm. Up to 255 seconds can be programmed.

Note: The exit delay countdown can be terminated by means of the 1. Entry/Exit final or 16. Exit delay terminator type zones.

Infinite exit delay - if the option is enabled, the partition exit delay can only be ended by means of the 1. Entry/Exit final, 16. Exit delay terminator or 17. Shunt lock type zones. If the exit delay countdown is not completed, the armed mode will not be activated (only the 3. Instant type zones will be armed).

Entry delay - the time counted from the moment of entry into the protected area which enables the partition to be disarmed before triggering an alarm. This parameter applies to the 0. Entry/Exit and 1. Entry/Exit final type zones. The delay programmed for the partition is taken into account in case of the zones for which the value 0 has been individually programmed. The delay is programmed in seconds. Up to 255 seconds can be programmed. If the value 0 is programmed, the zone will act as an instant one.

Warning time - the time of warning alarm signaling for the partial armed mode (see: Warning in partial arming zone option - Zones). The time is programmed in seconds. Up to 255 seconds can be programmed. If the value 0 is programmed, the Warning time will be 30 seconds. After expiry of the Warning time, unless the partition is disarmed, the burglary alarm will be triggered.

Note: The Warning time parameter does not apply to the time of signaling the warning alarm which is generated when mistakes are made when entering into the protected object (see: Warning alarm global option - Options).

Verification time - programming a value different from 0 means activating the alarm verification feature in the partition. Subject to verification are alarms from 0 to 5 type zones. The Verification time runs from the moment of alarm being triggered by such a zone. If during the Verification time an alarm is triggered by another zone in the partition, programmed as 0 to 5 type, the control panel will report a verified alarm. The time is programmed in minutes. Up to 255 minutes can be programmed.

Timer priority - if this option is enabled, the timer always disarms the system (if the option is disabled, the timer will only disarm the system, if it armed it).

Entry delay in Day Arm - with this option enabled, after partition is armed in day mode with no delay, the entry delay time remains valid (there is only no exit delay time). With this option disabled, after partition is armed with no delay, there is neither exit delay nor entry delay time.

Auto-arming delay - the time counted from the moment when the timer is to arm the partition, enabling the arming to be deferred. The delay time is programmed in seconds. Up to 255 seconds can be programmed. Programming the value 0 means that the arming deferment will be unavailable.

Deferment time - the time by which the user can defer arming by the timer. The time is programmed in minutes. Up to 255 minutes can be programmed. Programming the value 0 means that the arming deferment will be unavailable.

Simple deferment - if the option is enabled, the user can defer auto-arming by pressing the  key twice during the auto-arm delay time countdown.

Single deferment - if the option is enabled, the user can only use the simple deferment once, so as to postpone the auto-arming. Subsequent arming deferments are only possible by using the A-arm defer. user function.

Timer priority - if this option is enabled, the timer always disarms the system (if the option is disabled, the timer will only disarm the system, if it armed it).

## Hardware

Displayed in the tab is information on the hardware, i.e. the control panel mainboard, built-in modules and the devices connected to the control panel communication bus. The system structure is displayed in tree form. Click on any element of the tree to start programming it.

Main Board

Built-in modules

Expansion modules

### Main board

TMP input signals in part. - the partition in which an alarm will be triggered on violating the TMP input on the mainboard.

Mainboard TMP input - name - individual name of the input (up to 16 characters).

Main Board: Zones - you can assign any numbers within the 1 to 30 range to zones on mainboard. By default, the mainboard zones have numbers from 27 to 30. If number 0 is assigned, the zone will not be supported.

### Built-in modules

The VERSA Plus control panel has built in:

Ethernet communication module,

GSM communication module,

voice module (INT-VG).

The Ethernet communication module and the GSM communication module are treated by the control panel as one device. Its default name is “VERSA-ETH” (this name can be changed).

INT-VG

VERSA-ETH

#### INT-VG

Voice module allows remote operation of the control panel from the telephone keypad (interactive voice menu). It can store 16 voice messages for telephone messaging.

---------------------------------------------------

Content of voice messages - you can enter in the table the content of voice messages that will be used for voice notification. To synthesize these messages, click on the VG-Soft button and start the VG-Soft program (before clicking on the VG-Soft button, save the changes made to the system data file on the computer).

###### Buttons

VG-Soft - the button launches the VG-Soft program, if it is installed on your computer (first time the button is pressed you may need to indicate the access path to the program). The VG-Soft program allows you to manage voice messages and define macro commands in the INT-VG module.

#### VERSA-ETH

Ethernet communication module enables:

reporting events via the Ethernet network,

sending event notifications using e-mail messages,

operating the alarm system from mobile devices using VERSA Control application,

programming the control panel via the Ethernet network.

GSM communication module enables:

reporting events via the GSM/GPRS network,

notification of events by means of voice or text (SMS) messages,

controlling the alarm system by means of SMS messages,

programming the control panel via the GSM/GPRS network.

---------------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - the partition in which tamper alarm will be triggered in the event of no communication with the device.

###### DLOADX

DLOADX server - address of the computer with DLOADX program. If the computer is not in the same local network as the control panel, it must be a public address. You can enter either the IP address or the domain name.

Port - number of the port TCP used for communication between control panel a computer with DLOADX program via Ethernet / GPRS. You can enter values from 1 to 65535. Default value: 7090.

DLOADX key - a string of up to 12 alphanumeric characters (digits, letters and special characters) which is used for data encryption during communication between control panel and computer with DLOADX program via Ethernet / GPRS.

SMS - control command that will be sent in the SMS message to initiate communication between control panel and DLOADX program. It depends on the SMS message content whether communication will take place via Ethernet, modem or GPRS (see: Connection). You can enter up to 8 alphanumeric characters (you can use spaces, but at least one character must be different from the space).

ETHM

GSM

Messaging

Remote firmware update

##### ETHM

ETHM - if the option is enabled, the built-in module is supported by the control panel. The option should be disabled, if the module is not to be used. Disabling the option will prevent the unnecessary reporting of troubles related to this module.

Obtain IP address automatically (DHCP) - if this option is enabled, the module will automatically download data on IP address, subnet mask and gateway from the DHCP server (in such a case, you do not have to program these parameters).

Note: The IP address assigned to the module can be read in the LCD keypad using the Module ver. user function available in the Tests submenu. For a detailed description of the function please refer to the user manual for the control panel.

IP address - module IP address.

Subnet mask - the mask of the subnet in which the module is working.

Gateway - IP address of the network device through which the other devices in the local network can communicate with devices in other networks.

Obtain DNS server address automatically - if this option is enabled, the DNS server IP address is downloaded automatically from the DHCP server. The option is available, when the Obtain IP address automatically (DHCP) option is enabled.

DNS server - IP address of the DNS server which is to be used by the module. It can be programmed, if the Obtain DNS server address automatically option is disabled.

Address to test - address of the device to which a ping command to test communication is to be sent by the module. You can enter IP address or domain name.

Period - the time interval between successive communication tests using the ping command. If value 0 is programmed, the communication test is disabled.

Tries no. before trouble - the number of failed communication tests (the module received no answer to the ping command sent), after which the trouble will be reported. If value 0 is programmed, the communication test is disabled.

DLOADX->VERSA-ETHM connection - if this option is enabled, it is possible to initiate connection with the control panel via Ethernet from the DLOADX program.

Satel server (LAN) - if this option is enabled, the control panel connects to the SATEL server via the Ethernet module, while the SATEL server makes it possible to establish communication with the control panel. For communication vie the SATEL server, you do not need to additionally configure the network device through which the module connects to the public network.

Notes:

For establishing communication with the SATEL server, the DNS server must be used.

For communication via the SATEL server, the ports of 1024-65535 range are used as outgoing ports. These ports must not be blocked.

Satel server (GSM) - if this option is enabled, the control panel connects to the SATEL server via the GSM module (GPRS), while the SATEL server makes it possible to establish communication with the control panel.

Notes:

Make sure that the SIM card tariff plan is suited to the requirements of communication via the SATEL server (GPRS connection to the server is active at all times).

If the Satel server (LAN) and Satel server (GSM) options are enabled at the same time, communication via the Ethernet module has priority. Communication via the GSM module will be established only if an attempt to establish communication to the SATEL server via the Ethernet module fails.

Communication with mobile application - if this option is enabled, communication with the control panel can be established from the mobile application. The option is available if the Satel server (LAN) option is enabled.

Push notifications - if this option is enabled, the VERSA CONTROL application can provide information about alarm system events by means of push notifications.

MAC - information on module hardware address.

ID - information on individual identification number for the purpose of communication via the SATEL server (programming by means of DLOADX program, operating by means of VERSA Control application). The ID number is assigned automatically by the SATEL server.

Note: If the control panel is to be used in another alarm system, the hitherto used ID number must be deleted. It can be done from the keypad, when programming the built-in communication modules, in the last step, if the control panel is connected to the SATEL server. Having deleted the old ID number, the control panel will receive a new one. The VERSA Control applications using the old ID number will be unable to connect to the control panel.

IP - information on the module local / public address.

Refresh - pressing the button will update information presented in the MAC, ID and IP fields.

Get Date and Time from a time server (LAN) - if the option is enabled, the control panel clock will be synchronized with the time server once a day through the Ethernet module.

Note: For communication with the time server, the DNS server must be used.

Get Date and Time from a time server (GSM) - if the option is enabled, the control panel clock will be synchronized with the time server once a day through the GSM module (GPRS).

Note: If the Get Date and Time from a time server (LAN) and Get Date and Time from a time server (GSM) options are enabled at the same time, time synchronization via the Ethernet module has priority. Time synchronization by means of the GSM module will take place only if an attempt to synchronize time via the Ethernet module fails.

Time zone - difference between the universal time (GMT) and the zone time. The parameter is required, if the control panel clock is to be synchronized with the time server.

##### GSM

###### SIM 1 / SIM 2

SIM 1 / SIM 2 - if this option is enabled, the given SIM card is supported by the control panel. Disable the option, if the given card is not to be used. Disabling the option will prevent unnecessary reporting of troubles related to that card.

PIN - PIN code of the SIM card.

Note: If a wrong PIN code is programmed, a trouble will be reported after using it. After 255 seconds the control panel will retry to use the PIN code. After the third attempt to use a wrong PIN code, the SIM card will be blocked. To unblock the card, remove it and insert into a cell phone, and then enter the PUK code.

GPRS APN - access point name for Internet GPRS connection.

Username - user name for Internet GPRS connection.

Password - password for Internet GPRS connection.

DNS server - IP address of DNS server to be used by the module.

Note: The GPRS parameters can be obtained from the GSM network operator.

SMS center no. - telephone number of the short message service center. It is used as a connecting link when sending SMS messages. If the number has been saved by the operator to the SIM card memory, it need not be programmed. Otherwise, if the control panel is to send SMS messages, it must be entered. The number must be suitable for the operator of network in which the SIM card is registered.

Lock time - the time during which switch-over to the other SIM card is impossible. For reporting, the transmission paths programmed as subsequent ones, if they require switch-over to the other card, will be skipped during the lock lime countdown (see: GSM/ETHM reporting). Entering the value 0 means that instant switch-over to the other SIM card is possible.

Return time - the time after which the other SIM card is to be used. Entering the value 0 means that automatic switch-over to the other SIM card will not take place.

Note: If two SIM cards are to be used, one of them must be treated as the priority card. It is recommended that return time equal to 0 be programmed for it.

###### USSD retransmit code

SMS - control command that will be sent in the SMS message together with USSD code. The control panel will run the USSD code and send the response received from the operator to the phone number from which the SMS message with control command was sent. You can enter up to 8 alphanumeric characters (you can use spaces, but at least one character must be different from the space). Owing to the USSD codes you can, for example, check the account balance of SIM card installed in the control panel. The SMS message must have the following form: xxxx=yyyy= (“xxxx” - the control command; “yyyy” - the USSD code supported by the GSM network operator).

Note: It is not advisable to use the advanced functions available due to the USSD service if menu is presented in response to the entered code.

any number - if the option is enabled, the SMS messages containing USSD codes can be sent from all telephone numbers. If the option is disabled, only from the phone numbers included in the Telephone numbers table.

###### Answering

Audio call answering - if the option is enabled, the module receives the incoming voice calls.

Any number for audio - if the option is enabled, the module receives all incoming voice calls. If the option is disabled, only from the phone numbers included in the Telephone numbers table.

Data call answering - if the option is enabled, the module receives the incoming modem connections (CSD data transmissions).

Any number for data - if the option is enabled, the module receives all incoming modem connections. If the option is disabled, only from the phone numbers included in the Telephone numbers table.

###### Telephone numbers

The table presents:

1...8 - telephone numbers from which it is possible to:

control the alarm system by means of SMS messages (a user must be assigned to the phone number),

initiate by means of SMS messages establishment of communication with the DLOADX program (Ethernet, GPRS, CSD),

send the USSD codes (a user must be assigned to the phone number),

establish voice connections with the control panel (if a user having the INT-VG access right is assigned to the phone number, he will get access to the voice menu without having to enter the code),

establish modem connections with the control panel.

Note: Options are available for some of the above described functions, which, if enabled, allow these functions to be run from any phone number.

T1...T8 - phone numbers which are notified by phone, and from which the functions available in the case of phone numbers 1...8 can also be executed. These numbers can be edited when configuring the messaging (see: VERSA - Tel. messaging).

Telephone no. - telephone number.

Note: Do not enter the same telephone number twice.

User - the user assigned to the telephone number. It depends on the user rights whether:

she/he will have access to the voice menu,

the control panel will execute the control command sent in the SMS message.

SMS - if the option is enabled, unknown SMS messages received by the module are sent to the phone number (e.g. information received from GSM operator).

##### Messaging

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the e-mail and SMS messaging are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

###### E-mail messaging

E-mail messaging (LAN) - if the option is enabled, the control panel can notify of occurrence of specified events by means of e-mail messages using the Ethernet module.

E-mail messaging (GSM) - if the option is enabled, the control panel can notify of occurrence of specified events by means of e-mail messages using the GSM module (GPRS).

Note: If the E-mail messaging (LAN) and E-mail messaging (GSM) options are enabled at the same time, e-mail messaging via the Ethernet module has priority. E-mail messaging via the GSM module will take place only if an attempt to send an e-mail message via the Ethernet module fails.

Email address - e-mail address to which messages are to be sent for notification of events.

ON - with this option enabled, it will be possible to send messages to the given e-mail address for notification of events.

Events type - define of which events the given e-mail address is to be notified.

Part. - define the partitions, about the events from which the given e-mail address is to be notified.

###### SMTP account

Note: It is required to have an e-mail account so as to enter its parameters in the DLOADX program for the purpose of e-mail messaging.

Mail server (SMTP) - address of outgoing mail server.

Server port - number of outgoing mail port.

User name - name of the e-mail account used for authorization by the SMTP server (login to e-mail account).

Password - the password used for authorization by the SMTP server.

Encryption - you can define if and how the outgoing mail is encrypted:

none - outgoing mail is not encrypted.

STARTTLS - outgoing mail will be encrypted using the STARTTLS protocol.

SSL/TLS - outgoing mail will be encrypted using the SSL/TLS protocol.

Subject - subject of the e-mail message. It will be inserted in each e-mail message to be sent.

Sender address - e-mail address which will be inserted in the outgoing e-mail message as the sender address. If this field is blank, the name of e-mail account will be treated as the sender address.

###### SMS messaging

SMS messaging - if the option is enabled, the control panel can notify of occurrence of specified events by means of SMS messages.

Telephone no. - phone number to which SMS messages with information about events are to be sent.

ON - with this option enabled, it will be possible to send SMS messages to the given telephone for notification of events.

Events type - define of which events the given phone number is to be notified.

Part. - define the partitions, about the events from which the given phone number is to be notified.

###### Buttons

Read - click to read the data related to e-mail messaging (these data are not read after clicking on the  button in the main menu).

Write - click to write the data related to e-mail messaging (these data are not written after clicking on the  button in the main menu).

Starting the e-mail messaging

Starting the SMS messaging

##### Starting the e-mail messaging

- Enable the E-mail messaging option.

- Enter the e-mail addresses to be notified, and enable the ON option for those addresses.

- Define the events of which the control panel is to notify.

- Configure the parameters of e-mail account which is to be used for sending e-mail messages (Mail server (SMTP), Server port, User name, Password, Encryption, Sender address).

- Enter the subject for e-mail messages.

- Configure the Ethernet communication module:

enable the ETHM option,

configure the module network settings.

###### E-mail messaging via Ethernet module

- Enable the E-mail messaging (LAN) option.

- Configure the Ethernet communication module:

enable the ETHM option,

configure the module network settings.

###### E-mail messaging via GSM module

- Enable the E-mail messaging (GSM) option.

- Configure the built-in GSM module:

enable the SIM1 option and/or SIM2 option,

enter GPRS parameters required by the GSM network operator.

##### Starting the SMS messaging

- Enable the SMS messaging option.

- Enter the phone numbers that are to be notified, and enable the ON option for those telephones.

- Define the events of which the control panel is to notify.

- Configure the built-in GSM module:

enable the SIM1 option and/or SIM2 option,

enter the SMS center number.

##### Remote firmware update

###### Remote firmware update

LAN - if this option is enabled, communication with the UpServ update server will take place via the Ethernet module.

GPRS - if this option is enabled, communication with the UpServ update server will take place via the GSM module.

Note: If the LAN and GPRS options are enabled at the same time, communication via the Ethernet module will have priority. Communication via the GSM module will take place only if an attempt to establish communication via the Ethernet module fails.

Update server - address of the UpServ update server. You can enter the IP address or domain name.

Port - number of the TCP port used for communication with the UpServ update server. You can enter values from 1 to 65535.

Server address in SMS - if this option is enabled, you can enter server address and port number in the SMS message initiating the firmware download from the update server. If the message contains no address or port number, the control panel will use the preprogrammed settings.

###### Firmware download

SMS initiating download - the control command which can be sent in the SMS message to initiate firmware download from the UpServ update server. Up to 8 alphanumeric characters can be entered (you can use spaces, but at least one character must be different from space).

Note: The command content must be different from that of the other control commands preprogrammed in the control panel.

SMS messages

The control panel sends out an SMS notification on how the new firmware download has proceeded. The notification is sent to the telephone from which the SMS message initiating the firmware download was received. The message content may consist of up to 32 characters.

Firmware downloaded - the message to be sent by the control panel after completion of the firmware download from the UpServ update server.

No newer firmware - the message to be sent by the control panel, if it turns out, after connecting to the update server, that there is no new firmware.

Download failed - the message to be sent by the control panel, if attempts to download the new firmware fail.

###### Firmware update

SMS initiating update - the control command which can be sent in the SMS message to initiate update of the control panel firmware. You can enter up to 8 alphanumeric characters (spaces can be used, but at least one character must be different from space).

Note: The command content must be different from that of the other control commands preprogrammed in the control panel.

SMS messages

The control panel sends out an SMS notification on how the firmware update has proceeded. The notification is sent to the telephone from which the SMS message initiating the firmware download was received. The message content may consist of up to 32 characters.

Update successful - the message to be sent by the control panel after completion of the firmware update.

No firmw. downloaded - the message to be sent by the control panel, if the firmware update is not possible, because the new firmware version has not been downloaded.

### Expansion modules

Most of devices to be connected to the communication bus must have a suitable address set (see: Addresses).

Devices connected to the communication bus will only be recognized and properly handled after they are identified by the panel (see: Identification). Only then will the information about them be displayed in the Hardware tab. Click on any of the devices to proceed to its programming.

-----------------------------------------------------------

Store keyfob events - if this option is enabled, using the keyfob is written into the events log.

Block after 3 unknown codes/cards - if this option is enabled, after entering an invalid code / reading in an invalid card three times, the keypad / proximity card arm/disarm device will be blocked for 90 seconds. After this period of time has expired, each subsequent entry of an invalid code / read-in of an invalid card will block the keypad / proximity card arm/disarm device at once. The counter of invalid codes / cards will be reset after a correct code is used.

###### Buttons

Identification - click to start the function of identification of devices connected to the bus (see: Identification).

Add/Remove - click to add or remove device. This allows you to configure the devices before they are connected.

VERSA-LCD

VERSA-LCDR

VERSA-LED

VERSA-LCDM-WRL

INT-TSG

INT-TSH

INT-RX

VERSA-MCU

ACU-100

Zone expander

Output expander

INT-IT

#### Addresses

Most of devices that are to be connected to the communication bus must have a suitable address set in accordance with the table below.

| Address | Device type |
| --- | --- |
| 0 | INT-TSG / INT-TSH / VERSA-LCD / VERSA-LCDM / VERSA-LCDR / VERSA-LCDM-WRL / VERSA-LED |
| 1 |  |
| 2 |  |
| 3 |  |
| 4 |  |
| 5 |  |
| 7 | INT-RX-S / INT-RX |
| 8 | ACU-100 / ACU-250 |
| 12 | INT-E / CA-64 E / CA-64 EPS |
| 13 |  |
| 14 |  |
| 15 | INT-O / INT-ORS / CA-64 O / CA-64 OPS |
| 16 | INT-CR / INT-IT-2 / INT-IT |
| 17 |  |
| 18 |  |
| 19 |  |
| 20 |  |
| 21 |  |

You do not have to set any address in the following devices:

VERSA-MCU - after identification, the controller will occupy two addresses: 7 (as INT-RX) and 8 (as VERSA-MCU),

ACU-120 / ACU-270 - after identification, the controller will get the address 8.

Note: In the ACU-120 / ACU-270 controller, the switch 8 must be set to the ON position.

#### Identification

Devices connected to the communication bus will not be properly supported, unless they have been identified by the control panel. Identification of the devices is required after the first start-up of the control panel and then each time after a new device is added or the address was changed in a device supported by the control panel.

###### Starting the identification function

- Click on the  button in the main menu. The VERSA - Structure window will open.

- Click on the Hardware tab.

- Click on the Expanders branch.

- Click on the Identification button to run the identification function.

- After the identification is finished, a window will appear with a prompt whether to read the data. Click OK.

#### VERSA-LCD

The following devices are identified as the VERSA-LCD:

VERSA-LCD - hardwired LCD keypad with mechanical keys,

VERSA-LCDM - hardwired LCD keypad with mechanical keys.

-----------------------------------------------------------

Name - individual name of the keypad (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of keypad tamper (opening the enclosure or disconnecting the keypad from the bus).

CHIME signal of zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - zone violation will not trigger the CHIME signal,

orange - zone violation will trigger the CHIME signal.

Double-click on the field to change its color.

If the zone is armed, violation will not trigger the CHIME signal.

Date/Time format - the way how date and time will be presented on the display.

LCD backlight - the way how the display backlight will work.

Keys backlight - the way how the keys backlight will work.

Auto-backlight - the way to turn on the automatic backlight of keys and the display.

Sounder volume - control of the volume level of sounds generated in the keypad.

###### Options

Sign. entry delay - if this option is enabled, the keypad will audibly signal the entry delay countdown.

Sign. exit delay - if this option is enabled, the keypad will audibly signal the exit delay countdown.

Sign. alarms - if this option is enabled, the keypad will signal the alarms audibly. The alarm is signaled during the Keypad’s alarm time (see: Times).

Quick arming - Partition 1 - if this option is enabled, partition 1 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 2 - if this option is enabled, partition 2 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Keys sound - with this option enabled, pressing the keypad keys is confirmed by beeps.

Sign. trbl in part. arm - if this option is enabled, the  LED goes off after both partitions are fully armed (if the option is disabled, the LED goes off after just one of the partitions is armed in any mode).

Show code entering - if this option is enabled, entering the code is presented on the keypad display by asterisks.

Chime on/off - if this option is enabled, the chime signal can be turned on/off by means of the  key (the key is to be pressed for about 3 seconds).

Quick control - if this option is enabled, the users can control the outputs by using the number keys. The 15. Controlled outputs must be assigned to the keys (see: Quick control).

Sign. new trouble - if this option is enabled, the keypad will audibly signal occurrence of any new trouble (additionally, the Trouble memory until review option must be enabled in the control panel - see: Options). The signaling will be turned off after reviewing the trouble with the System state user function. The new troubles will not be signaled, if the Grade 2 option is enabled in the control panel.

Auto-Arm delay countdown - if this option is enabled, the auto-arm delay countdown is signaled acoustically.

Arm mode review - if this option is enabled, holding down the  key for about 3 seconds will display information on the partition status. The users cannot check the partition status using the  key, if the Grade 2 option is enabled.

###### Alarm messages

Partitions - if this option is enabled, messages on partition alarms will be displayed (they contain the name of partition).

Zones - if this option is enabled, messages on alarms from zones will be displayed (they contain the name of zone). The zone alarm messages have the priority.

Note: The messages will not be displayed, if the Grade 2 global option is enabled.

###### Alarms

PANIC alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the panic alarm.

silent - if this option is enabled, the panic alarm triggered from the keypad will be a silent one (without loud signal). The option is available, if the PANIC alarm option is enabled.

FIRE alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the fire alarm.

AUX. alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the auxiliary (medical) alarm.

Alarm 3 incorrect codes - if this option is enabled, entering incorrect code three times will trigger the alarm.

Volume

##### Volume [VERSA-LCDM]

Volume - volume level of the beeps generated during keypad operation (key pressing, confirmation of performed operation, etc.).

Chime - volume level of the beeps generated after zone violation (CHIME).

Entry delay - volume level of the entry delay beeps.

Exit delay - volume level of the exit delay beeps.

Fire alarm - volume level of the fire alarm beeps.

Burglary alarm - volume level when signaling burglar, panic and auxiliary (medical) alarms.

Warning alarm - volume level when signaling warning alarms.

Trouble signaling - volume level when signaling troubles.

#### VERSA-LCDR

VERSA-LCDR - hardwired LCD keypad with mechanical keys and built-in proximity card reader.

-----------------------------------------------------------

Name - individual name of the keypad (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of keypad tamper (opening the enclosure or disconnecting the keypad from the bus).

CHIME signal of zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - zone violation will not trigger the CHIME signal,

orange - zone violation will trigger the CHIME signal.

Double-click on the field to change its color.

If the zone is armed, violation will not trigger the CHIME signal.

Date/Time format - the way how date and time will be presented on the display.

LCD backlight - the way how the display backlight will work.

Keys backlight - the way how the keys backlight will work.

Auto-backlight - the way to turn on the automatic backlight of keys and the display.

Sounder volume - control of the volume level of sounds generated in the keypad.

###### Options

Sign. entry delay - if this option is enabled, the keypad will audibly signal the entry delay countdown.

Sign. exit delay - if this option is enabled, the keypad will audibly signal the exit delay countdown.

Sign. alarms - if this option is enabled, the keypad will signal the alarms audibly. The alarm is signaled during the Keypad’s alarm time (see: Times).

Quick arming - Partition 1 - if this option is enabled, partition 1 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 2 - if this option is enabled, partition 2 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Keys sound - with this option enabled, pressing the keypad keys is confirmed by beeps.

Sign. trbl in part. arm - if this option is enabled, the  LED goes off after both partitions are fully armed (if the option is disabled, the LED goes off after just one of the partitions is armed in any mode).

Show code entering - if this option is enabled, entering the code is presented on the keypad display by asterisks.

Chime on/off - if this option is enabled, the chime signal can be turned on/off by means of the  key (the key is to be pressed for about 3 seconds).

Quick control - if this option is enabled, the users can control the outputs by using the number keys. The 15. Controlled outputs must be assigned to the keys (see: Quick control).

Sign. new trouble - if this option is enabled, the keypad will audibly signal occurrence of any new trouble (additionally, the Trouble memory until review option must be enabled in the control panel - see: Options). The signaling will be turned off after reviewing the trouble with the System state user function. The new troubles will not be signaled, if the Grade 2 option is enabled in the control panel.

Auto-Arm delay countdown - if this option is enabled, the auto-arm delay countdown is signaled acoustically.

Arm mode review - if this option is enabled, holding down the  key for about 3 seconds will display information on the partition status. The users cannot check the partition status using the  key, if the Grade 2 option is enabled.

###### Alarm messages

Partitions - if this option is enabled, messages on partition alarms will be displayed (they contain the name of partition).

Zones - if this option is enabled, messages on alarms from zones will be displayed (they contain the name of zone). The zone alarm messages have the priority.

Note: The messages will not be displayed, if the Grade 2 global option is enabled.

###### Alarms

PANIC alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the panic alarm.

silent - if this option is enabled, the panic alarm triggered from the keypad will be a silent one (without loud signal). The option is available, if the PANIC alarm option is enabled.

FIRE alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the fire alarm.

AUX. alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the auxiliary (medical) alarm.

Alarm 3 incorrect codes - if this option is enabled, entering incorrect code three times will trigger the alarm.

Volume

Proximity cards

##### Volume

Volume - volume level of the beeps generated during keypad operation (key pressing, confirmation of performed operation, etc.).

Chime - volume level of the beeps generated after zone violation (CHIME).

Entry delay - volume level of the entry delay beeps.

Exit delay - volume level of the exit delay beeps.

Fire alarm - volume level of the fire alarm beeps.

Burglary alarm - volume level when signaling burglar, panic and auxiliary (medical) alarms.

Warning alarm - volume level when signaling warning alarms.

Trouble signaling - volume level when signaling troubles.

##### Proximity cards

###### Arming

Card hold-down - if you select this option, the user will have to bring the card close to the keys and hold it still for about 3 seconds to arm the system.

Card read - if you select this option, the user will only have to bring the card close to the keys to arm the system.

Note: When configuring the keypad by using functions available in the service mode, use the Prox.card - arms option to define how to arm the system using the proximity card (option enabled = Card read; option disabled = Card hold-down).

###### Card hold-down control outputs

If you have selected the Card read option, you can permit the users to toggle the 15. Controlled type outputs (the output status will change after the card is brought close to the keys and held still for about 3 seconds). Select the outputs the users will be allowed to control.

#### VERSA-LED

VERSA-LED - hardwired LED keypad with mechanical keys.

-----------------------------------------------

Name - individual name of the keypad (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of keypad tamper (opening the enclosure or disconnecting the keypad from the bus).

CHIME signal of zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - zone violation will not trigger the CHIME signal,

orange - zone violation will trigger the CHIME signal.

Double-click on the field to change its color.

If the zone is armed, violation will not trigger the CHIME signal.

Keys backlight - the way how the keys backlight will work.

Auto-backlight - the way to turn on the automatic backlight of keys.

Sounder volume - control of the volume level of sounds generated in the keypad.

###### Options

Sign. entry delay - if this option is enabled, the keypad will audibly signal the entry delay countdown.

Sign. exit delay - if this option is enabled, the keypad will audibly signal the exit delay countdown.

Sign. alarms - if this option is enabled, the keypad will signal the alarms audibly. The alarm is signaled during the Keypad’s alarm time (see: Times).

Quick arming - Partition 1 - if this option is enabled, partition 1 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 2 - if this option is enabled, partition 2 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Keys sound - with this option enabled, pressing the keypad keys is confirmed by beeps.

Sign. trbl in part. arm - if this option is enabled, the  LED goes off after both partitions are fully armed (if the option is disabled, the LED goes off after just one of the partitions is armed in any mode).

Show code entering - if this option is enabled, entering the code is presented by means of LEDs in the lower line of LEDs.

Chime on/off - if this option is enabled, the chime signal can be turned on/off by means of the  key (the key is to be pressed for about 3 seconds).

Quick control - if this option is enabled, the users can control the outputs by using the number keys. The 15. Controlled outputs must be assigned to the keys (see: Quick control).

Sign. new trouble - if this option is enabled, the keypad will audibly signal occurrence of any new trouble (additionally, the Trouble memory until review option must be enabled in the control panel - see: Options). The signaling will be turned off after reviewing the trouble with the System state user function. The new troubles will not be signaled, if the Grade 2 option is enabled in the control panel.

Arm mode review - if this option is enabled, holding down the  key for about 3 seconds will display information on the partition status. The users cannot check the partition status using the  key, if the Grade 2 option is enabled.

###### Alarms

PANIC alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the panic alarm.

silent - if this option is enabled, the panic alarm triggered from the keypad will be a silent one (without loud signal). The option is available, if the PANIC alarm option is enabled.

FIRE alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the fire alarm.

AUX. alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the auxiliary (medical) alarm.

Alarm 3 incorrect codes - if this option is enabled, entering incorrect code three times will trigger the alarm.

#### VERSA-LCDM-WRL

VERSA-LCDM-WRL - wireless LCD keypad with mechanical keys.

-----------------------------------------------

Name - individual name of the keypad (up to 16 characters).

Tamper signaled in part. - partition in which tamper alarm will be triggered if the keypad tamper switch is opened or the keypad is not present.

CHIME signal of zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - zone violation will not trigger the CHIME signal,

orange - zone violation will trigger the CHIME signal.

Double-click on the field to change its color.

If the zone is armed, violation will not trigger the CHIME signal. The wireless keypad signals the CHIME from zones not more frequently than once every 30 seconds. In the inactive mode, the CHIME from zones is only signaled if the Wake-up option is enabled.

Date/Time format - the way how date and time will be presented on the display.

LCD backlight - the way how the display backlight will work in the active mode:

not present - disabled.

permanent 50% - enabled: brightness 50%.

permanent 100% - enabled: brightness 100%.

auto 0-50% - enabled: brightness 50%.

auto 0-100% - enabled: brightness 100%.

auto 50%-100% - enabled: brightness 100%.

Keys backlight - the way how the keys backlight will work in the active mode:

not present - disabled.

auto - enabled.

permanent -  enabled.

###### Options

Sign. entry delay - if this option is enabled, the keypad will audibly signal the entry delay countdown. In the inactive mode, the entry delay is not signaled.

Sign. exit delay - if this option is enabled, the keypad will audibly signal the exit delay countdown. In the inactive mode, the exit delay is not signaled.

Sign. alarms - if this option is enabled, the keypad will signal the alarms audibly. The alarm is signaled during the Keypad’s alarm time (see: Times). In the inactive mode, the alarms are not signaled. The alarms are not signaled, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 1 - if this option is enabled, partition 1 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 2 - if this option is enabled, partition 2 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Keys sound - with this option enabled, pressing the keypad keys is confirmed by beeps.

Sign. trbl in part. arm - if this option is enabled, the  LED goes off after both partitions are fully armed (if the option is disabled, the LED goes off after just one of the partitions is armed in any mode).

Show code entering - if this option is enabled, entering the code is presented on the keypad display by asterisks.

Chime on/off - if this option is enabled, the chime signal can be enabled/disabled by means of the  key (the key is to be pressed for about 3 seconds).

Quick control - if this option is enabled, the users can control the outputs by using the number keys. The 15. Controlled outputs must be assigned to the keys (see: Quick control).

Sign. new trouble - if this option is enabled, the keypad will audibly signal occurrence of any new trouble (additionally, the Trouble memory until review option must be enabled in the control panel - see: Options). The signaling will be turned off after reviewing the trouble with the 7. System state user function. In the inactive mode, new troubles are not signaled. The new troubles will not be signaled, if the Grade 2 option is enabled in the control panel.

Auto-Arm delay countdown - if this option is enabled, the auto-arm delay countdown is signaled acoustically. In the inactive mode, the auto-arm delay countdown is not signaled.

Arm mode review - if this option is enabled, holding down the  key for about 3 seconds will display information on the partition status. The users cannot check the partition status using the  key, if the Grade 2 option is enabled in the control panel.

###### Alarm messages

Partitions - if this option is enabled, messages on partition alarms will be displayed (they contain the name of partition).

Zones - if this option is enabled, messages on alarms from zones will be displayed (they contain the name of zone). The zone alarm messages have the priority.

Note: The messages will not be displayed, if the Grade 2 global option is enabled.

###### Alarms

PANIC alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the panic alarm.

silent - if this option is enabled, the panic alarm triggered from the keypad will be a silent one (without loud signal). The option is available, if the PANIC alarm option is enabled.

FIRE alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the fire alarm.

AUX. alarm - if this option is enabled, pressing the  key for approx. 3 seconds will trigger the auxiliary (medical) alarm.

Alarm 3 incorrect codes - if this option is enabled, entering invalid code three times will trigger the alarm.

Note: The auto-backlight parameters do not affect the wireless keypad performance.

Volume

Proximity cards

##### Volume

Volume - volume level of the beeps generated during keypad operation (key pressing, confirmation of performed operation, etc.).

Chime - volume level of the beeps generated after zone violation (CHIME).

Entry delay - volume level of the entry delay beeps.

Exit delay - volume level of the exit delay beeps.

Fire alarm - volume level of the fire alarm beeps.

Burglary alarm - volume level when signaling burglar, panic and auxiliary (medical) alarms.

Warning alarm - volume level when signaling warning alarms.

Trouble signaling - volume level when signaling troubles.

##### Proximity cards

###### Arming

Card hold-down - if you select this option, the user will have to bring the card close to the keys and hold it still for about 3 seconds to arm the system.

Card read - if you select this option, the user will only have to bring the card close to the keys to arm the system.

Note: When configuring the keypad by using functions available in the service mode, use the Prox.card - arms option to define how to arm the system using the proximity card (option enabled = Card read; option disabled = Card hold-down).

###### Card hold-down control outputs

If you have selected the Card read option, you can permit the users to toggle the 15. Controlled type outputs (the output status will change after the card is brought close to the keys and held still for about 3 seconds). Select the outputs the users will be allowed to control.

#### INT-TSG

INT-TSG - hardwired touchscreen keypad.

-----------------------------------------------

Name - individual name of the keypad (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of keypad tamper (opening the enclosure or disconnecting the keypad from the bus).

CHIME signal of zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - zone violation will not trigger the CHIME signal,

orange - zone violation will trigger the CHIME signal.

Double-click on the field to change its color.

If the zone is armed, violation will not trigger the CHIME signal.

Date/Time format - the way how date and time will be presented on the display.

###### Options

Sign. entry delay - if this option is enabled, the keypad will audibly signal the entry delay countdown.

Sign. exit delay - if this option is enabled, the keypad will audibly signal the exit delay countdown.

Sign. alarms - if this option is enabled, the keypad will signal the alarms audibly. The alarm is signaled during the Keypad’s alarm time (see: Times).

Quick arming - Partition 1 - if this option is enabled, partition 1 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 2 - if this option is enabled, partition 2 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Keys sound - with this option enabled, pressing the keypad keys is confirmed by beeps.

Sign. trbl in part. arm - if this option is enabled, the  LED goes off after both partitions are fully armed (if the option is disabled, the LED goes off after just one of the partitions is armed in any mode).

Show code entering - if this option is enabled, entering the code is presented on the keypad display by asterisks.

Chime on/off - if this option is enabled, the chime signal can be turned on/off after tapping and holding for 3 seconds  on terminal.

Quick control - if this option is enabled, you can control the outputs without entering the code:

after tapping  on the main screen,

using the keys designated by numbers on terminal. When programming the control panel, assign the 15. Controlled outputs to the keys (see: Quick control).

Sign. new trouble - if this option is enabled, the keypad will audibly signal occurrence of any new trouble (additionally, the Trouble memory until review option must be enabled in the control panel - see: Options). The signaling will be turned off after reviewing the trouble with the 7. System state user function. The new troubles will not be signaled, if the Grade 2 option is enabled in the control panel.

Auto-Arm delay countdown - if this option is enabled, the auto-arm delay countdown is signaled acoustically.

Arm mode review - if this option is enabled, you can inspect the partition state without entering the code:

after tapping  on the “System status” screen,

after tapping and holding for 3 seconds  on the terminal.

###### Alarm messages

Partitions - if this option is enabled, messages on partition alarms will be displayed (they contain the name of partition).

Zones - if this option is enabled, messages on alarms from zones will be displayed (they contain the name of zone). The zone alarm messages have the priority.

Note: The messages will not be displayed, if the Grade 2 global option is enabled.

###### Alarms

PANIC alarm - if this option is enabled, you can trigger panic alarm from the keypad by tapping and holding for 3 seconds:

on the “Emergency” screen,

on the terminal.

silent - if this option is enabled, the panic alarm triggered from the keypad will be a silent one (without loud signal). Additionally, the silent panic alarm can be triggered by tapping and holding any part of the status screen for about 3 seconds. The option is available, if the PANIC alarm option is enabled.

FIRE alarm - if this option is enabled, you can trigger fire alarm from the keypad by tapping and holding for 3 seconds:

on the “Emergency” screen,

on the terminal.

AUX. alarm - if this option is enabled, you can trigger medical alarm from the keypad by tapping and holding for 3 seconds:

on the “Emergency” screen,

on the terminal.

Alarm 3 incorrect codes - if this option is enabled, entering incorrect code three times will trigger the alarm.

###### Auto-backlight

The keypad can be woken up after occurrence of a specified event in the system: starting the entry delay countdown in a selected partition, or violating a selected zone.

###### Wake-up

You can define how the keypad will respond to the wake-up (after a tap on the screen by the user or occurrence of a specified event in the system):

Status screen - status screen will be displayed.

Menu screen - main screen will be displayed.

Disarming - if at least one partition managed by the keypad is armed, the authorization screen will be displayed (after entering the code and tapping , and depending on the system state: the partition(s) will be disarmed / partition selection screen will be displayed / “Alarm clearing / Disarming” screen will be displayed). If none of the partitions is armed, the main screen will be displayed.

Photo frame - if this option is enabled, the following will be displayed after 10 minutes of keypad inactivity:

slide show - if there are at least two pictures on the memory card and the value of Change picture every parameter is different from 0,

clock - if there are one or no pictures on the memory card or the value of Change picture every parameter is 0.

If this option is disabled, the screen will go blank after 10 minutes of keypad inactivity.

Status screen

##### Status screen

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the status screen are stored in the keypad and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

The status screen is displayed automatically after the keypad is idle for 60 seconds. This rule does not apply if the terminal is running. In such a case, the status screen may be displayed later or even will not be displayed at all (e.g. when the service menu is open). The following information can be displayed on the status screen:

any text defined by the installer,

partition status by means of symbols (select individual partitions whose status will be displayed),

zone status by means of symbols (select individual zones whose status will be displayed),

output status by means of symbols (select individual outputs whose status will be displayed),

date and time (particular elements, such as day, month, year, hour, minutes and seconds are to be configured individually),

keypad name,

zone status by means of messages (select individual zones whose status will be displayed, and define the content and color of messages for normal state and for violation, because only these two states are presented in the form of message),

output status by means of messages (select individual outputs whose status will be displayed, and define the content and color of messages for active and inactive output).

There are three font sizes available for use on the status screen. You can also define color of the font to be used. Using the “drag and drop” method, you can easily select the place where the given information will be presented on the display.

Change picture every - the parameter defines how quickly the pictures will change during the slide show. The slide show can be displayed as the status screen background or the screensaver. The photos to be displayed should be stored on a microSD memory. Their size should not exceed 480 x 272 pixels. Only images in BMP format are supported. If the programmed time is 0, the pictures will not change (the first picture stored on the microSD card will be displayed all the time).

###### Buttons

Wallpaper - click to select another status screen wallpaper.

Save to SD card - click to save the new wallpaper on the microSD card.

Export to file - click to export the status screen settings to a file.

Import from file - click to import the status screen settings from a file.

Read - click to read the data related to status screen (these data are not read after clicking on the  button in the main menu).

Write - click to write the data related to status screen (these data are not written after clicking on the  button in the main menu).

Quit - click to terminate data reading/writing.

Reset - click to restore the factory settings of the status screen in the keypad (after the factory settings have been restored, click on Read button to read the data related to status screen).

#### INT-TSH

INT-TSH - hardwired touchscreen keypad.

-----------------------------------------------

Name - individual name of the keypad (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of keypad tamper (opening the enclosure or disconnecting the keypad from the bus).

CHIME signal of zones - the numbers of fields in the table correspond to those of zones. The field color has the following meanings:

white - zone violation will not trigger the CHIME signal,

orange - zone violation will trigger the CHIME signal.

Double-click on the field to change its color.

If the zone is armed, violation will not trigger the CHIME signal.

Date/Time format - the way how date and time will be presented on the display.

###### Options

Sign. entry delay - if this option is enabled, the keypad will audibly signal the entry delay countdown.

Sign. exit delay - if this option is enabled, the keypad will audibly signal the exit delay countdown.

Sign. alarms - if this option is enabled, the keypad will signal the alarms audibly. The alarm is signaled during the Keypad’s alarm time (see: Times).

Quick arming - Partition 1 - if this option is enabled, partition 1 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Quick arming - Partition 2 - if this option is enabled, partition 2 can be armed without entering the code. The quick arming is not possible, if the Grade 2 option is enabled in the control panel.

Keys sound - with this option enabled, pressing the keypad keys is confirmed by beeps.

Sign. trbl in part. arm - if this option is enabled, the trouble information on status bar and on terminal will be hidden after both partitions are fully armed (if the option is disabled, the trouble information will be hidden after just one of the partitions is armed in any mode).

Show code entering - if this option is enabled, entering the code is presented on the keypad display by asterisks.

Chime on/off - if this option is enabled, the chime signal can be turned on/off after tapping and holding for 3 seconds  on terminal.

Quick control - if this option is enabled, you can control the outputs without entering the code:

after tapping  on the main screen,

using the keys designated by numbers on terminal. When programming the control panel, assign the 15. Controlled outputs to the keys (see: Quick control).

Sign. new trouble - if this option is enabled, the keypad will audibly signal occurrence of any new trouble (additionally, the Trouble memory until review option must be enabled in the control panel - see: Options). The signaling will be turned off after reviewing the trouble with the 7. System state user function. The new troubles will not be signaled, if the Grade 2 option is enabled in the control panel.

Auto-Arm delay countdown - if this option is enabled, the auto-arm delay countdown is signaled acoustically.

Arm mode review - if this option is enabled, you can inspect the partition state without entering the code:

after tapping  on the “System status” screen,

after tapping and holding for 3 seconds  on the terminal.

###### Alarm messages

Partitions - if this option is enabled, messages on partition alarms will be displayed (they contain the name of partition).

Zones - if this option is enabled, messages on alarms from zones will be displayed (they contain the name of zone). The zone alarm messages have the priority.

Note: The messages will not be displayed, if the Grade 2 global option is enabled.

###### Alarms

PANIC alarm - if this option is enabled, you can trigger panic alarm from the keypad by tapping and holding for 3 seconds:

on the “Emergency” screen,

on the terminal.

silent - if this option is enabled, the panic alarm triggered from the keypad will be a silent one (without loud signal). Additionally, the silent panic alarm can be triggered by tapping and holding any part of the status screen for about 3 seconds. The option is available, if the PANIC alarm option is enabled.

FIRE alarm - if this option is enabled, you can trigger fire alarm from the keypad by tapping and holding for 3 seconds:

on the “Emergency” screen,

on the terminal.

AUX. alarm - if this option is enabled, you can trigger medical alarm from the keypad by tapping and holding for 3 seconds:

on the “Emergency” screen,

on the terminal.

Alarm 3 incorrect codes - if this option is enabled, entering incorrect code three times will trigger the alarm.

###### Auto-backlight

The keypad can be woken up after occurrence of a specified event in the system: starting the entry delay countdown in a selected partition, or violating a selected zone.

###### Wake-up

You can define how the keypad will respond to the wake-up (after a tap on the screen by the user or occurrence of a specified event in the system):

Status screen - status screen will be displayed.

Menu screen - main screen will be displayed.

Disarming - if at least one partition managed by the keypad is armed, the authorization screen will be displayed (after entering the code and tapping , and depending on the system state: the partition(s) will be disarmed / partition selection screen will be displayed / “Alarm clearing / Disarming” screen will be displayed). If none of the partitions is armed, the main screen will be displayed.

Photo frame - if this option is enabled, the screen will not go blank after the keypad is idle for 10 minutes. If this option is disabled, the screen will go blank after the keypad is idle for 10 minutes. See also the Show clock option, related to the status screen.

Status screen

##### Status screen

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the status screen are stored in the keypad and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

The status screen is displayed automatically after the keypad is idle for 60 seconds. This rule does not apply if the terminal is running. In such a case, the status screen may be displayed later or even will not be displayed at all (e.g. when the service menu is open). The status bar at the top of the screen indicates the system status by means of icons. Additionally, the following information can be presented on the status screen:

any text defined by the installer,

partition status by means of symbols (select individual partitions whose status will be displayed),

zone status by means of symbols (select individual zones whose status will be displayed),

output status by means of symbols (select individual outputs whose status will be displayed),

date and time (particular elements, such as day, month, year, hour, minutes and seconds are to be configured individually),

keypad name,

zone status by means of messages (select individual zones whose status will be displayed, and define the content and color of messages for normal state and for violation, because only these two states are presented in the form of message),

output status by means of messages (select individual outputs whose status will be displayed, and define the content and color of messages for active and inactive output).

There are three font sizes available for use on the status screen. You can also define color of the font to be used. Using the “drag and drop” method, you can easily select the place where the given information will be presented on the display.

Change picture every - the parameter defines how quickly the pictures will change during the slide show. The slide show can be displayed as the status screen background or the screensaver. The photos to be displayed should be stored on a microSD memory. Their size should not exceed 800 x 480 pixels. Only images in BMP format are supported. If the programmed time is 0, the pictures will not change (the first picture stored on the microSD card will be displayed all the time).

Show clock - if this option is enabled, the clock and status bar will be displayed after the keypad is idle for 10 minutes.

Color - you can select the color of the clock.

###### Buttons

Wallpaper - click to select another status screen wallpaper.

Save to SD card - click to save the new wallpaper on the microSD card.

Export to file - click to export the status screen settings to a file.

Import from file - click to import the status screen settings from a file.

Read - click to read the data related to status screen (these data are not read after clicking on the  button in the main menu).

Write - click to write the data related to status screen (these data are not written after clicking on the  button in the main menu).

Quit - click to terminate data reading/writing.

Reset - click to restore the factory settings of the status screen in the keypad (after the factory settings have been restored, click on Read button to read the data related to status screen).

#### INT-RX

The following devices are identified as INT-RX:

INT-RX - 433 MHz keyfobs receiver expansion module,

INT-RX-S - 433 MHz keyfobs receiver expansion module,

VERSA-MCU - 433 MHz wireless system controller (the controller is identified as two devices).

These devices allow to control the alarm system by using the 433 MHz keyfobs.

-----------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - the partition in which tamper alarm will be triggered in the event of tamper or disconnection of the device from the system.

###### Keyfob information table

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the keyfobs are stored in the expander and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

After expansion module containing the keyfob data is connected to the control panel, keyfobs will be automatically assigned to the existing users.

User - the field shows the user's number and name.

S/N - the field shows the serial number of 433 MHz keyfob assigned to the user.

Keyfob buttons - the field shows the number of function to be run by pressing a given button or a combination of buttons (two buttons at the same time: 1 and 2 or 1 and 3) on the keyfob. Click on the field and press the right mouse button to display a drop-down menu where you can select functions.

###### Buttons

Read - click to read the data related to keyfobs (these data are not read after clicking on the  button in the main menu).

Write - click to write the data related to keyfobs (these data are not written after clicking on the  button in the main menu).

New - click to add a keyfob (see: Adding 433 MHz keyfob).

Delete - click to remove a keyfob (see: Removing 433 MHz keyfob).

##### Adding 433 MHz keyfob

You can add the keyfob by entering its serial number manually or reading the serial number during transmission which is sent after the button is pressed.

Note: After adding the keyfob, its settings will be configured automatically based on the user schedule.

###### Entering the serial number manually

- Click on the Read button to read the data related to keyfobs from the expander.

- Click on the field in the S/N column next to the name of the user to whom you want to assign a keyfob.

- Enter the keyfob serial number and confirm by pressing ENTER.

- Click on the Write button to write the new keyfob data to the expander.

###### Reading the serial number during transmission

- Click on the Read button to read the data related to keyfobs from the expander.

- Click on the field in the S/N column next to the name of the user to whom you want to assign a keyfob.

- Click on the New button. The New window will open.

- According to the command which will appear in the window, press the keyfob button.

- When the keyfob serial number is displayed in the window, click on the OK button. The New window will close. The serial number of the new keyfob will be shown in the S/N column.

- Click on the Write button to write the new keyfob data to the expander.

###### Assigning new function to the keyfob button (combination of buttons)

Right click on the field corresponding to the keyfob button. The drop-down menu will be displayed, in which you can select a new function.

##### Removing 433 MHz keyfob

- Click on the Read button to read the data related to keyfobs from the expander.

- Click on the field in S/N column next to the name of user whose keyfob is to be removed.

- Click on the Delete button.

- In the window which will be displayed, click on the Yes button to confirm that you want to remove the keyfob. The window will be closed, and the keyfob serial number displayed in the S/N column will be cleared.

- Click on the Write button to save the changes to the expander.

#### VERSA-MCU

VERSA-MCU - 433 MHz wireless system controller (the controller is identified as two devices, the other device being INT-RX).

The controller enables 433 MHz wireless detectors to be used in the alarm system.

---------------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of device tamper (opening the enclosure or disconnecting from the bus).

###### The table with list of wireless detectors

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the wireless detectors are stored in the controller and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

No. - number of the zone to which the wireless detector is assigned.

Name - name of the zone to which the wireless detector is assigned.

Type - type of the zone to which the wireless detector is assigned.

Device type - type of the wireless detector.

Serial number - serial number of the wireless detector.

Presence contr. - if this option is enabled, the detector is checked for presence. If no transmission is received from the detector within an hour, trouble will be reported (loss of communication with the detector).

###### Buttons

Read - click to read the data related to wireless detectors (these data are not read after clicking on the  button in the main menu).

Write - click to write the data related to wireless detectors (these data are not written after clicking on the  button in the main menu).

- click to open VERSA - Wireless devices window.

New device - click to add wireless detector (see: Adding 433 MHz wireless detector).

Delete - click to remove wireless detector (see: Removing 433 MHz wireless detector).

##### Adding 433 MHz wireless detector

Note: The control panel can support up to 30 wireless detectors.

- Click on the Read button to read the data related to wireless detectors from the controller.

- Click on the zone to which a new wireless detector is to be assigned (you can also select the zone later in the New wireless dev. window).

- Click on the New device button. The New wireless dev. window will open.

- Enter the 7-digit serial number of the added detector. The serial number can be found on the electronics board or on the enclosure.

- Open the detector tamper contact.

- The message will confirm that a new detector has been added (unless you have entered an invalid serial number, of which you will be informed by a message). The new zone name will be displayed. You can change it.

- Click on the OK button (you can click on the Quit button to cancel adding a new detector or on the Next button to proceed to adding a next wireless detector). The New wireless dev. window will close. The new detector will appear in the table.

- Click on the Write button to write the new wireless detector data to the controller.

##### Removing 433 MHz wireless detector

- Click on the Read button to read the data related to wireless detectors from the controller.

- Click on the zone to which the detector you want to delete is assigned.

- Click on the Delete button. The Confirm window will open.

- Click on the Yes button. The Confirm window will close.

- Click on the Write button to save the changes to the controller.

#### ACU-100

The following controllers of ABAX wireless system are identified as ACU-100:

ACU-120

ACU-270

ACU-100

ACU-250

The controller makes it possible to use ABAX wireless system devices in the alarm system and control the alarm system by using the ABAX keyfobs.

-----------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - partition where alarm will be triggered in the event of device tamper (opening the enclosure or disconnecting from the bus).

Response period - communication with wireless devices takes place in specified intervals. The controller is then gathering information on the status of wireless devices and, if necessary, sending commands to the devices, e.g. switching the detectors to their active/passive state, switching on/off the test mode and/or changing configuration of the devices. The response period can be 12, 24 or 36 seconds. The less often communication between the controller and the wireless devices takes place, the more wireless devices can work within each other's operating range (12 seconds - up to 150, 24 seconds - up to 300, 36 seconds - up to 450). Beyond the response period, information about tampers of devices and violations of detectors operating in active mode are sent to the controller. The response period has an effect on the level of energy consumption by the wireless devices. The less often communication between the controller and the wireless devices takes place, the lower energy consumption and the longer battery life are.

Note: In the case of the AMD-103 detector and ASP-100 siren, no communication takes place during polling.

Higher sensitivity for jamming detection - if this option is enabled, the sensitivity of detection of radio communication jamming is boosted.

User can replace VERSA-LCDM-WRL battery - if this option is enabled, the users can replace battery in the VERSA-LCDM-WRL wireless keypads (for 3 minutes after the code is entered and confirmed with the  key, the status of tamper switch will not be monitored on the keypad that was used to enter the code).

###### The table with list of wireless devices

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the wireless devices are stored in the controller and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

No. - number of the zone/output to which the wireless device is assigned.

Name - name of the zone/output to which the wireless device is assigned.

Type - type/function of the zone/output to which the wireless device is assigned.

Device type - type of the wireless device.

Serial number - serial number of the wireless device.

Always active - the option is available for most of the wireless detectors. It can permanently activate the detector.

Note: The AMD-103 detector and the wireless detectors assigned to 24-h zones are always in the active mode, therefore the Always active option does not have to be enabled for them.

Configuration - see: Configuring the ABAX wireless devices.

Filter - the number of consecutive response periods, during which communication with the device failed to be established, before no communication with the device is reported. Values from the 0 to 50 range can be entered. Entering the digit 0 will disable control of the device presence in the system.

Note: In the case of the AMD-103 magnetic contact and ASP-100 siren, the presence check is performed in a different way than for the other ABAX system devices. If the value programmed for the Filter parameter differs from 0, the lack of presence will be reported if no transmission from the AMD-103 magnetic contact / ASP-100 siren is received within one hour.

-----------------------------------------------

###### Keyfobs

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the ABAX keyfobs are stored in the controller and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

After controller containing the keyfob data is connected to the control panel, keyfobs will be automatically assigned to the existing users.

User - the field shows the user's number and name.

S/N - the field shows the serial number of APT-100 keyfob assigned to the user.

Keyfob buttons - the field shows the number of function to be run by pressing a given button or a combination of buttons on the keyfob. Click on the field and press the right mouse button to display a drop-down menu where you can select functions.

LED - the field shows the number corresponding to that of the information function assigned to the given LED. Click on the field and press the right mouse button to display a drop-down menu where you can select functions.

-----------------------------------------------

###### LCD-WRL

The ACU-120 and ACU-270 controllers make it possible to use the VERSA-LCDM-WRL wireless keypads in the alarm system.

Before making any changes, click on the Read button, and after making the changes - on the Write button (the data relating to the wireless keypads are stored in the controller and are not read after clicking on the  button or saved after clicking on the  button in the DLOADX program main menu).

No. - keypad address.

Name - keypad name.

Type - keypad type.

Serial number - serial number of the wireless keypad.

Presence contr. - if this option is enabled, the keypad presence is being monitored. If there is no transmission from the keypad for 1 hour, missing keypad will be reported.

Wake-up - if this option is enabled, the CHIME from zones will also be signaled in the inactive mode, while an alarm or start of entry delay countdown will start the active mode.

Note: If the Wake-up option is enabled, the keypad will be awaiting for transmissions with information on events. As a result, the energy consumption will be growing and the battery life will be considerably reduced.

Card reader - if this option is enabled, the card reader is supported.

###### Buttons

Read - click to read the data related to wireless devices / keyfobs / wireless keypads (these data are not read after clicking on the  button in the main menu).

Write - click to write the data related to wireless devices / keyfobs / wireless keypads (these data are not written after clicking on the  button in the main menu).

Test mode - click to start the test mode in the ABAX system. In the test mode:

LED indicators are enabled in the wireless devices (the LEDs are disabled during normal operation) - information provided by means of the LEDs depends on the device,

signaling is blocked in the ASP-105 and ASP-205 sirens.

The test mode is started/ended during polling, which results in a delay, its duration depending on the programmed response period. The test mode will be turned off automatically after 30 minutes of:

starting the test mode from the DLOADX program (the 30-minute period is running from the moment of exiting the controller settings),

exiting the service mode in the control panel.

Notes:

According to requirements of the EN50131 standard, the level of radio signals sent by wireless devices is reduced during the test mode operation.

For the AMD-103 detector, entering the test mode remotely is not possible.

- click to open VERSA - Wireless devices window.

Synchronize - click to start the procedure of synchronization, i.e. checking for presence of other ABAX wireless system controllers working within the controller operating range. The controller will synchronize the response period so that the radio transmissions of some controllers should not be mutually jammed. Synchronization is performed automatically upon starting the controller and after each operation of adding/removing devices supported by it.

New device - click to add wireless device (see: Adding ABAX wireless device) / keyfob (see: Adding ABAX keyfob) / wireless keypad (see: Adding the wireless keypad).

Delete - click to remove wireless device (see: Removing ABAX wireless device) / keyfob (see: Removing ABAX keyfob) / wireless keypad (see: Removing the wireless keypad).

##### Adding ABAX wireless device

Notes:

The control panel can support up to 30 wireless devices. The number of actually supported devices depends on how many positions the individual devices occupy. Each position means one wireless zone or one wireless zone and one wireless output.

If a device occupies two or more positions, its addition will respectively decrease the number of wireless devices that can still be registered (e.g. after adding a ACX-200 expander, which takes up 4 positions, the controller can still support 26 other wireless devices).

Even if a device occupies several zones in the system, only the first of them should be indicated during the device adding procedure. The next ones are assigned automatically (these are the zones following the selected one).

If the device occupies an output as well, its number will be the same as the number of zone selected during the device adding procedure.

The control panel does not support wireless outputs with numbers from 13 to 30.

- Click on the Read button to read the data related to wireless devices from the controller.

- Click on the zone to which a new wireless device is to be assigned (you can also select the zone later in the New wireless dev. window).

- Click on the New device button. The New wireless dev. window will open.

- Enter the 7-digit serial number of the added device. The serial number can be found on the electronics board or on the enclosure. Each ARF-100 radio signal level tester has serial number 0000500.

- Depending on the device type:

ACX-200 / ACX-201: power-up the expander,

ARF-100: turn on the device,

ASW-100 E / ASW-100 F: insert the controller into 230 V AC socket,

other devices: open the tamper contact.

- The message will confirm that a new device has been added (unless you have entered an invalid serial number, of which you will be informed by a message). The new zone name will be displayed. You can change it. The same name will also be given to the output, if the device is assigned to the output. For some devices, you can also select whether the device will take up one or two positions on the list of devices. Depending on the device, if one position is selected:

AMD-102 - only additional inputs (roller shutter and NC) will be supported;

AOD-200 - only the motion detector will be supported;

AVD-100 - only the vibration detector will be supported.

- Click on the OK button (you can click on the Quit button to cancel adding a new device or on the Next button to proceed to adding a next wireless device). The New wireless dev. window will close. The new device will appear in the table.

- Click on the Write button to write the new wireless device data to the controller.

##### Removing ABAX wireless device

- Click on the Read button to read the data related to wireless devices from the controller.

- Click on the zone to which the device you want to delete is assigned (if the device is assigned to several zones, you can click on any of them).

- Click on the Delete button. The Confirm window will open.

- Click on the Yes button. The Confirm window will close.

- Click on the Write button to save the changes to the controller.

##### Adding ABAX keyfob

You can add the keyfob by entering its serial number manually or reading the serial number during transmission which is sent after the button is pressed.

Note: After adding the keyfob, its settings will be configured automatically based on the user schedule.

###### Entering the serial number manually

- Click on the Read button to read the data related to keyfobs from the controller.

- Click on the field in the S/N column next to the name of the user to whom you want to assign a keyfob.

- Enter the keyfob serial number and confirm by pressing ENTER.

- Click on the Write button to write the new keyfob data to the controller.

###### Reading the serial number during transmission

- Click on the Read button to read the data related to keyfobs from the controller.

- Click on the field in the S/N column next to the name of the user to whom you want to assign a keyfob.

- Click on the New button. The New window will open.

- According to the command which will appear in the window, press the keyfob button.

- When the keyfob serial number is displayed in the window, click on the OK button. The New window will close. The serial number of the new keyfob will be shown in the S/N column.

- Click on the Write button to write the new keyfob data to the controller.

###### Assigning new function to the keyfob button (combination of buttons)

Right click on the field corresponding to the keyfob button. The drop-down menu will be displayed, in which you can select a new function.

###### Assigning new function to the LED

Right click on the field corresponding to the LED. The drop-down menu will be displayed, in which you can select a new function.

##### Removing ABAX keyfob

- Click on the Read button to read the data related to keyfobs from the controller.

- Click on the field in S/N column next to the name of user whose keyfob is to be removed.

- Click on the Delete button.

- In the window which will be displayed, click on the Yes button to confirm that you want to remove the keyfob. The window will be closed, and the keyfob serial number displayed in the S/N column will be cleared.

- Click on the Write button to save the changes to the controller.

##### Adding the wireless keypad

Note: You can add a wireless keypad, if the ACU-120 or ACU-270 controller is connected to the control panel. Before adding the keypad, make sure that the switch 8 in the controller is set to the ON position.

- Click on the Read button to read the data related to wireless keypads from the controller.

- Click on the New device button. The New wireless dev. window will open.

- In the Serial number field enter the 7-digit serial number of the added device. The serial number can be found on the electronics board.

- In the Address field, select which address is to be assigned to the keypad to be added.

- Press any button on the keypad or open its tamper switch.

- The message will confirm that a keypad has been added (unless you have entered an invalid serial number, of which you will be informed by a message). The name assigned to the keypad will be displayed. You can change it.

- Click OK (to cancel adding the keypad, click on the Quit button). The New wireless dev. window will close. The new keypad will appear in the table, LCD-WRL tab, as well as on the list of expanders.

- Click on the Write button to write the new wireless keypad data to the controller. The new keypad data will be automatically written to the control panel.

##### Removing the wireless keypad

- Click on the Read button to read the data related to wireless keypads from the controller

- Click on the wireless keypad you want to remove.

- Click on the Delete button. The Confirm window will open.

- Click on the Yes button. The Confirm window will close.

- Click on the Write button to save the changes to the controller and control panel.

##### Configuring the ABAX wireless devices

Some of the wireless devices provide additional parameters and options, which can be configured by radio (shown in square brackets is information on the zone for which additional parameters can be programmed, if the device takes up more than 1 zone).

AGD-100 (wireless glass-break detector) - enter a digit from the 1 to 3 range to set the sensitivity (1 - low, 2 - medium, 3 - high).

AMD-100 / AMD-101 (wireless magnetic contact) - enter the digit 0 (bottom reed switch) or 1 (side reed switch) to determine which of the two reed switches is to be active.

AMD-102 (wireless magnetic contact with input for roller shutter detector) - for the magnetic contact [first zone], enter the digit 0 (bottom reed switch) or 1 (side reed switch) to determine which of the two reed switches is to be active. For the roller shutter input [second zone], enter 2 digits:

1st digit - number of pulses after which alarm will be triggered by the roller shutter input: from 1 to 8.

2nd digit - time during which the specified number of pulses must occur for the roller shutter input to trigger alarm: 0 (30 seconds), 1 (120 seconds), 2 (240 seconds) or 3 (unlimited duration).

AOD-200 (wireless outdoor dual technology motion detector) - for the first position taken by the detector, enter 3 digits:

1st digit - sensitivity of PIR sensor: from 1 to 4 (1 - minimum; 4 - maximum).

2nd digit - sensitivity of microwave sensor: from 1 to 8 (1 - minimum; 8 - maximum).

3rd digit - sensitivity of dusk sensor: from 1 to 4 (1 - minimum; 4 - maximum).

APMD-150 (wireless dual motion detector) - enter 3 digits:

1st digit - sensitivity of PIR sensor: from 1 to 4 (1 - minimum; 4 - maximum).

2nd digit - sensitivity of microwave sensor: from 1 to 8 (1 - minimum; 8 - maximum).

3rd digit - the way of operation in the test mode: 0 (alarm triggered after motion is sensed by both detectors), 1 (alarm triggered after motion is sensed by infrared detector) or 2 (alarm triggered after motion is sensed by microwave detector).

APD-100 (wireless passive infrared detector) - enter 2 digits:

1st digit - sensitivity: 1 (low), 2 (medium) or 3 (high),

2nd digit - pet immunity option: 0 (disabled) or 1 (enabled).

ARD-100 (wireless reorientation detector) - enter a number from the 1 to 16 range to determine sensitivity (1 - minimum; 16 - maximum).

AVD-100 (wireless vibration detector and magnetic contact) - for the magnetic contact [first zone], enter the digit 0 (bottom reed switch) or 1 (side reed switch) to determine which of the two reed switches is to be active. For the vibration detector [second zone], enter 2 digits:

1st digit - sensitivity (registering a single vibration meeting the sensitivity criterion will cause alarm): from 1 to 8 (1 - minimum; 8 - maximum).

2nd digit - number of pulses which, if registered by vibration detector will cause alarm (the pulses need not meet the sensitivity criterion): from 0 to 7. For the value 0, pulses are not counted.

Note: Working parameters of the vibration detector are independently analyzed. The detector can trigger alarm after registering a single, strong vibration caused by a powerful impact, and also on registering several slight vibrations caused by a series of weak strikes.

ASP-100 (wireless outdoor siren) - enter 2 digits:

1st digit - type of acoustic signaling: from 1 to 4.

2nd digit - maximum duration of signaling: 1 (1 minute), 2 (3 minutes), 3 (6 minutes) or 4 (9 minutes).

ASP-105 (wirelessly triggered outdoor siren) - enter 2 digits:

1st digit - type of acoustic signaling: from 1 to 4.

2nd digit - maximum duration of acoustic signaling: 1 (1 minute), 2 (3 minutes), 3 (6 minutes) or 4 (9 minutes).

ASP-205 (wireless indoor siren) - for both positions taken on the list by the siren, enter 3 digits:

1st digit - maximum duration of signaling: 1 (1 minute), 2 (3 minutes), 3 (6 minutes) or 4 (9 minutes).

2nd digit - type of acoustic signaling: 0 (disabled), 1 (sound type 1), 2 (sound type 2) or 3 (sound type 3).

3rd digit - optical signaling: 0 (disabled) or 1 (enabled).

ASW-100 E / ASW-100 F (230 V AC wireless controller) - enter 0 (only remote control of the electric circuit); 1 (remote or manual control of the electric circuit) or 2 (remote or manual control of the electric circuit, but with option to manually block the remote control).

#### Zone expander

The control panel supports the following zone expanders: INT-E, CA-64 E and CA-64 EPS.

Zone expander enables the system expansion by 8 zones. Numeration of the expander zones depends on the expander address:

12 (0Ch) - 7-14

13 (0Dh) - 15-22

14 (0Eh) - 23-30

-----------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - the partition in which tamper alarm will be triggered in the event of device tamper.

EOL resistance value [applies to the expanders identified as CA-64 Ei and CA-64 EPSi] - the value of end-of-line resistors. You can enter values from the 500 Ohm to 15 kOhm range.

Notes:

The sum of values programmed for the resistors R1 and R2 may not be lower than 500 Ohm or higher than 15 kOhm.

You can program the value 0 for the resistor R2. In the 2EOL configuration you must use then two resistors, the resistance value of each being equal to half the value defined for the resistor R1.

In the EOL configuration, the resistance value is equal to the sum of values programmed for the resistors R1 and R2.

AC loss report delay [applies to the expanders identified as CA-64 EPS and CA-64 EPSi] - time during which the expander must be without AC power before the trouble is reported. A delay in reporting the trouble prevents sending information about short-time voltage decays, having no effect on normal operation of the system.

#### Output expander

The control panel supports the following output expanders: INT-O, INT-ORS, CA-64 O and CA-64 OPS. The output expander enables expansion of the system by 8 outputs. The expander outputs are numbered from 5 to 12 in the system.

-----------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - the partition in which tamper alarm will be triggered in the event of device tamper.

AC loss report delay [applies to the expanders identified as CA-64 OPS] - time during which the expander must be without AC power before the trouble is reported. A delay in reporting the trouble prevents sending information about short-time voltage decays, having no effect on normal operation of the system.

#### INT-IT

The following proximity card arm/disarm devices are identified as INT-IT:

INT-IT

INT-IT-2

INT-CR

The device enables arming / disarming and alarm clearing in partitions by means of proximity cards, key fobs and other 125 kHz passive transponders.

-----------------------------------------------

Name - individual name of the device (up to 16 characters).

Tamper signaled in part. - the partition in which tamper alarm will be triggered in the event of disconnection of the device from the control panel.

###### The table defining module functionality

R - reaction of the partition after moving the card away, when the red LED is on.

G - reaction of the partition after moving the card away, when the green LED (mode A) is on.

Y - reaction of the partition after moving the card away, when the yellow LED (mode B) is on.

Double click on the particular table fields to make required changes.

###### Options

Alarm signal - the device can audibly signal alarms during the Keypad’s alarm time.

until canceled - the device can audibly signal the alarm memory.

3 wrong cards alarm - reading the unknown card code three times can trigger alarm.

Sign. entry delay - the device can audibly signal the entry delay countdown.

Sign. exit delay - the device can audibly signal the exit delay countdown and the auto-arming delay.

Sign. card (hardware) - the device can signal by a single beep that the card code has been read out or the LED has lit up (the code is sent to the control panel after removal of the card and only then the panel reaction to the read code is audibly signaled).

# Global parameters

Options

Times

## Options

Reporting - TELEPHONE - if the option is enabled, the control panel can send event codes to the monitoring station by means of the telephone line.

Reporting - ETHM/GSM - if the option is enabled, the control panel can send event codes to the monitoring station over Ethernet, via GPRS, using CSD technology, using SMS messages and over GSM voice channel.

Telephone messaging - if the option is enabled, the control panel can notify about the occurrence of specific events by means of voice or text messages using the phone communicator.

Answering - modem - if the option is enabled, external initiation of the modem communication with the control panel is possible.

Double call - the option applies to the analog telephone communicator. If enabled, you must call the control panel twice to be connected. The first time, wait for the preset number of rings and then hang up. Then call again within three minutes and the control panel will answer the call immediately. This solution makes it possible to connect after the control panel some additional devices which will be activated after a preset number of rings (e.g. answering machine, fax, etc.).

Tone dialing - the option applies to the analog telephone communicator. If enabled, the control panel will tone dial the telephone numbers (pulse dial, if this option is disabled).

Pulse 1/1.5 (off 1/2) - this option applies to pulse dialing. Before you enable it, make yourself familiar with the valid standard of pulse dialing.

No dial tone test - the option applies to the analog telephone communicator. If enabled, the control panel will not perform the test for dial tone before dialing the number and will start dialing the number 5 seconds after going “off hook”. This makes it possible for the control panel to dial the number when some non-standard tones occur on the telephone line after going off hook (e.g. interrupted tone). When this option is disabled, the control panel will start dialing the number 3 seconds after going off hook, provided that the dial tone is present.

No answer tone test - the option applies to the analog telephone communicator. If enabled:

voice messaging: the voice message is played back 8 (first round) or 16 (next rounds) seconds after completion of number dialing (the control panel does not check whether the line is off-hook),

reporting: the control panel will ignore any signals (including the busy tone) received from the telephone exchange after dialing the telephone number, and will wait for the handshake from the monitoring station.

Enable this option if, after dialing the number, non-standard signals are received from the telephone exchange or in case of very poor quality connections.

Store keyfob events - if the option is enabled, using the keyfob is written into the event log.

Trouble memory until review - if the option is enabled, the trouble memory is being signaled until it is cleared (clearing the trouble memory is possible in VERSA - troubles window or when you quit the 7. System state user function).

Grade 2 - if the option is enabled, the system operates in accordance with the EN 50131 standard requirements for Grade 2, i.e.:

the way of informing the users about the system state by means of LEDs, display and beeps in the keypads meets the requirements of the standard,

the quick arming from keypad (without entering the code) is not available,

new codes in the system must be composed of at least 5 characters,

prior to arming, the control panel checks that no circumstances have occurred that prevent arming (ref. Prevent arming if not ready global option),

in case of arming by means of the LCD keypad, the control panel will check if there are any zones bypassed in the partition - information on the bypassed zones is presented, if the user has the Inspection right,

the warning alarm feature is enabled in the system (see: Warning alarm global option),

the warning alarm is signaled at the 2. Internal siren function output (ref. Warning alarm on internal sirens global option).

Serial data on OUT 3/4 - if the option is enabled, OUT3 and OUT4 outputs send the system status data (zone alarms, fire alarms, troubles, armed modes, etc.) and do not execute any other programmed functions. The outputs may be used to control the NR2-DSC radio monitoring transmitter (NEMROD system - PC-16 OUT format), made by NOKTON.

OUT 3/4 data extended mode - if the option is enabled, the OUT3 and OUT4 outputs will send the system status data in the form of frames (PC-16 OUT UA format). The option is available, if the Serial data on OUT 3/4 option is enabled.

Arm./Disarm./Clear. signaling from zones only - if the option is enabled, outputs with the functions 1. External siren and 2. Internal siren with enabled Arm/Disarm/clear sign. option will signal only:

starting of the arming procedure by zone or by means of keyfob,

no possibility of arming (see: Prevent arming if not ready option or Grade 2 option), if the arming command has been sent from keyfob,

failed attempt of arming by means of keypad or keyfob (see: Prevent arming if not ready option or Grade 2 option),

disarming by zone or by means of keyfob,

alarm clearing by zone or by means of keyfob.

Starting the arming procedure, disarming or alarm clearing by means of keypad, proximity card arm/disarm device or timer are not signaled.

Clear messaging on alarm clearing - if the option is enabled, clearing the alarm will automatically cancel messaging about this alarm, if the user clearing the alarm has the Tel. mess. clearing right.

Service message after tamper alarm - if the option is enabled, information on the tamper alarm can only be cleared from the troubles memory by using the service code. In the LCD keypad, the “System tamper, call service” message will be displayed after the tamper alarm (unless the alarm messages are displayed). The message will no longer be displayed after the troubles memory is reset by the service.

Warning alarm - if the option is enabled, the warning alarm feature is enabled. It purpose is to delay the loud signaling and reporting, if any mistakes are made when entering the protected facility. The warning alarm is not reported. It can be signaled on the keypad, proximity card arm/disarm device or outputs with the function 2. Internal siren. The warning alarm is triggered by the following zone types:

0. Entry/Exit or 1. Entry/Exit final - unless the system is disarmed before completion of the Entry delay countdown,

2. Entry/Exit route - if it is violated during the Entry delay countdown, and the system is not disarmed before completion of the Delay time countdown,

3. Instant - if it is violated during the Entry delay countdown.

The warning alarm lasts 30 seconds. Unless the alarm system is disarmed during this time, the alarm will be triggered by the zone.

Warning alarm on internal sirens - if the option is enabled, the warning alarm will be signaled on outputs with the 2. Internal siren function. The option is available, if the Warning alarm option is enabled.

Tamper alarm always audible - if the option is enabled, the tamper alarm will be signaled always on outputs with the 1. External siren and 2. Internal siren functions (if the option is disabled, only in armed mode). Also, lack of the expander is always saved in the event log as a tamper alarm. If the option is disabled, lack of the expander will be saved in the event log:

as a trouble, if the partition to which the expander is assigned, is disarmed (but the keypad will signal tamper alarm anyway),

as a tamper alarm, if the partition is armed.

Tamper alarm on internal sirens - if the option is enabled, the tamper alarm will be signaled always on outputs with the 2. Internal siren function (in armed mode only if the option is disabled). Additionally, the output will always signal lack of the expander (also when the event is logged as a trouble - see: Tamper alarm always audible option).

Block after 3 unknown codes/cards - if the option is enabled, after entering an incorrect code / reading in an incorrect card three times, the keypad / proximity card arm/disarm device will be blocked for 90 seconds. After this period of time has expired, each subsequent entry of an incorrect code / read-in of an incorrect card will block the keypad / proximity card arm/disarm device at once. The counter of incorrect codes / cards will be reset after a correct code is used.

Service Mode from RESET pins - if the option is enabled, it is possible to start the service mode and local programming “from pins”.

Limit storing "Test transm." events - when the option is enabled, if the “Test transmission” events directly follow one another, they are only written to the event log 3 times. Information on sending next test transmissions is not recorded. Any other event occurring in the system will reset the counter, i.e. it will be possible to log next three consecutive test transmissions.

Prevent arming if not ready - when the option is enabled, if the user arm the system by means of keypad or keyfob, the control panel checks that there are no circumstances that prevent the arming:

a zone with Priority option is violated in the partition which is to be armed,

the 3. Instant, 4. Double knock, 5. 24h burglary, 6. 24h tamper, 7. 24h panic, 8. 24h panic silent, 9. 24h medical or 10. 24h fire type zone is violated in the partition which is to be armed,

there is a trouble in the system.

If one of the aforementioned situations takes place, the control panel will not start the arming procedure (the LCD keypad enables forced arming). If none of the conditions is met, the control panel will start the arming procedure, but at the end of the exit delay countdown it will check again if the arming is possible (the quick arming being an exception). A violated zone or a trouble mean that the arming is not possible (i.e. the arming procedure will fail).

Additionally, when the option is enabled and the user has the Inspection right, the LCD keypad will inform, prior to arming, that there are bypassed zones in the partition (it does not apply to the quick arming).

Arm even if not ready after exit delay - if the option is enabled, a zone violation or trouble found at the end of exit delay countdown does not affect the arming procedure - the system will be armed. The option is available, when the Prevent arming if not ready or Grade 2 option is enabled.

Answering/remote control when armed partition 1 / 2 - if the option is enabled, telephone answering and remote control features are only available when selected partitions are armed.

-----------------------------------------------

Rings before answer - number of rings after which the control panel will answer the incoming call. The parameter refers to the analog communicator.

User code min. lenght - the minimum number of characters required for the control panel to accept a new code or a changed code. This parameter will be included when creating and editing the codes (it is irrelevant to the codes already existing in the system).

## Times

Keypad’s alarm time - time period during which alarm is signaled in keypads and proximity card arm/disarm devices. Up to 255 seconds can be programmed. Programming the value 0 means that the Keypad’s alarm time will be 3 seconds.

No armed indication after - time counted from the moment of partition arming, after expiry of which the keypad LED indicating the partition armed status will go out. Up to 255 seconds can be programmed. Programming the value 0 means that the LED will be lit as long as the partition is armed.

AC loss report delay - time during which the control panel must be without AC power before the trouble is reported. A delay in reporting the trouble prevents sending information about short-time voltage decays, having no effect on normal operation of the system. The trouble reporting delay can be up to 255 minutes.

Tel. line loss report delay - time during which abnormal voltage must be on the telephone line for the control panel to report the telephone line trouble. A delay in reporting the trouble prevents sending information about short-time voltage dips (e.g. during a phone call) or decays. The trouble reporting delay can be up to 255 minutes.

Summer/winter time - the control panel can automatically adjust the clock settings due to a change from the summer time to the winter time and vice versa. The following correction schemes are available:

no correction,

according to the European Union rules,

according to the United States' rules,

correction by 1 hour according to dates,

correction by 2 hours according to dates.

Summer time from / Winter time from - if the control panel clock is to be corrected by 1 or 2 hours according to dates, you should enter the dates (day, month) after the clock is changed to the summer time (moved forward) or to the winter time (moved back).

RTC clock correction - if the accuracy of control panel clock is inadequate, the clock settings may be adjusted once per 24 hours (at midnight) by a defined time. The maximum correction can be ±19 seconds per 24 hours.

# Zones

Zone - 1. a separated part of the protected area that can supervised by a detector or detectors. 2. the terminals on control panel/expander electronics board to which you can connect a detector or another device whose state is to be supervised (panic button, siren tamper contact, power supply output indicating loss of 230 V AC supply, etc.).

A zone can be assigned to one or two partitions. If the zone is assigned to two partitions, it can be armed when both partitions are armed or one of them only.

The system supports the following zones:

hardwired - on the control panel PCB and in expanders. The number of available hardwired zones is determined by the control panel during the identification procedure.

wireless - after connecting the 433 MHz wireless system controller (VERSA-MCU) or the ABAX wireless system controller (ACU-120, ACU-270, ACU-100 or ACU-250). The number of available wireless zones depends on the number of wireless devices registered in the system and is determined during the procedure of adding them.

virtual - zones which do not physically exist, but are controlled by means of keyfobs.

---------------------------------------------------

###### Zone parameters

Zone name - individual name of zone (up to 16 characters).

Partition 1 / Partition 2 - partition to which the zone is assigned. The zone must be assigned at least one partition, for its status to be supervised.

Wiring type - type of detector and the method of its connection (zone configuration):

no detector - no detector is connected to the zone,

NC - the zone supports a detector of NC (normally closed) type,

NO - the zone supports a detector of NO (normally open) type,

EOL - the zone supports a detector of NO or NC type with EOL resistor in the circuit,

2EOL/NO - the zone supports a detector of NO type with two EOL resistors in the circuit,

2EOL/NC - the zone supports a detector of NC type with two EOL resistors in the circuit,

roller - the zone supervise a roller shutter detector,

vibration - the zone supervise a vibration detector (also NC type detector).

Note: In case of the Vibration zone wiring, opening the circuit for 200 ms or longer -irrespective of the programmed number of pulses and sensitivity (see below) - will be interpreted as violation. This solution enables a magnetic contact to be connected in series with the vibration detector.

Sensitivity - depending on selected wiring type:

NO, NC, EOL and 2EOL - the time during which the zone must be violated, so that it can be noted by the control panel. Values from the 20 ms to 5100 ms range can be entered.

ROLLER - 2 digits are to be programmed:

1. - pulse validity - the time counted from the pulse occurrence during which subsequent pulses must occur (their number being defined as the Pulse count) so that the zone is violated. You can enter 0 (the pulse counter will only be reset on arming / disarming), 1 (30 seconds), 2 (120 seconds) or 3 (240 seconds). The pulse counter is automatically reset on arming / disarming.

2. - pulse count - the number of pulses after which the zone will be violated. You can enter values from 1 to 8.

VIBRATION - 2 digits are to be programmed:

1. - sensitivity - occurrence of a pulse with duration equal to or longer than the defined time period will cause zone violation. You can program values from the 3 ms to 96 ms range (with 3 ms increments).

2. - pulses count - the number of pulses after which the zone will be violated. You can enter values from 0 to 7 (for value 0, no pulses will be counted - Sensitivity only will be taken into account).

Zone type - see: Zone types.

Entry delay - the time counted from the moment of violating the 0. Entry/Exit or 1. Entry/Exit final type zone, which makes disarming possible before triggering the alarm. Up to 255 seconds can be programmed. If the value 0 is programmed, the Entry delay programmed for the partition will be taken into account. If the value 0 is programmed for both the zone and the partition, the zone will act as an instant one.

Delay - the time counted from the moment of violating the 2. Entry/Exit route type zone, if it acts as a delayed one. Up to 255 seconds can be programmed. If the value 0 is programmed, the Entry delay programmed for the partition will be treated as the Delay time. If the value 0 is programmed for both the zone and the partition, the zone will act as an instant one.

Delay activation time - the time counted from the moment of violating the 18. Entry route enabling type zone. During countdown of this time, the 2. Entry/Exit route type zone will act as the delayed ones. Up to 255 seconds can be programmed. If the value 0 is programmed, the Entry delay programmed for the partition will be treated as the Delay activation time. If the value 0 is programmed for both the zone and the partition, violation of the zone will have no effect.

Waiting time - the time counted from the moment of violating the 4. Double knock type zone. If the zone is violated again during the waiting time, it will trigger alarm. Up to 255 seconds can be programmed. Programming the value 0 means that the Waiting time will be 30 seconds.

Arm mode - the armed mode activated after violating the 13. Arm/Disarm or 14. Arming type zone. You can select either fully arming, day arming or night arming.

Event - number of the event that will be written into the control panel memory and can be reported to the monitoring station upon violation of the 19. Trouble type zone. You can enter the following values for the corresponding codes of alarm events:

1 - 201 Low water pressure

2 - 202 Low CO2

3 - 203 Gate valve sensor

4 - 204 Low water level

5 - 205 Pump activated

6 - 206 Pump failure

51 - 151 Gas detected

52 - 152 Refrigeration

53 - 153 Loss of heat

54 - 154 Water leakage

55 - 155 Foil break trouble

56 - 156 Day trouble

57 - 157 Low bottle gas level

58 - 158 High temperature

59 - 159 Low temperature

61 - 161 Loss of air flow

62 - 162 Carbon monoxide (CO) detected

63 - 163 Tank level trouble

Entering a different value means that the zone violation will trigger the trouble signaling, but no alarm events from zone will be written to the event log.

Wiring type - type of detector and the method of its connection (zone configuration):

no detector - no detector is connected to the zone,

NC - the zone supports a detector of NC (normally closed) type,

NO - the zone supports a detector of NO (normally open) type,

EOL - the zone supports a detector of NO or NC type with EOL resistor in the circuit,

2EOL/NO - the zone supports a detector of NO type with two EOL resistors in the circuit,

2EOL/NC - the zone supports a detector of NC type with two EOL resistors in the circuit,

roller - the zone supervise a roller shutter detector,

vibration - the zone supervise a vibration detector (also NC type detector).

Note: In case of the Vibration zone wiring, opening the circuit for 200 ms or longer -irrespective of the programmed number of pulses and sensitivity (see below) - will be interpreted as violation. This solution enables a magnetic contact to be connected in series with the vibration detector.

Sensitivity - depending on selected wiring type:

NO, NC, EOL and 2EOL - the time during which the zone must be violated, so that it can be noted by the control panel. Values from the 20 ms to 5100 ms range can be entered.

ROLLER - 2 digits are to be programmed:

1. - pulse validity - the time counted from the pulse occurrence during which subsequent pulses must occur (their number being defined as the Pulse count) so that the zone is violated. You can enter 0 (the pulse counter will only be reset on arming / disarming), 1 (30 seconds), 2 (120 seconds) or 3 (240 seconds). The pulse counter is automatically reset on arming / disarming.

2. - pulse count - the number of pulses after which the zone will be violated. You can enter values from 1 to 8.

VIBRATION - 2 digits are to be programmed:

1. - sensitivity - occurrence of a pulse with duration equal to or longer than the defined time period will cause zone violation. You can program values from the 3 ms to 96 ms range (with 3 ms increments).

2. - pulses count - the number of pulses after which the zone will be violated. You can enter values from 0 to 7 (for value 0, no pulses will be counted - Sensitivity only will be taken into account).

Max. violation time - if the zone is violated for the preset time (e.g. because the detector is damaged or masked), a trouble will be reported. Up to 255 seconds can be programmed. Programming the value 0 means that the control panel will not check whether the zone is violated too long.

Max. no violation time - if zone is not violated for the preset time (e.g. because of damaging or masking the detector), a trouble will be reported. When the zone is armed, the countdown is not running. You can program up to 255 hours. Programming the value 0 means that the control panel will not check whether the zone is violated or not.

###### Zone options

Alarm on exit delay end - when the option is enabled, if the zone is violated at the moment of ending the exit delay countdown, it will trigger an alarm (if this option is disabled, the zone will only trigger the alarm when the status changes from normal to violation during the armed mode).

Priority - if the option is enabled, arming is impossible when the zone is violated.

Bypass disabled - if the option is enabled, the user cannot bypass the zone.

Active in night arm - if the option is enabled, the zone is armed when the night armed mode is activated.

Active in day arm - if the option is enabled, the zone is armed when the day armed mode is activated.

Power-up delay - if the option is enabled, the zone is bypassed for 120 seconds after power supply is turned on (this will prevent triggering false alarms e.g. during start-up of the control panel).

Warning in partial arming - if the option is enabled and the partition is set to day or night arm mode, the zone will trigger a warning alarm. It can be signaled in the keypad, in the proximity card arm/disarm device or at the 2. Internal siren function output. It is not reported to the monitoring station. If you do not disarm the system during the warning alarm, the zone will trigger a burglary alarm (see: parameter Warning time - Partitions).

Note: Warning alarm in the partial armed mode will work irrespective of the Warning alarm global option, which refers to the delay of loud signaling and reporting if any mistakes are made when entering into the protected facility.

Warning on internal sirens - if the option is enabled, warning alarm in the partial armed mode is signaled on the output with the 2. Internal siren function.

Signaling on internal sirens - option for the 19. Trouble zone type. If it is enabled, the zone violation is indicated on the internal sirens.

Auto-reset 3 - if the option is enabled, the zone can trigger up to 3 alarms. As long as the alarm is not cleared or the partition is not armed/disarmed, violations of the zone will not trigger any alarm.

Auto-reset 1 - if the option is enabled, the zone can trigger only 1 alarm. As long as the alarm is not cleared or the partition is not armed/disarmed, violations of the zone will not trigger any alarm.

Note: If the Auto-reset 3 and Auto-reset 1 options are enabled at the same time, the Auto-reset 3 option will have priority.

Clearing Autoreset - if the option is enabled, the alarm counters for zones for which the Auto-reset 3 or Auto-reset 1 option is enabled will be automatically reset at midnight (violations of these zones will be able to trigger alarms again).

Armed if one part. armed - the option refers to the zones which are assigned to both partitions. If the option is enabled, the zone is armed when one of the partitions is armed. If the option is disabled, the zone is armed when both partitions are armed. The option is also available in the event of ubypassing zones during disarming (if the option is enabled, the zone will only be unbypassed after disarming both partitions).

Blocks verification - an option for the 0. Entry/Exit, 1. Entry/Exit final and 17. Shunt lock zone types. If it is enabled, the zone will block alarm verification in the partition:

after the zone violation - the 0. Entry/Exit and 1. Entry/Exit final zone types, and also the 17. Shunt lock zone type, when the Restore disables verif. option is disabled,

after the zone restore - the 17. Shunt lock zone type, when the Restore disables verif. option is enabled.

In case of the 17. Shunt lock zone type, the zone will disarm the system when the Blocks verification option is disabled.

Restore disarms - an option for the 17. Shunt lock zone type. If the option is enabled, the zone restore will disarm the partition to which the zone belongs, and the zone violation will shorten the exit delay time. If the option is disabled, the zone violation will disarm the partition, and zone restore will shorten the exit delay time. The option is available, if the Blocks verification option is disabled.

Restore disables verif. - an option for the 17. Shunt lock zone type. If the option is enabled, the zone restore will block verification in the partition to which the zone belongs, and the zone violation will shorten the exit delay time. If the option is disabled, the zone violation will block verification, and the zone restore will shorten the exit delay time. The option is available, if the Blocks verification option is enabled.

Alarm clearing - an option for the 13. Arm/Disarm and 15. Disarming zone types. If the option is enabled, together with disarming, the alarm is cleared (except for the tamper alarms). Violation of the 15. Disarming type zone will also clear the alarm, when the system is not armed.

Store to event log - an option for the 12: No alarm action zone type. If the option is enabled, violation of the zone is saved into the event log (the way of saving the event depends on the Keybox control option).

Store event only if armed - an option for the 12: No alarm action zone type. If the option is enabled, zone violations are saved in the event log when the partition to which the zone belongs is armed. The option is available when the Store to event log option is enabled.

Keybox control - an option for the 12: No alarm action zone type. If this option is enabled, violation of the zone will result in logging an event which informs that the keybox is open. The event code is sent to the monitoring station. If this option is disabled, an event will be logged informing about zone violation, which will not be reported. The option is available when the Store to event log option is enabled.

## Zone types

0. Entry/Exit - a delayed zone combining two functions:

entry - violation of the zone starts entry delay counting in the partition and turns on delay for the 2. Entry/Exit route type zone.

exit - violation of the zone during exit delay countdown is equivalent to the partition exit.

1. Entry/Exit final - the same as the 0. Entry/Exit type, but if the arming procedure has started and the control panel registers the zone restore, the exit delay countdown will be terminated.

2. Entry/Exit route - during the countdown of Entry delay or Delay activation time the zone acts as a delayed one (alarm will be triggered after expiry of the Delay time). In other situations it acts as an instant zone.

3. Instant - instant zone, which is already armed during exit delay countdown.

4. Double knock - the zone triggers the burglary alarm only after the second violation. The first violation of the zone only results in the “Zone violation” event being logged (the event to may reported in format 4/2). The second violation must take place during the Waiting time countdown.

5. 24h burglary - dedicated zone for the detectors which should be armed at all times (e.g. glass break detectors).

6. 24h tamper - dedicated, permanently armed zone for tamper circuits. Violation of the zone is additionally signaled as a trouble.

7. 24h panic - permanently armed zone, intended for operating the panic buttons.

8. 24h panic silent - permanently armed zone, intended for operating the panic buttons. Alarm from the zone is not signaled on keypads, proximity card arm/disarm devices and outputs, but the event code is sent to the monitoring station.

9. 24h medical - permanently armed zone for calling medical assistance.

10. 24h fire - dedicated, permanently armed zone for operating fire detectors.

11. Detector mask - permanently armed zone for antimasking control. Violation of the zone is interpreted by the control panel as a detector trouble.

12. No alarm action - the zone may be used to control the output with function 13. Zone violation, 15. Controlled or 16. READY status. An additional option enables the zone to be used for supervision of the key box (Keybox control option).

13. Arm/Disarm - the zone controls the arming status of the partition it belongs to. Violation of the zone starts the arming procedure or disarms the partition (depending on the current status of the partition).

14. Arming - violation of the zone starts the procedure of arming the partition to which the zone belongs.

15. Disarming - violation of the zone disarms the partition to which the zone belongs.

16. Exit delay terminator - violation of the zone ends the partition exit delay countdown.

17. Shunt lock - the zone ends the partition exit delay countdown and - depending on the Blocks verification option - will disable verification or disarm the partition to which it belongs. The way of controlling (the zone violation / zone restore) is determined by the option Restore disables verif. or Restore disarms.

18. Entry route enabling - violation of the zone activates delay for the 2. Entry/Exit route type zones in the partition to which the zone belongs. The zones will act as delayed ones for the Delay activation time. After expiry of the time, unless the system is disarmed, the zones will again act as the instant ones. If the Delay activation time for a zone will be programmed as equal to 0, and at the same time the Entry delay programmed for the partition is equal to 0, violation of the zone will have no effect.

19. Trouble - violation of the zone is treated by the control panel as a trouble. Additionally, an alarm event may be written into the control panel memory (see: Event parameter - Zones).

# VERSA - Outputs

Using the outputs, the control panel controls the operation of external devices. There can be up to 12 outputs in the system. The system supports the following outputs:

hardwired - on the control panel PCB and in the expander.

wireless - after connection of the ABAX wireless system controller (ACU-120, ACU-270, ACU-100 or ACU-250). The number of available wireless outputs depends on the number of wireless devices registered in the system and is determined during the procedure of adding them.

Outputs

Quick control

## Outputs

###### Output parameters

Output name - individual name of the output (up to 16 characters).

Output function - see: Output functions.

Cut-off time - time during which the alarm outputs and the outputs with functions 13. Zone violation, 14. Chime, 15. Controlled and 21. Detectors resetting are active. Entering the value 0 modifies the way of functioning of some outputs:

alarm outputs remain active until the alarm is cleared,

the 13. Zone violation output remains active throughout the time of zone violation (the Pulse option is disabled then),

the 14. Chime output remains active until deactivated by the Outputs reset user function,

the 15. Controlled output remains active until another violation of the controlling zone, disabling of timer or disabling of the output by means of keypad (bistable mode).

Triggering - depending on the type of output, its status depends on:

- the status of selected zones;

- 18. Armed status - the armed mode active in the partition;

- 19. Trouble status and 22. ETHM/GSM trouble status - the occurrence of selected troubles;

- 20. Alarm/arm status - the armed mode active in the partition or the alarm in the selected partition.

###### Output options

Clearing from part. 1 / Clearing from part. 2 - depending on the output function:

alarm outputs - the alarm can be cleared by users having access to the selected partition,

the 1. External siren and 2. Internal siren outputs with enabled Arm/Disarm/Clear sign. option - the output will be activated when in the selected partition the procedure of arming has been initiated, arming is not possible, armed mode is deactivated, or when alarm is cleared in it,

5. “DURESS” alarm - the users having access to the selected partition can deactivate the output by means of the Outputs reset user function.

Partition 1 / Partition 2 - depending on the output function:

12. Power supply on armed - the output is active when the selected partition is armed (it activates after starting the arming procedure, without taking the exit delay into account),

15. Controlled - the output can be controlled by the users having access to the selected partition by means of the user function Control (if no partition is selected, the function Control will not be available in the keypad),

17. Exit delay status - the output is active when the exit delay countdown is running in the selected partition,

21. Detectors resetting - the output activates for a preset time, when the arming procedure is initiated in the selected partition (without taking into account the exit delay). The users authorized to access the given partition can activate the output by using the Outputs reset function.

Reset in partition 1 / Reset in partition 2 - depending on the output function:

11. Fire detectors power supply - the users having access to the selected partition can deactivate the output for 16 seconds by means of the Outputs reset user function,

14. Chime, for which the Cut-off time equal to 0 has been programmed - the users having access to the selected partition can deactivate the output by means of the Outputs reset user function.

Pulse - output with pulsating mode of operation. This option refers to the outputs for which the cut-off time is to be programmed (except for the 1. External siren and 2. Internal siren outputs), and outputs with the 17. Exit delay status, 18. Armed status, 19. Trouble status and 22. ETHM/GSM trouble status functions.

Polarity +12V - sets the output operating mode (see table below). If the option is disabled, the output is inverted (for the relay output, it means that the NC terminal is open, and the NO terminal is closed).

|  | “-” terminal of high-current output / low-current output |
| --- | --- |
|  | option enabled (normal polarity) | option disabled (reverse polarity) |
| active state | shorted to ground | disconnected from ground |
| inactive state | disconnected from ground | shorted to ground |

Fire alarms sign. - option for the 1. External siren and 2. Internal siren outputs. The output signals in pulsating mode the fire alarms from selected zones and partitions (see: Alarm signaling - partition 1 and Alarm signaling - partition 2 output options).

One partition sign. - option for the 18. Armed status and 20. Alarm/arm status outputs. The output indicates armed mode when any of the two partitions is armed (if the option is disabled, only when both partitions are armed).

Arm/Disarm/Clear sign. - option for the 1. External siren and 2. Internal siren outputs (see also: Clearing from part. 1 and Clearing from part. 2 output options and Arm./Disarm./Clear. signaling from zones only global option - Options). The output signals:

starting the arming procedure (which is equivalent to arming if no exit delay has been programmed) - 1 tone,

disarming - 2 tones,

alarm clearing - 4 tones,

denial of arming or arming procedure failure (see: Prevent arming if not ready global option or Grade 2 global option - Options) - 7 tones.

Tone duration is about 0.3 second.

Alarm signaling - part. 1 / Alarm signaling - part. 2 - an option for the alarm outputs. The output signals the selected partition alarms which were not triggered by zones.

Timer 1 / Timer 2 / Timer 3 / Timer 4 - options for the 15. Controlled outputs. The output is controlled by selected timer (if timer status changes to “ON", the output will be activated for the Cut-off time).

Mainboard TMP input - an option for the 1. External siren, 2. Internal siren and 10. Tamper alarm outputs. The output will be activated by the mainboard tamper (violation of the mainboard TMP zone).

###### Output S

On the control panel electronics board, there is a dedicated output for connecting a sounder to be installed in the enclosure (the sounder is included in the control panel delivery set).

---------------------------------------------------

Cut off time - period of time during which the output is active.

Signaling mode - type of audible signaling.

### Output functions

0. Not used

1. External siren - signals the burglary, panic and tamper alarms.

2. Internal siren - signals the burglary, panic and tamper alarms, as well as the warning alarms.

Note: The way of signaling the tamper alarms by the outputs with functions 1. External siren and 2. Internal siren depends on the global options Tamper alarm always audible and Tamper alarm on internal sirens (see: Options).

3. Burglary - signals the alarms from 0 to 5 type zones.

4. Fire alarm - signals the fire alarms from keypad and from 10. 24h fire type zones.

5. “DURESS” alarm - signals that code with Duress right was used for arming/disarming or alarm clearing.

6. Panic alarm - signals the panic alarms from keypad and from 7. 24h panic type zones.

7. AUX. alarm - signals the medical assistance call alarms triggered from keypad and from 9. 24h medical type zones.

8. Alarm - not verified - signals the unverified alarms.

9. Alarm - verified - signals the verified alarms.

10. Tamper alarm - signals the tamper alarms.

11. Fire detectors power supply - the dedicated output for power supply of the fire detectors with automatic verification alarm. After violation of the fire zone the output will be disabled for 16 seconds. If, after the power is turned on again, another violation from the fire zone occurs, the fire alarm will be triggered.

12. Power supply on armed - the dedicated output for power supply of the detectors which should not be active when the system is disarmed. It gets activated at the moment of starting the arming procedure (the exit delay is not taken into account).

13. Zone violation - signals violation of the zones.

14. Chime - signals violation of the zones when they are disarmed.

15. Controlled - controlled by means of zones, timers, keypad or from keyfob.

16. READY status - indicates whether the system is ready for arming, i.e. whether there are no violated zones (active when there is no violation).

17. Exit delay status - indicates that the Exit delay countdown is running.

18. Armed status - indicates the armed mode (after completion of the exit delay countdown).

19. Trouble status - indicates troubles.

20. Alarm/arm status - indicates alarms (pulsating mode) and arm status (continuous mode - after end of the exit delay countdown).

21. Detectors resetting - dedicated output to control the alarm memory reset in detectors. Activated at the moment of starting the arming procedure (the exit delay is not taken into account). It can also be activated by using the Outputs reset user function.

22. ETHM/GSM trouble status - indicates ETHM module troubles.

## Quick control

If the quick control of the outputs 15. Controlled is to be available in keypads, the outputs of this type must be assigned to the corresponding keypad keys. One output can be assigned to each of the keys designated with numerals.

# VERSA - Timers

The timer compares the time to that of the control panel clock and executes the selected function at the programmed time. Using the timers, it is possible to control the armed mode of partitions and the outputs 15. Controlled. You can program 4 timers.

---------------------------------------------------

Timer names - individual timer names (up to 16 characters).

Arming: Partition 1 / Arming: Partition 2 - the arming mode that will be activated in the partition when the timer will start.

On - timer starting time (the timer can be started twice a day: according to the settings scheduled for the given day of the week and according to the everyday settings).

Off - timer ending time (the timer can be ended twice a day: according to the settings scheduled for the given day of the week and according to the everyday settings).

Exception - the period during which the timer will be started/ended at a different time than indicated in the weekly schedule. 4 exceptions can be programmed for a timer. You can program for each exception:

the date from which the exception will apply,

the date to which the exception will apply,

the timer start/end time when an exception applies.

# VERSA - Reporting

The control panel can send event codes to the monitoring station by using the following transmission paths:

analog telephone line [built-in analog telephone communicator],

Ethernet network [built-in Ethernet communication module],

GPRS [built-in GSM communication module],

CSD [built-in GSM communication module],

SMS messages (control panel gets no acknowledgement of event code receipt) [built-in GSM communication module],

GSM voice channel (the use of this transmission path is not recommended because of distortions that may occur when sending the event codes) [built-in GSM communication module].

Monitoring Stations

GSM/ETHM reporting

SIA-IP

Event codes

Starting the reporting

## Monitoring Stations

Reporting - TEL. - if the option is enabled, the control panel can send event codes to the monitoring station by means of the telephone line.

Reporting - ETHM/GSM - if the option is enabled, the control panel can send event codes to the monitoring station over Ethernet, via GPRS, using CSD technology, using SMS messages and over GSM voice channel.

###### Options

Station 1 or 2 - if the option is enabled, the control panel will make an attempt to send the event code to station 1 and, if unsuccessful, to station 2.

Station 1 - if the option is enabled, the event codes are only sent to station 1.

Station 2 - if the option is enabled, the event codes are only sent to station 2.

Station 1 and 2 - if the option is enabled, the event codes are sent to both stations.

Events amount limiting - if the option is enabled, events from the same source are saved into the event log and reported to the monitoring station 3 times only. This option does not apply to the alarms from zones (see: Auto-reset 3 or Auto-reset 1 zone option - Zones).

Report module restarts - if the option is enabled, in case of sending event codes in Contact ID or SIA format, the monitoring station is informed about module restarts.

Restore after bell - if the option is enabled, the zone restore code will only be sent to the monitoring station after the alarm signaling ends. If a few outputs are signaling alarm, the zone restore code will be sent when one of them stops signaling the alarm.

Restore after disarm - if the option is enabled, the zone restore code will only be sent to the monitoring station after disarming the partition to which the zone belongs.

###### Station 1 / Station 2

Reporting format - format in which event codes are sent to the monitoring station.

Note: In the TELIM format, events can only be sent via the analog telephone line.

Telephone

Telephone no. - telephone number of the monitoring station for reporting via the analog telephone line (see: Programming telephone numbers).

Repetitions - the number of attempts to send an event code via the analog telephone line. If all attempts fail, the control panel will suspend reporting via the analog telephone line. Up to 31 retries can be programmed. Programming the value 0 means that monitoring will be suspended after 8 attempts.

Suspend time - the time for which reporting will be suspended, if attempts fail to send an event code through all provided transmission paths. The control panel will resume the attempt of establishing telephone connection with the monitoring station after this time expires or a next, new event occurs. Up to 30 minutes can be programmed. Programming the value 0 means that an attempt to establish telephone connection with the monitoring station will only be taken after occurrence of a new event in the system.

ETHM/GPRS

Server address - network address of the monitoring station for reporting via Ethernet or GPRS. You can enter either the IP address or the domain name.

Port - number of port used for communication between the control panel and the monitoring station. You can enter a value from 1 to 65535.

Station key - a string of up to 12 alphanumeric characters (digits, letters and special characters), which is used for encryption of data sent to the monitoring station.

ETHM/GPRS key - a string of up to 5 alphanumeric characters to be used for identification of the control panel for the purposes of reporting via Ethernet or GPRS.

Identifiers

Event codes are sent to the monitoring station with one of the four identifiers:

identifier 1 - events from zones (alarms, tampers, troubles),

identifier 2 - alarms triggered from keypad, arming/disarming by means of zones, quick arming, loss of communication with wireless devices, as well as expander troubles and tampers,

identifier 3 - arming/disarming and alarm clearing by means of code or proximity card,

system identifier - power supply troubles, zone bypasses, troubles of control panel high-current outputs, communication bus trouble, programming related events, etc.

The identifier consists of 4 hexadecimal characters (digits or letters from A to F). Entering the value 0000 means that events assigned to that identifier will not be reported. Using the digit 0 in the identifiers is not recommended.

SIA / TELIM prefix - 2 characters which will precede each of the identifiers in case of the SIA and TELIM formats. Thus an identifier consisting of 6 characters can be obtained. 2 hexadecimal characters (digits or letters from A to F) can be programmed. Entering 00 means that the prefix will not be added. Using the digit 0 in the prefix is not recommended.

Station 1 options / Station 2 options

SIA - send part. name - if the option is enabled, in the SIA format, the name of partition where the event took place will also be sent, in addition to the event code.

SIA - send source name - if the option is enabled, in the SIA format, the name of event source (zone, user, etc.) will also be sent, in addition to the event code.

SIA - confirm each block - if the option is enabled, the control panel will wait for acknowledgement by the monitoring station of receiving every data block sent in the SIA format. The option applies to telephone reporting.

SIA - id. conf. required - if the option is enabled, the control panel will wait for acknowledgement by the monitoring station of receiving the identifier with which the data were sent. The option applies to telephone reporting.

Longer waiting for initial handshake - if the option is enabled, the control panel will wait longer for handshake from the monitoring station in case of sending events in the Ademco Express, Contact ID or SIA format. Enable this option in the event of telephone reporting, if the monitoring station sends a non-standard initial handshake.

Long kiss-off signal - if the option is enabled, the control panel will accept a long kiss-off (acknowledgment) signal for receiving events in case of Ademco Express and Contact ID formats. Enable this option in the event of telephone reporting, if the monitoring station acknowledges receiving events in a non-standard way (the kiss-off signal is longer than 800 ms).

###### Test transmissions

Note: The test transmission is sent through all transmission paths which are shown on the list defining the order in which transmission paths are used (see: GSM/ETHM reporting).

The test transmission may be sent:

at a specified time. The test transmission code will be sent regularly at a defined time. The number of days between transmissions and the time of sending transmission are programmed. Programming the value 0 for days means that the transmission will be sent everyday (in the same way, as in case programming the value 1).

in specified time intervals. You can program the time intervals in which test transmissions are to be sent when the system is disarmed and when the system is armed (number of days, hours and minutes). The test transmission code will be sent:

after a predefined period of time has elapsed since the last transmission, irrespective of whether it was a test transmission, or the code of another event was sent (the No sync. to last transmission option disabled),

at predefined time intervals (the No sync. to last transmission option enabled).

###### Buttons

Export to STAM - click to export the names of zones, partitions, users and modules for the needs of STAM-1 or STAM-2 monitoring station.

Print - click to print all reporting parameters.

OK - click to close the window.

## GSM/ETHM reporting

###### Transmission priority

If sending an event code to the monitoring station using one transmission path fails, the control panel can use another transmission path. You must specify the order of using different transmission paths by the control panel. A successful send of the event code to the monitoring station will terminate the procedure (except for the test transmissions).

Notes:

The control panel will only use the transmission paths for which priority is specified (they are included in the list defining the order of using transmission paths).

In the case of SMS reporting, the control panel gets no acknowledgement of receiving the event codes by the monitoring station, hence this transmission path should be used as the last one.

The switch-over from one SIM card to the other one requires time (for example, to log onto the network), so it is better to use up all the transmission paths available for one SIM card.

The switch-over from one SIM card to the other is affected by the Lock time and Return time parameters (see: GSM).

Programming the order of transmission paths:

- Click on the Add button. The list with all transmission paths will be displayed.

- Click on the transmission path you want to add.

- Repeat steps 1 and 2 to add next transmission paths.

- If you want to change the order of transmission paths on the list, use the  and  buttons to do so.

###### Telephone numbers

GSM reporting - phone number of the monitoring station for reporting via GSM voice channel.

SMS reporting - phone number of the monitoring station for reporting by means of SMS messages.

CSD reporting - phone number of the monitoring station for reporting with the use of CSD technology.

###### SMS format

SMS format for reporting by means of SMS messages. It must be defined as required by the monitoring station. The SMS message format, preset by default in the control panel, corresponds to the default settings of the STAM-2 monitoring station (firmware version 1.2.0 or newer) for the Contact ID format. When programming the SMS message format, you should keep in mind that only event code and identifier will be sent for formats other than Contact ID.

## SIA-IP

###### Monitoring station 1 / Monitoring station 2

IP format - if the event codes are to be sent via Ethernet or GPRS, specify whether SATEL format or SIA-IP format (SIA DC-09 standard) will be used.

Protocol - if the event codes are to be sent via Ethernet or GPRS, specify whether TCP or UDP protocol will be used.

Options - options related to SIA-IP format:

Send MAC address - if this option is enabled, the MAC address is sent with event code.

Send timestamp - if this option is enabled, the date and time are sent with event code (the monitoring station can change the date and time in the control panel).

Encrypt data - if the option is enabled, the data being sent are encrypted, and the date and time are sent with event code (the monitoring station can change the date and time in the control panel).

SIA-IP key - the key to encrypt data to be sent using the SIA-IP format.

hex - if the option is enabled, you can enter up to 32 hexadecimal characters as the SIA-IP key. If the option is disabled, you can enter up to 16 alphanumeric characters as the SIA-IP key.

SIA-IP acct - a string of up to 16 hexadecimal characters, which is used to identify the control panel for the purpose of reporting in SIA-IP format.

Supervision interval - in the case of reporting in the SIA-IP format, an additional transmission can be sent at specified intervals to check communication with the monitoring station. You can program a number of days, hours, minutes and seconds between the transmissions. Entering zeros only means that no additional transmission will be sent.

## Event codes

For the pulse and Ademco Express formats, it is necessary to program codes which will be reported to the monitoring station if the defined events occur. An event code consists of 2 hexadecimal characters (digits or letters from A to F). The reported events are those for which a code different from “00” has been programmed.

For the Contact ID and SIA formats, event codes consistent with format specification are sent. In case of the Contact ID (selected) and SIA (selected), the codes must be programmed at the events which are to be reported (not the programmed code, but a code consistent with the format specification will be sent).

## Starting the reporting

- Get the data necessary to properly start the reporting from the monitoring station operator:

  - depending on the transmission path:

    - telephone number of the monitoring station (reporting via analog telephone line, CSD reporting, SMS reporting, reporting via GSM voice channel),

    - server address, TCP port number, Station key and ETHM/GPRS key (reporting via Ethernet network and GPRS reporting),

    - SMS message format (SMS reporting),

  - transmission format required by the monitoring station,

  - identifiers assigned to the alarm system,

  - list of event codes (not applicable to Contact ID and SIA formats).

- Determine whether the event codes will be sent to both monitoring stations or to one of them only (enable one of the options: Station 1 or 2, Station 1, Station 2 or Station 1 and 2 - Monitoring Stations).

- Determine whether the number of events from the same source is to be limited (Events amount limiting option - Monitoring Stations).

- Determine when the restore code is to be sent (Restore after bell, Restore after disarm options - Monitoring Stations).

- For the monitoring station to which event codes are to be sent (Monitoring Stations):

- define the format in which event codes will be sent (Reporting format parameter),

- if you select Ademco Express, Contact ID or SIA format, configure the additional options (SIA - send part. name, SIA - send source name, SIA - confirm each block, SIA - id. conf. required, Longer waiting for initial handshake, Long kiss-off signal),

- program the identifiers to be sent with the event codes,

- for the SIA or TELIM format, if the identifier is to consist of 6 characters, program SIA / TELIM prefix.

- Define the parameters of test transmissions (Monitoring Stations).

- If a transmission format other than Contact ID (full) or SIA (full) is selected, program the codes for events which are to be reported (Event codes).

- Define priority of the transmission paths to be used by the control panel (GSM/ETHM reporting).

Reporting via analog telephone line

Reporting via Ethernet network

Reporting with the use of GPRS technology

Reporting with the use of CSD technology

Reporting by means of SMS messages

Reporting via GSM voice channel

### Reporting via analog telephone line

- Enable the Reporting - TELEPHONE option (Monitoring Stations).

- Program the monitoring station parameters (Monitoring Stations):

phone number for reporting via analog telephone line,

the number of attempts to connect to the station after which, if there is no connection, the control panel will suspend reporting,

time for which reporting will be suspended after the programmed number of attempts to establish connection with the station has been made.

- Configure the global options for analog telephone communicator (Options):

determine how the telephone numbers should be dialed (Tone dialing; in case of the pulse dialing option - Pulse 1/1,5 (off 1/2)),

determine whether the control panel, prior to dialing the number, should check the telephone line for dialing signal (No dial tone test),

determine the reaction to signals received after dialing the number (No answer tone test).

### Reporting via Ethernet network

- Enable the Reporting - ETHM/GSM option (Monitoring Stations).

- Program the monitoring station parameters (Monitoring Stations):

monitoring station address,

TCP port,

data encryption key (Station key),

control panel identifier for the purposes of monitoring via Ethernet/GPRS (ETHM/GPRS key).

- Define whether the events are to be sent in SATEL format or SIA-IP format (IP format - SIA-IP).

- If the SIA-IP format is to be used, configure the additional options and parameters (Send MAC address, Send timestamp, Encrypt data, SIA-IP key, hex, SIA-IP acct and Supervision interval - SIA-IP).

- Specify whether TCP or UDP protocol is to be used (SIA-IP).

- Configure the Ethernet communication module (ETHM):

enable the ETHM option,

configure the module network settings.

### Reporting with the use of GPRS technology

- Enable the Reporting - ETHM/GSM option (Monitoring Stations).

- Program the monitoring station parameters (Monitoring Stations):

monitoring station address,

TCP port,

data encryption key (Station key),

control panel identifier for the purposes of monitoring via Ethernet/GPRS (ETHM/GPRS key).

- Define whether the events are to be sent in SATEL format or SIA-IP format (IP format - SIA-IP).

- If the SIA-IP format is to be used, configure the additional options and parameters (Send MAC address, Send timestamp, Encrypt data, SIA-IP key, hex, SIA-IP acct and Supervision interval - SIA-IP).

- Specify whether TCP or UDP protocol is to be used (SIA-IP).

- Configure the built-in GSM module (GSM):

enable the SIM1 option and/or SIM2 option,

enter GPRS parameters required by the GSM network operator.

### Reporting with the use of CSD technology

- Enable the Reporting - ETHM/GSM option (Monitoring Stations).

- Program the monitoring station phone number for CSD reporting (GSM/ETHM reporting).

- In the built-in GSM module settings, enable the SIM1 option and/or SIM2 option (GSM).

### Reporting by means of SMS messages

- Enable the Reporting - ETHM/GSM option (Monitoring Stations).

- Program the monitoring station parameters (GSM/ETHM reporting):

phone number for reporting by means of SMS messages,

SMS message format (if other than default).

- Configure the built-in GSM module (GSM):

enable the SIM1 option and/or SIM2 option,

enter the SMS center number.

### Reporting via GSM voice channel

- Enable the Reporting - ETHM/GSM option (Monitoring Stations).

- Program the monitoring station phone number for reporting via GSM voice channel (GSM/ETHM reporting).

- In the built-in GSM module settings, enable the SIM1 option and/or SIM2 option (GSM).

# VERSA - Tel. messaging

In this window you can configure the notification realized by means of:

voice messages [analog telephone communicator or GSM communication module],

installer defined text messages, which can be sent as:

PAGER type messages [analog telephone communicator],

SMS messages [GSM communication module].

Telephone no.

Event assignment

SMS/Pager messages

Starting the telephone messaging

## Telephone no.

Telephone messaging - if the option is enabled, the control panel can notify about the occurrence of specific events by means of voice or text messages using the phone communicator.

Round count - the number of attempts made by the control panel to notify the selected telephone number about the event. You can program from 1 to 7.

Retries no. for one round - the number of attempts made by the control panel to get through during one round. You can program from 1 to 7.

###### The list of telephone numbers to be notified

Description - individual name of the telephone number (up to 16 characters).

Telephone no. - the telephone number to which messaging is effected (see: Programming telephone numbers).

Mode - selection of the form in which the indicated telephone number is to be notified (0 - no messaging, 1 - PAGER1, 2 - PAGER2, 3 - voice message, 4 - SMS).

GSM - the option applies to voice messaging. If it is enabled, the messaging is performed by the built-in GSM module. If it is disabled - by the built-in analog telephone communicator.

Code - 4 digits which, if entered using the telephone keys, will acknowledge receipt of the voice notification and clear telephone messaging of the event.

User - the user assigned to the phone number. If the user has the INT-VG access right, he will get automatically access to the voice menu after acknowledging the voice notification.

Comments - in this field, you can enter additional information on the given phone.

## Event assignment

The tabs can be used for programming how particular events should be notified.

Telephone numbers - telephone numbers from the list of telephones to be notified (Telephone no.). Double click on individual fields to enter changes. The X symbol means that messaging will be effected to the given phone number, if the event occurs.

Message no. - enter in the field the number of text message that will be used for notification. If the notification is to be effected in the form of voice messages (Telephone no.), the voice message assigned to that text message (SMS/Pager messages) will be used.

Message - the field shows the content of text message, as defined in the SMS/Pager messages tab.

Voice msg. - displayed in this field is the number of voice message that will be used for notification of the event. The number is assigned to the text message number in the SMS/Pager messages tab.

## SMS/Pager messages

No. - number of text message.

Voice msg. - enter the number of voice message that will be assigned to the given text message. When entering the text message number in the Event assignment tab, you automatically select the number of voice message. The voice messages are numbered from 0 to 15. The same voice message can be assigned to several text messages.

Message - enter the content of text message.

###### Message type

Select the type of message editing:

Digital - for messages to be sent to PAGER call systems.

Text - for messages to be sent as SMS messages.

###### Pager parameters

Pager 1 / Pager 2 - you can define pager identification parameters in this field.

SMS-GSM SATEL - when the option is enabled, the pager identification parameters are adjusted according to the GSM module requirements for conversion of the PAGER type message into the SMS message.

## Starting the telephone messaging

- Enable the Telephone messaging option (Telephone no.).

- Define the number of attempts made by the control panel to notify about the event (parameters Round count and Retries no. for one round - Options).

- Enter the phone numbers that are to be notified, and description of those phone numbers (Telephone no.).

- Specify, of which events, which phone numbers and by means of which messages the control panel is to notify (remember that a text message number is assigned to each event, and the voice message assigned to that text message will be used for voice notification) (Event assignment).

- Determine whether alarm clearing should cancel the messaging (global option Clear messaging on alarm clearing - Options).

PAGER messaging

Voice messaging

SMS messaging

### PAGER messaging

- Select PAGER1 or PAGER2 as the messaging type for the phone number to be notified (Telephone no.).

- Enter the content of messages that are to be used for notification (SMS/Pager messages).

- Define the pager identification parameters (SMS/Pager messages).

- Configure the global options related to analog telephone communicator (Options):

determine how the telephone numbers should be dialed (Tone dialing; in case of the pulse dialing option - Pulse 1/1,5 (off 1/2)),

determine whether the control panel, prior to dialing the number, should check the telephone line for dialing signal (No dial tone test),

### Voice messaging

- For the telephone number to be notified: (Telephone no.):

select voice messaging as the type of notification,

enter the code, if the telephone user can confirm having listened to the voice message and clear the messaging,

indicate the alarm system user, if the telephone user is to automatically get access to the voice menu after entering the code (the user must have the INT-VG access right).

- Assign voice messages to text messages (SMS/Pager messages).

- Synthesize the voice messages that are to be used for notification (INT-VG).

###### Voice messaging via analog telephone line

- Disable the GSM option for the telephone number to be notified (Telephone no.).

- Configure the global options related to analog communicator telephone (Options):

determine how the telephone numbers should be dialed (Tone dialing; in case of the pulse dialing option - Pulse 1/1,5 (off 1/2)),

determine whether the control panel, prior to dialing the number, should check the telephone line for dialing signal (No dial tone test),

determine whether the control panel is to play back the voice message after going off-hook, or 8/16 seconds after the dialing is completed (No answer tone test).

###### Voice messaging via GSM network

- Enable the GSM option for the telephone number to be notified (Telephone no.).

- Enable the SIM1 option and/or SIM2 option in the settings of built-in GSM module (GSM).

### SMS messaging

- Select SMS as the type of messaging for the telephone number to be notified (Telephone no.).

- Enter the content of messages which are to be used for notification (SMS/Pager messages).

- Configure the built-in GSM module (GSM):

enable the SIM1 option and/or SIM2 option,

enter the SMS center number.

# SMS control

The alarm system can be controlled by means of SMS messages containing appropriate control commands. The SMS messages should be sent to the number of the currently used SIM card. You can program 16 control commands.

Note: SMS control can be exercised from the telephones whose numbers and users are included in the table available when configuring the built-in GSM module (GSM).

-----------------------------------------------

Control SMS - control command which can be sent in the SMS message to run the function assigned to the command. You can enter up to 8 alphanumeric characters (spaces can be used, but at least one character must be different from the space).

Notes:

The content of control commands must vary. If the content of two different commands is identical, the control panel, having received the SMS messages, will execute only one function anyway.

The content of one control command must not be inserted into the content of another command.

Function - the function that will be started after the built-in GSM module receives an SMS message containing control command to which the function is assigned. To select the function:

- Right click on a field in the Function column. A menu will be displayed, showing the available function groups.

- Hover the cursor over one of such groups. A list of functions available in that group will be displayed.

- Click on the function that is to be assigned to the control command.

# VERSA - Users

Users

User Schedules

## Users

The data about users are presented in the table.

User name - individual user name (up to 16 characters).

Schedule - the user schedule, defining the authority level of the given user. Click on the field to display the  button. Click on the  button to display a list of all available schedules.

Part. 1, Part. 2 - partitions. The X symbol indicates that the user has access to the partition. Double click on the field to enter changes.

Code - user code. It can consist of 4 to 8 digits. The codes are presented as a sequence of asterisks, unless the Show codes field is selected. You can enter a new code using the keyboard.

Card - code of the user's proximity card.

---------------------------------------------------------

Show codes - select the option in the Code column to display the codes of the users who have not changed their codes.

###### Buttons

Card - click to add a proximity card to the user (see: Adding proximity card).

Print - click to print out information on users, user schedules and functions assigned by default to the keyfob buttons.

OK - click to close the window.

Adding a user

Removing a user

Adding proximity card

Removing proximity card

### Adding a user

- Enter the user's individual name.

- Select the user schedule, i.e. define the user authority level.

- Select the partition(s) to which the user is to have access.

- Enter the user code.

- Click on  to save the data to the control panel.

### Removing a user

- Click on the field in the Schedule column, next to the user to be removed. The  button will appear in the field.

- Click on the  button and, from the menu that will be displayed, select 0: NOT PRESENT. The user name will be grayed out and the other fields will be blank.

- Click on  to save the changes to the control panel.

### Adding proximity card

You can add a proximity card by entering its number manually or reading its number by means of a device provided with proximity card reader.

###### Entering the number manually

- In the Card column, click on the field of the user to whom you want to add a card.

- Enter the card number and confirm by pressing ENTER.

- Click on  to save the changes to the control panel.

###### Reading the number

- Click on any field related to the user to whom you want to add a proximity card.

- Click on the Card button. The card adding window will open.

- According to the prompts displayed in the window, read in the card twice on a device provided with proximity card reader (keypad, proximity card arm/disarm device).

- When the Card read message is displayed, click on the Close button. The card adding window will be closed. The new card number will be displayed in the Card column.

- Click on  to save the changes to the control panel.

### Removing proximity card

- In the Card column, double click on the field of the user whose card you want to remove.

- Press the DELETE key to clear the card number.

- Click on  to save the changes to the control panel.

## User schedules

The control panel offers 5 user schedules. The user schedule defines the user rights. When adding or editing a user, one of the user schedules is selected.

The default settings of keyfob are tied to the user schedule. If a keyfob is assigned to the user, the default keyfob settings will be suitable for the user schedule.

---------------------------------------------------------

###### Schedule names

You can enter into the table individual names of the user schedules (up to 16 characters).

###### Rights list

The digits by which the columns are designated correspond to the numbers of user schedules from the table with schedule names. The X symbol in the field means that the given right is assigned to the user schedule. Double click on the field to be able to enter changes.

Note: Any changes made to the rights list of a given user schedule will automatically change the authority level of the users to whom the given schedule is assigned.

###### Default functions of keyfob buttons and LEDs

For each user schedule, you can choose the functions that will be assigned by default to the buttons and LEDs on the keyfob. When adding a new keyfob, a default set of functions provided for the user schedule will be suggested, which, however, can be individually modified for each user. Changing the default functions for buttons and LEDs does not affect the keyfobs which have already been added to the users.

The digits by which the columns are designated correspond to the numbers of user schedules from the table with schedule names. Click on the field and press the right mouse button to display a drop-down menu, where you can select the function.

Rights

### Rights

Arming - the user can arm the system.

Disarming - the user can disarm the system.

Alarm clearing - the user can clear alarms.

Tel. mess. clearing - the user can cancel messaging by means of the Abort v.msg. user function (if he has at same time the Alarm clearing right and the Clear messaging on alarm clearing global option is enabled, the messaging will be automatically canceled when the alarm is cleared).

Auto-arming defer - using the A-arm defer. function, the user can defer arming by the timer.

Zone inhibition - the user can inhibit the system zones by means of the Inhibit function.

Zone isolation - using the Isolate function, the user having additionally the Zone inhibition right can isolate the system zones.

Change access code - the user can change own access code (Change code function).

Users editing - the user can add, edit and delete users (Users function).

Control - the user can control the outputs by means of the Control function.

Programming - the user has access to the Settings function, which allows him to program the control panel clock, timers, telephone numbers for messaging and codes to clear messaging.

DOWNLOAD/SERVICE - the user can define the rules of service access and initiate remote programming of the control panel from the keypad.

Inspection - the user has access to the Event log and System state functions. In case of arming by means of the LCD keypad, the user gets information about bypassed zones and causes of denial of arming, if any (the user can enforce the arming).

Tests - the user has access to the Tests submenu.

DURESS - a special right that allows to define in the system a code/card which, if used for arming/disarming or alarm clearing, will trigger a silent alarm (which is signaled in no way, but the alarm code is sent to the monitoring station). The alarm will be triggered in the partition in which alarm would be triggered in the event of tamper of the keypad/proximity card arm/disarm device used for arming/disarming or alarm clearing.

INT-VG access - the user can operate the control panel by means of a telephone (DTMF), using the interactive voice menu.

# Data comparison

Presented in the window is information on differences between the computer data and those recently read from the alarm control panel.

###### Buttons

Undo change - click to undo the selected change (settings read out from the control panel will be restored).

Undo all changes - click to undo all changes (all settings read out from the control panel will be restored).

Refresh - click to refresh the list of differences. If the window is open, the list of differences will be refreshed automatically every 2 seconds.

Close - click to close the window.

# VERSA Event log

Presented in the window is a list of alarm system events.

No. - number of event in the list.

Date - date of event occurrence.

Time - time of event occurrence.

Event - description of event.

Details - additional information on the event, e.g. name of the partition, zone, user, etc., to which the event refers.

Part. - partition number.

Code - the inner code assigned to an event in the control panel (consistent with the Contact ID format code in case of events which are monitored in this format).

Z/M/U - number of zone, module or user.

S1 S2 - reporting status (S1 - monitoring station 1, S2 - monitoring station 2):

no symbol - the event is not reported.

+ - event successfully reported to the monitoring station.

. - event waiting to be reported to the monitoring station.

! - event not reported yet because of failure of communication with the station (the station does not confirm receiving this information).

Note: If, since the last readout, the number of events has exceeded the capacity of control panel memory, part of the older events will be erased. In such a case, a message about lack of continuity of the event log will be displayed in the window.

-----------------------------------------------

Choose - click to open the Choose window.

Print - click to open the Print window.

Refresh - click to refresh the event log (new events are read).

Colored list - with this field selected, the events will be displayed in color (the colors assigned to various event types are presented in the Choose window).

Font - click to open the Font window, where you can set parameters of the font used for event presentation.

Grade2 events - click to open the Grade2 events window.

Close - click to close the window.

## Choose

The window enables the user to select events which are presented in the VERSA Event log window. The events can be filtered according to the following criteria:

Events type - types of events that are to be displayed (the event types are highlighted in color, if the Colored list field has been selected in the VERSA Event log window).

Range - the range of displayed events can be limited to the selected partition.

Note: If no partition has been selected, events from both partitions will be presented.

From - you can define a date in this field, if events that occurred after this date are to be displayed.

To - you can define a date in this field, if events that occurred before this date are to be displayed.

Only including text - you can define the text that must be included in event description for the event to be displayed.

And including text - you can define the text that, if included in the event description, will cause the event to be displayed next to the events that have been selected by other criteria (event type, range, etc.).

Without including text - you can define the text that, if included in the event description, will cause the event not to be displayed.

###### Buttons

All - click on the button to close the window and display all events in the VERSA Event log window (without taking into account the criteria defined in the Choose window).

Choose - click on the button to close the window and display events in the VERSA Event log window according to the criteria defined in the Choose window.

Cancel - click on the button to cancel the event selection and close the window.

## Print

The window allows you to define parameters of a printout containing the event log.

Printer - in this field, information on the selected printer is displayed.

Events - the field displays information on events to be printed. The printout contains events currently displayed in the VERSA Event log or Grade2 events window.

Printout with reporting status - select this field to include reporting status information in the printout.

Print to text file - with this field selected, the event log will be exported to a text file instead of a printout.

Range - you can define a printout range.

###### Buttons

Properties - click to change a printer.

Print - click to print / export to file the event log.

Cancel - click to close the window.

## Grade2 events

The window displays events required by the EN 50131 standard for Grade 2. The event types are highlighted in color, if the Colored list field has been selected in the VERSA Event log window.

No. - number of event in the list.

Date - date of event occurrence.

Time - time of event occurrence.

Event - description of event.

Details - additional information on the event, e.g. name of the partition, zone, user, etc., to which the event refers.

Part. - partition number.

Code - the inner code assigned to an event in the control panel (consistent with the Contact ID format code in case of events which are monitored in this format).

Z/M/U - number of zone, module or user.

###### Buttons

Print - click to open the Print window.

Refresh - click to refresh the event log (new events are read).

Close - click to close the window.

# System state

Keypad

Partitions state

Zones state

Outputs and modules state

Troubles

Module power supply

Wireless devices

## Keypad

The keypad displayed on screen is a fully functional keypad. It can be used to operate the control panel in the same way as the LCD keypad connected to the control panel.

Note: Operation of the system from the virtual keypad is available when the program is communicating with the control panel.

## VERSA - Partitions state

Presented in the window is information on the status of partitions of the alarm system with which the program is currently communicating. The window data are automatically updated.

## VERSA - Zones state

The window presents information on the status of zones of the alarm system with which the program is currently communicating. The window data are automatically updated.

## Outputs and modules state

The window presents information on the status of outputs and modules of the alarm system with which the program is currently communicating. The window data are automatically updated.

## VERSA - Troubles

The window presents information on the troubles in the alarm system with which the program is currently communicating.

Clear trouble memory - the button is available, if the Trouble memory until review option is enabled in the control panel (see: Options). You can use it to reset the trouble memory.

## Module power supply

The window displays real-time information about the power supply of modules connected to the control panel communication buses.

## VERSA - Wireless devices

The window shows information about communication with the 433 MHz wireless detectors / ABAX system wireless devices.

No. - number of zone or output to which the wireless device is assigned.

Zone name - name of zone to which the wireless device is assigned.

Device type - type of wireless device.

Serial number - serial number of wireless device.

Signal level - level of radio signal received from the wireless device. Presented as a percentage.

Connection quality - quality of the communication with wireless device (expressed as a percentage ratio between the transmissions received and the transmissions expected).

###### Communication diagnostics [only ABAX devices]

Test restart - click to reset information about connection quality and restart analyzing of communication data again.

Testing since - the date from which information about communication with wireless devices are analyzed.

###### Buttons

Close - click to close the window.

# Configuration

Port RS-232

Modem

Data

## Port RS-232

The tab does not apply to the VERSA Plus control panel.

## Modem

Use the tab to define parameters related to modem communication with the control panel.

You can define two sets of parameters for the modem connected to computer, suitable for the communication method:

analog modem for 300 bps transmission,

analog or GSM modem for CSD transmission.

After clicking on the  button you can configure the selected set of parameters (see: Configuring the modem connected to computer).

Dialing - the method of dialing numbers by the modem connected to computer (tone or pulse).

Dial tones control - if option is enabled, the modem connected to computer will detect the dial tone or busy signal before dialing the number.

Speaker - operating mode of the modem speaker. The speaker can be always OFF, or ON until connection with the control panel is established (auto), or always ON.

Volume - volume of modem speaker.

Answering - how the DLOADX program reacts when the control panel is connecting to the program. Communication can be established automatically after a preset number of rings, or the program will only indicate an attempt to establish communication by the control panel (communication will only be established after clicking on the Answer button).

Double call - you can define duration of the pause between the first and the second call, if the control panel is set to go off-hook after the second call.

### Configuring the modem connected to computer

Note: You can edit the parameters after clicking on the Change button.

Port RS-232 - computer COM port to which the modem is connected.

Modem - list of modems, the parameters of which are defined. The list of modems and their settings will be written to disk in the “modem.ini” file.

Baud Rate - transmission rate of the serial port. It is recommended that the highest rate acceptable by the modem be set (only some modems may require the 300 bps setting in order to enforce operation with exactly this speed).

Reset command - the command to reset the modem. Typically, it is the ATZ command (reset with restoration of the user's zero profile). Some modems may require using the AT&F command (reset with restoration of the factory default settings).

Initializing - lines containing the modem initialization commands:

300 bps transmission - in the first line: E0V1Q0 - a command required for proper operation of the modem. You should also add the operating mode selection: B0 or B1 (selection of transmission format: V.21 or Bell103), and the commands limiting transmission rate over telephone line to 300 bps. These are commands specific for the given modem model, e.g. N0S37=3, F1 or +MS=1,0,300,300 etc. Information on how to limit the modem transmission rate is usually included in the device manual. The other line should contain the following commands: S0=0S9=1S7=120S10=255.

CSD transmission - in the first line: E0V1Q0. The command to be entered in the second line depends on the type of modem connected do computer:

analog modem: S0=0S7=120,

GSM modem: S0=0.

###### Buttons

Change - click to edit parameters of the selected modem or add a new modem to the list.

Test - click to test settings. The initialization window will show the initializing commands and the modem answers. The commands sent to the modem will always begin with the AT prefix. The modem acknowledges receiving the command with either OK or ERROR message (if the command is wrong). The MODEM NOT RESPONDING message means a wrongly selected COM port number or too high transmission rate.

OK - click to confirm the changes made and close the window.

Cancel - click to cancel the changes and close the window.

## Data

In this tab, you can specify location of the data catalog on the computer hard disk. The catalog is automatically created when the program is run for the first time.

Note: Changing location of the catalog which already contains some data written to it is not recommended, since it may cause loss of access to those data.

# Connection

Port USB - VERSA Plus

Modem 300bps

VERSA Plus - GSM modem

TCP/IP: DLOADX -> ETHM

TCP/IP: DLOADX <- ETHM/GPRS

TCP/IP: SATEL server

## Port USB - VERSA Plus

If the control panel is to be programmed locally through the USB port, connect the USB port of the control panel with the port of the computer running the DLOADX program. When a prompt asking you whether to connect to the control panel is displayed in the DLOADX program, click Yes. You can establish communication using one of the following methods.

###### Establishing communication with verification of identifiers

Use the keypad to start the local programming function [Start DwnlUSB]:

- Enter the service code and press .

- Press in turn   .

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Establishing communication without verification of identifiers

If no communication identifiers have been programmed in the DLOADX program, use the keypad to enter the service mode:

- Enter the service code and press .

- Press in turn   . The service mode will be started and, additionally, the local programming function will be started [Start DwnlUSB].

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Emergency communication establishing procedure (“from pins”)

If the control panel does not support keypads, does not accept the service code, etc., start the service mode “from pins”.

- Disconnect the cable connecting the control panel USB port with the computer.

- Power off the control panel (disconnect AC mains first, and the battery next).

- Place a jumper across the pins located on the control panel mainboard.

- Power up the control panel (first connect the battery and then the AC power).

- Wait a few seconds and remove the jumper from the pins. The service mode will be started in control panel.

Note: If the Service mode from RESET pins option (Options) is disabled in the control panel then, depending on the type of keypad in which the lowest address is set:

LCD: the ,  and  LEDs of the second partition will be lit, and the message “Restore factory settings ? 1=Yes” will come up on the display,

LED: the  and  LEDs of the second partition will be lit and the  LED will be blinking rapidly.

Pressing the  key will restore the factory default settings of the control panel, thus making it possible to enter the service mode.

- Connect the control panel USB port with the computer port.

- When a window appears with prompt asking you whether you want to connect to the control panel, click Yes.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Finishing local programming

You can finish the local programming function from the keypad by using the FinishDwnlUSB function (enter the service code and press , and then press in turn   ).

The local programming function will be finished automatically 4 hours after communication with the DLOADX program is ended.

## Modem 300bps

The 300 bps modem connection between the DLOADX program and the control panel can be established if:

a modem is connected to computer running the DLOADX program,

telephone line is connected to the analog telephone communicator of the control panel or the GSM communicator of the control panel is running.

Note: The communication identifiers in control panel and program must be identical, or the control panel identifiers must have their factory default value (see: Communication identifiers and establishing connection).

###### Initiating a modem connection from DLOADX program

This method of establishing connection is only possible by means of the analog telephone communicator.

Control panel settings (you can configure them using the keypad or during programming via the USB port):

do not program the telephone number of modem connected to computer!

enable Answering - modem option (Options),

define the number of rings after which the control panel will answer incoming calls (Options),

enable the Double call option if the control panel is to answer only after the second call (Options).

DLOADX program settings:

program the telephone number of control panel (analog communicator) (Connection settings window - you can open it by pressing Ctrl+R),

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click Modem 300bps. Window with modem initialization information will be displayed.

- After modem initialization, click on the Connect button. Information on connection establishment will be displayed.

Note: If the Double call option is enabled in the control panel, select the Double call field before pressing the Connect button.

- When the control panel goes off-hook, the DLOADX program will signal establishing connection by a suitable message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a modem connection from DLOADX program, with control panel calling back and making the call

This method of establishing connection is only possible by means of the analog telephone communicator.

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the telephone number of modem connected do computer - the number for modem communication via the analog telephone communicator (Connection settings),

enable Answering - modem option (Options),

define the number of rings after which the control panel will answer incoming calls - Rings before answer (Options),

enable the Double call option if the control panel is to answer only after the second call (Options),

configure the analog telephone communicator options (Options).

DLOADX program settings:

program the telephone number of control panel (analog communicator) (Connection settings window - you can open it by pressing Ctrl+R),

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click Modem 300bps. Window with modem initialization information will be displayed.

- After modem initialization, click on the Connect button. Information on connection establishment will be displayed.

Note: If the Double call option is enabled in the control panel, select the Double call field before pressing the Connect button.

- The control panel will receive the call, but will hang up. The DLOADX program will inform you that the control panel will call back.

- The control panel will call back the number of computer modem (the number for communication via the analog communicator). The DLOADX program will receive the call automatically or you will have to accept establishing communication (see: Modem). The DLOADX program will signal establishing communication by an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a modem connection by control panel (analog telephone communicator)

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the telephone number of modem connected to computer - the number for modem communication via analog telephone communicator (Connection settings),

configure the analog telephone communicator options (Options).

DLOADX program settings:

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click Modem 300bps. Window with modem initialization information will be displayed.

- Ask the user to start the Start DwnlTEL function (he is supposed to enter the code and press , and then press in turn   ). The control panel will call the computer modem number (the number for communication via analog communicator).

- The DLOADX program will receive the call automatically or you will have to accept establishing communication (see: Modem). The DLOADX program will signal establishing communication by an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a modem connection by control panel (GSM communicator)

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the telephone number of modem connected to computer - the number for modem communication via the GSM communicator (Connection settings),

configure the built-in GSM module (GSM).

DLOADX program settings:

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click Modem 300bps. Window with modem initialization information will be displayed.

- Ask the user to start the GSM audio function (he is supposed to enter the code and press , and then press in turn    ). The control panel will call the computer modem number (the number for communication via GSM communicator).

- The DLOADX program will receive the call automatically or you will have to accept establishing communication (see: Modem). The DLOADX program will signal establishing communication by an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

## VERSA Plus - GSM modem

The CSD (9600 bps) modem connection between the DLOADX program and the control panel can be established if:

a modem is connected to the computer running the DLOADX program,

the control panel GSM communicator is running.

Note: The communication identifiers in control panel and program must be identical, or the control panel identifiers must have their factory default value (see: Communication identifiers and establishing connection).

###### Initiating a modem connection from DLOADX program

Control panel settings (you can configure them using the keypad or during programming via the USB port):

do not program the telephone number of modem connected to computer!

enable Answering - modem option (Options),

configure the built-in GSM module (GSM).

DLOADX program settings:

program the telephone number of control panel (built-in GSM module) (Connection settings window - you can open it by pressing Ctrl+R),

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click VERSA Plus - GSM modem. Window with modem initialization information will be displayed.

- After modem initialization, click on the Connect button. Information on connection establishment will be displayed.

- When the control panel goes off-hook, the DLOADX program will signal establishing connection by a suitable message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a modem connection from DLOADX program, with control panel calling back and making the call

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the telephone number of modem connected to computer - the number for modem communication via the GSM communicator (Connection settings),

enable Answering - modem option (Options),

configure the built-in GSM module (GSM).

DLOADX program settings:

program the telephone number of control panel (built-in GSM module) (Connection settings window - you can open it by pressing Ctrl+R),

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click VERSA Plus - GSM modem. Window with modem initialization information will be displayed.

- After modem initialization, click on the Connect button. Information on connection establishment will be displayed.

- The control panel will receive the call, but will hang up. The DLOADX program will inform you that the control panel will call back.

- The control panel will call back the number of computer modem (the number for communication via GSM communicator). The DLOADX program will receive the call automatically or you will have to accept establishing communication (see: Modem). The DLOADX program will signal establishing communication by an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a modem connection by control panel

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the telephone number of modem connected to computer - the number for modem communication via the GSM communicator (Connection settings),

configure the built-in GSM module (GSM).

DLOADX program settings:

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click VERSA Plus - GSM modem. Window with modem initialization information will be displayed.

- Ask the user to start the GSM CSD function (he is supposed to enter the code and press , and then press in turn    ). The control panel will call the computer modem number (the number for communication via GSM communicator).

- The DLOADX program will receive the call automatically or you will have to accept establishing communication (see: Modem). The DLOADX program will signal establishing communication by an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a modem connection by using SMS message

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the telephone number of modem connected to computer - the number for modem communication via the GSM communicator (Connection settings),

program the control command that will be sent in the SMS message to initiate communication between control panel and DLOADX program (VERSA-ETH),

configure the built-in GSM module (GSM).

DLOADX program settings:

configure the modem communication parameters (Modem tab in the Configuration window).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click VERSA Plus - GSM modem. Window with modem initialization information will be displayed.

- Send to the phone number of built-in GSM module the following SMS message:

xxxx=csd= (“xxxx” - control command to initiate establishing communication with DLOADX program) - the control panel is to call the phone number of modem connected to computer, as programmed in the control panel (Connection settings),

xxxx=csd:nnnn= (“xxxx” - control command to initiate establishing communication with DLOADX program; “nnnn” - phone number of modem connected to computer) - the control panel is to call the phone number given in the SMS message.

Note: The SMS message can be sent from the telephone whose number and user are included in the table available when configuring the built-in GSM module (GSM).

- Having received the SMS message, the control panel will call the indicated number of computer modem.

- The DLOADX program will receive the call automatically or you will have to accept establishing communication (see: Modem). The DLOADX program will signal establishing communication by an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

## TCP/IP: DLOADX -> ETHM

The DLOADX program can establish connection with the control panel via the Ethernet network, if:

the computer running the DLOADX program is connected to the network,

the built-in Ethernet module of the control panel is connected to the network.

Note: The communication identifiers in control panel and program must be identical, or the control panel identifiers must have their factory default value (see: Communication identifiers and establishing connection).

Control panel settings (you can configure them using the keypad or during programming via the USB port):

enable DLOADX->VERSA-ETHM connection option (ETHM),

program the number of TCP port which will be used for communication and the data encryption key (VERSA-ETH),

configure the Ethernet communication module (ETHM).

DLOADX program settings (Connection settings window - you can open it by pressing Ctrl+R):

program the control panel address,

program the number of TCP port which will be used for communication and the data encryption key (or select the “LAN: VERSA-ETH” parameter set - the data programmed in settings of built-in communication modules will be used).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click TCP/IP: DLOADX -> ETHM (if you have programmed both sets of parameters for communication via the Ethernet network, when you hover mouse over TCP/IP: DloadX -> ETHM, you can select LAN/WAN or LAN). The Connection TCP/IP: DLOADX -> ETHM-1 window will be displayed.

- Click on the Connect button in the Connection TCP/IP: DLOADX -> ETHM-1 window. Connection establishment information will be displayed.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

## TCP/IP: DLOADX <- ETHM/GPRS

The control panel can establish connection with the DLOADX program via the Ethernet/GPRS network, if:

the computer running the DLOADX program is connected to the network,

the control panel built-in Ethernet module is connected to the network / the control panel GSM communicator is running.

Note: The communication identifiers in control panel and program must be identical, or the control panel identifiers must have their factory default value (see: Communication identifiers and establishing connection).

###### Initiating an Ethernet connection by the control panel

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the address of the computer with DLOADX program, the number of TCP port which will be used for communication and the data encryption key (VERSA-ETH),

configure the Ethernet communication module (ETHM).

DLOADX program settings (Connection settings window - you can open it by pressing Ctrl+R):

program the number of TCP port which will be used for communication and the data encryption key (or select the “LAN: VERSA-ETH” parameter set - the data programmed in settings of built-in communication modules will be used).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click TCP/IP: DLOADX <- ETHM/GPRS. The Connection TCP/IP: DLOADX <- ETHM-1 window will be displayed.

- Ask the user to start the function ETHM-1-> DLOADX (he is supposed to enter the code and press , and then press in turn   ). The control panel will connect to the computer network address.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating an Ethernet connection by using SMS message

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the address of the computer with DLOADX program, the number of TCP port which will be used for communication and the data encryption key (VERSA-ETH),

program control command that will be sent in the SMS message to initiate communication between control panel a DLOADX program (VERSA-ETH),

configure the Ethernet communication module (ETHM).

DLOADX program settings (Connection settings window - you can open it by pressing Ctrl+R):

program the number of TCP port which will be used for communication and the data encryption key (or select the “LAN: VERSA-ETH” parameter set - the data programmed in settings of built-in communication modules will be used).

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click TCP/IP: DLOADX <- ETHM/GPRS. The Connection TCP/IP: DLOADX <- ETHM-1 window will be displayed.

- Send to the phone number of built-in GSM module the following SMS message:

xxxx=ethm= (“xxxx” - control command to initiate establishment of communication with DLOADX program) - the control panel is to connect to the computer address programmed in control panel,

xxxx=ethm:aaaa:p= (“xxxx” - control command to initiate establishment of communication with DLOADX program; “aaaa” - address of the computer with DLOADX program; “p” -TCP port) - the control panel is to connect to the address given in SMS message and use the TCP port given in SMS message for communication.

Note: The SMS message can be sent from the telephone whose number and user are included in the table available when configuring the built-in GSM module (GSM).

- Having received the SMS message, the control panel will connect to the indicated network address.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a GPRS connection by the control panel

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the address of the computer with DLOADX program, the number of TCP port which will be used for communication and the data encryption key (VERSA-ETH),

configure the built-in GSM module (GSM).

DLOADX program settings (Connection settings window - you can open it by pressing Ctrl+R):

program the number of TCP port which will be used for communication and the data encryption key.

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click TCP/IP: DLOADX <- ETHM/GPRS. The Connection TCP/IP: DLOADX <- ETHM-1 window will be displayed.

- Ask the user to start the GPRS->DLOADX function (he is supposed to enter the code and press , and then press in turn   ). Control panel will connect to the computer network address.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

###### Initiating a GPRS connection by using SMS message

Control panel settings (you can configure them using the keypad or during programming via the USB port):

program the address of the computer with DLOADX program, the number of TCP port which will be used for communication and the data encryption key (VERSA-ETH),

program the control command that will be sent in the SMS message to initiate communication between control panel and DLOADX program (VERSA-ETH),

configure the built-in GSM module (GSM).

DLOADX program settings (Connection settings window - you can open it by pressing Ctrl+R):

program the number of TCP port which will be used for communication and the data encryption key.

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click TCP/IP: DLOADX <- ETHM/GPRS. The Connection TCP/IP: DLOADX <- ETHM-1 window will be displayed.

- Send to the phone number of built-in GSM module the following SMS message:

xxxx=gprs= (“xxxx” - control command to initiate establishment of communication with DLOADX program) - the control panel is to connect to the computer address programmed in control panel,

xxxx=gprs:aaaa:p= (“xxxx” - control command to initiate establishment of communication with DLOADX program; “aaaa” - address of the computer with DLOADX program; “p” - TCP port) - the control panel is to connect to the address given in SMS message and use the TCP port indicated in SMS message for communication.

Note: The SMS message can be sent from the telephone whose number and user are included in the table available when configuring the built-in GSM module (GSM).

- Having received the SMS message, the control panel will connect to the indicated network address.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

## TCP/IP: SATEL server

Connection between the DLOADX program and the control panel via the SATEL server can be established, if:

the computer running the DLOADX program is connected to the network,

the control panel built-in Ethernet module is connected to the network.

Note: The communication identifiers in control panel and program must be identical, or the control panel identifiers must have their factory default value (see: Communication identifiers and establishing connection).

Control panel settings (you can configure them using the keypad or during programming via the USB port):

enable DLOADX->VERSA-ETHM connection and Satel server (LAN) options (ETHM),

program the data encryption key (VERSA-ETH).

DLOADX program settings (Connection settings window - you can open it by pressing Ctrl+R):

enter the individual identification number of the control panel for the purpose of communication via the SATEL server,

enter the MAC address of built-in Ethernet module,

program the data encryption key.

- Click on the  button in DLOADX program main menu. A drop down menu will be displayed.

- Click TCP/IP: Satel server. The Connection TCP/IP: DLOADX <-> ETHM-1 window will be displayed.

- Click on the Connect button in the Connection TCP/IP: DLOADX <-> ETHM-1 window. Connection establishment information will be displayed.

- The DLOADX program will signal establishing communication by displaying an appropriate message. The message contents depends on whether the program has been connected to a new alarm system, or a system whose data have already been saved (see: Communication identifiers and establishing connection).

## Communication identifiers and establishing connection

###### Establishing communication with a new alarm system

If the factory default identifiers are programmed in the control panel, the program will inform that communication has been established with a new alarm system. A window will be displayed in which you will be able to give a name to the new system, and in which the program will suggest randomly generated identifiers instead of the factory default ones. The identifiers can be freely changed. After closing the window, the program will read all data from the control panel and write the new communication identifiers to the control panel. If the system data are written to the computer hard disk, the program will identify the control panel and choose a data file to match it.

###### Establishing communication with a system whose data are in the computer

If, based on the communication identifiers, the program determines that the alarm system data are written to the computer, it will suggest opening the file that contains those data.

###### Establishing communication with a system whose data are not in the computer

If, based on the communication identifiers, the program determines that the alarm system data are not written to the computer, while they are not also the factory default identifiers, establishing communication will only be possible after identifiers consistent with those programmed in the control panel are programmed in the Connection settings window (available in the drop-down menu after you click on the Communication command in the main menu). You can check the identifiers in the control panel by means of the LCD keypad (Service mode >0. SrvMod config).

# Connection settings

###### PC - DLOADX

DLOADX identifier - identifier of the computer with DLOADX program. It consists of 8 characters (digits or letters from A to F). It enables the control panel to recognize the computer with DLOADX program. The control panel will only establish connection with the program which uses the valid identifier. Click  to see the sequence of characters.

PC phone number - telephone number of the modem connected to computer with DLOADX program installed. The number for modem communication via the built-in analog telephone communicator.

Phone number for GSM - telephone number of the modem connected to computer with DLOADX program installed. The number for modem communication via the built-in GSM communicator.

###### VERSA

VERSA identifier - identifier of the alarm control panel. It consists of 8 characters (digits or letters from A to F). It enables the DLOADX program to recognize the control panel and match the data file to it, provided the data file has been written to the computer. Do not program the same identifier for different control panels which are operated from the same computer (the DLOADX program will be incapable of distinguishing between them). Click  to see the sequence of characters.

Note: In case of establishing communication with the alarm system whose identifier have factory defaults, the DLOADX program will suggest random generated identifier.

Panel’s tel. no - telephone number of the control panel.

###### TCP/IP connection: DLOADX -> ETHM

Connection - you can define two sets of parameters:

LAN/WAN - parameters for communication via local or wide network.

LAN: VERSA-ETH - parameters for communication via local network only. In this case, the port number and data encryption key programmed in the settings of built-in communication modules will be used during communication.

Server - address of the control panel. If the control panel is not in the same local network as the computer with DLOADX program, it must be a public address. You can enter either the IP address or the domain name.

Port - the number of TCP port used for communication between the control panel and computer with DLOADX program via Ethernet / GPRS. You can enter a value from 1 to 65535. Default value: 7090.

DLOADX key - a string of up to 12 alphanumeric characters (digits, letters and special characters), used for data encryption during communication between the control panel and the computer with DLOADX program via Ethernet / GPRS. Click  to see the sequence of characters.

###### Satel server

ETHM-1 ID - individual identification number of the control panel for the purpose of communication via the SATEL server. Click  to see the sequence of characters.

ETHM-1 MAC - hardware address of built-in Ethernet module. Click  to see the sequence of characters.

# Programming telephone numbers

When programming a telephone number, you can use all the characters defined in the DTMF standard, i.e. digits from 0 to 9 and special characters:

B - switch-over to pulse dialing;

C - switch-over to tone dialing (DTMF);

D - waiting for additional signal;

E - 3 second pause;

F - 10 second pause;

* - signal * in DTMF mode;

# - signal # in DTMF mode;

a, b, c, d - other signals generated in DTMF mode.

Note: Do not overuse the control characters. They are only to be used when necessary. There is no need for putting them at the beginning, before the telephone number digits. The basic method of dialing, appropriate pause and awaiting the dial tone before dialing are set in the telephone options (see: Options).

# Changing the DLOADX program access code

- Click on File >Access setup >Change access code. Dialog window with a field for entering the code will be displayed.

- Enter the old access code to the program and click OK. Another dialog window with a field for entering the code will be displayed.

- Enter the new access code to the program and click OK. Another dialog window with a field for entering the code will be displayed.

- Re-enter the new access code to the program and click OK. A dialog window will be displayed with a message that the code has been changed.

- Click OK to close the window and finish the procedure.