Radio signal level tester

Quick guide

abax2_tester_en 09/20

Full manuals are available on www.satel.eu

Changes, modifications or repairs not authorized by the manufacturer shall void your rights under the warranty.

The ARF-200 tester allows you to check the level of radio signal received and transmitted by ABAX 2 system wireless devices. It also allows you to check the level of radio noise in the frequency band used by ABAX 2 devices. For how to add the tester to the system, refer to the ABAX 2 system controller manual.

Buttons:

–	switches the tester ON / OFF.

–	changes the tester operating mode.

–	used to check the level of radio noise in the system channels / change how frequently the tester communicates with the controller (change the refresh rate of the tester indicator).

The tester indicator consists of 7 LEDs which are used to present information.

The tester is powered from the rechargeable battery. If the battery needs charging, all the indicator LEDs are flashing. In order to charge the battery, connect the charger to the type-B micro-USB port. You can use the port to connect the tester to the computer (for tester firmware update / battery charging).

When the battery is fully charged, disconnect the charger from the power supply.

Charger and USB cable are not included with the tester.

If not used, the tester will switch off automatically after 10 minutes.

For more information about the tester, refer to the full manual.

Hereby, SATEL sp. z o.o. declares that the radio equipment type ARF-200 is in compliance with Directive 2014/53/EU. The full text of the EU declaration of conformity is available at the following internet address: www.satel.eu/ce

SATEL sp. z o.o. • ul. Budowlanych 66 • 80-298 Gdańsk • POLAND

tel. +48 58 320 94 00

www.satel.eu

druk (2 na 1):

1,1