AMD-100

amd100_int 02/11

WIRELESS MAGNETIC CONTACT

# General

The AMD-100 detector is designed for operation within the ABAX two-way wireless system. This manual applies to the device with electronics version 3.5 J or later which is supported by the ACU-100 controller with firmware version 1.06 or later and by the INTEGRA 128-WRL control panel.

Two reed switches are used in the device and you can program by radio which of them is to be active.

The LED is only functioning in the test mode:

it is lit up for 80 milliseconds, when being polled;

it is lit up for 2 seconds in the event of alarm (opening of reed switch contacts after magnet is moved away, opening of additional input) or tamper (opening of tamper contact).

FIGURE 1. View of detector electronics board.

1	-	additional input terminals. An NC type hardwired detector can be connected to the input or else the terminals must be shorted. The input is connected in series with reed switches.

2	-	tamper contact, which opens when the cover is removed or the unit is removed from its mounting surface.

3	-	CR123A 3 V lithium battery, ensuring operation for approx. 3-year period. The detector controls the battery status. When the voltage drops to 2.6 V, the "low battery" information is sent to the controller. The low battery signaling continues until the battery is replaced.

4	-	location of the side reed switch (mounted on the other side of the electronics board).

5	-	location of the bottom reed switch (mounted on the other side of the electronics board).

FIGURE 2. Example of magnetic contact installation.

# Specifications

Operating frequency band	868.0 MHz ÷ 868.6 MHz

Radio communication range (in open area)	up to 150 m

Battery	lithium battery CR123A 3 V

Battery life expectancy	approx. 3 years

Additional input sensitivity	312 ms

Standby current consumption	50 µA

Maximum current consumption	16 mA

Security grade according to EN50131-2-6	Grade 2

Environmental class according to EN50130-5	II

Operating temperature range	-10°C...+55°C

Maximum humidity	933%

Complied with standards	EN 50130-4, EN 50130-5, EN 50131-1, EN 50131-2-6, EN 50131-5-3

Enclosure dimensions	24 x 110 x 27 mm

Weight	56 g

Hereby, SATEL sp. z o.o., declares that this detector is in compliance with the essential requirements and other relevant provisions of Directive 1999/5/EC. The declaration of conformity may be consulted at www.satel.eu/ce

# Installation

The battery should be mounted just before registering the detector into the ABAX system.

Be particularly careful during installation so as not to make damage to the reed switches on the electronics board.

Be particularly careful when replacing the battery. If inappropriately done, replacement of the battery may lead to a risk of explosion. The Manufacturer bears no responsibility for any consequences of incorrect replacement of the battery.

The used batteries must not be discarded, but should be disposed of in accordance with the existing rules for environment protection.

The magnetic contact is designed for indoor installation. The detector should be mounted on a fixed surface (e.g. window or door frame), and the magnet on a movable surface (e.g. window or door). Mounting the magnetic contact on ferromagnetic surfaces and/or near to strong magnetic and electrical fields is not advisable, because it can result in malfunctioning of the device.

- Open the enclosure.

- Install the battery and add the device to the wireless system (see the ACU-100 controller manual, INTEGRA 128-WRL or VERSA control panel installer manual).

- Fasten the detector temporarily at the place of its future installation.

- Check the level of signal received from the detector by the ACU-100 controller or by the INTEGRA 128-WRL control panel. If necessary, select another place for installation, to ensure adequate communication quality.

- If a detector is to be connected to the additional input terminals, make a hole in the enclosure base, run the wires through the hole and fasten them to screw terminals. The maximum permissible length of wires: 3 m.

- Fasten the enclosure base to the mounting surface.

- Close the magnetic contact enclosure.

- Secure the magnet, taking into account the maximum permissible distance from the reed switch (see Fig. 4).

- Determine, which reed switch is to be active (see: manual for ACU-100 controller or programming manual for INTEGRA or VERSA control panels).

- Enter the test mode and check whether the LED lights up after moving the magnet away (i.e. opening a window or door). If the additional input is used, make sure that violation of the detector connected to it will cause the LED to light up.

- Exit the test mode. The magnetic contact is now ready for work.

FIGURE 3. Dimensions of enclosure and location of reed switches. 1 – bottom reed switch. 2 – side reed switch.

FIGURE 4. Maximum ranges of the reed switches (magnet located at the height of magnetic contact electronics board).

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl