AQUA Luna

aqua_luna_int 08/11

DIGITAL PASSIVE INFRARED DETECTOR WITH LIGHTING FEATURE

# Features

Dual element pyrosensor.

Fully digital motion detection algorithm.

Two-way pyrosensor signal analysis, based on value and quantity.

Pre-alarm feature.

Digital temperature compensation.

Set of LEDs to perform the lighting function.

Remote switching of lighting.

Low supply voltage signaling (voltage drop below 9 V ±5%).

# Electronics board

FIGURE 1. View of detector electronics board.

1	-	terminals:

NC	-	relay (NC)

TMP	-	tamper contact

COM	-	common ground

12V	-	supply input

2	-	terminals to connect the lighting control signal. A control panel output, e.g. preprogrammed as MONO switch, can be used for the control (activated for a preset time period, e.g. after detector violation). If an OC type output is used, connect it to the “–” terminal (and +12 V voltage to the “+” terminal). If a high-current output is used, connect it to the “+” terminal (and common ground to the “–” terminal).

3	-	red color LED to indicate:

- prealarm – short flash (approx. 120 ms);

- alarm – ON for 2 seconds;

- warm-up – blinking rapidly;

- low supply voltage – ON.

4	-	socket for connection of LEDs to provide lighting feature.

5	-	pyroelectric sensor.

6	-	tamper contact.

7	-	scale for positioning of pyroelectric sensor against the lens (see: Fig. 7).

8	-	fixing screw hole.

9	-	detector configuration pins:

PIR SENS.	-	setting detector sensitivity (see Fig. 2);

LED ON/OFF	-	enabling/disabling the LED signaling. The signaling is enabled when the pins are shorted.

FIGURE 2. Setting the detector sensitivity (A – low sensitivity, B and C – medium sensitivity, D – high sensitivity) [ – pins shorted;  – pins open].

# Coverage area

FIGURE 3. Coverage area of a detector with EWA type lens.

The EWA lens, mounted in the detector as standard, can be optionally replaced with:

LR – long range array: range 30 m; main beam 3 m wide at the end of range; or

VB – vertical barrier array: range 22.5 m; beam 2.2 m wide at the end of range.

# Installation

- Open the enclosure (Fig. 4) and disconnect the LED lighting from its socket on electronics board.

- Remove the electronics board.

- Make the openings for screws and cable in the enclosure base.

- Pass the cable through the prepared opening.

- Fix the enclosure base to the wall or to the attached bracket (Fig. 5).

- Fasten the electronics board, taking into consideration the height of detector installation (Fig. 7).

- Connect the wires to the corresponding terminals.

- Using jumpers, set the working parameters of the detector.

- Connect the LED lighting to its socket on electronics board and close the detector enclosure.

FIGURE 4. Removing the cover.

FIGURE 5. Ways of installing the detector.

FIGURE 6. Mounting the detector on the bracket.

Note:	For compliance with the requirements of EN50131-2-2, the detector shall be installed directly on the mounting surface, without the additional bracket.

FIGURE 7. The way of positioning the electronics board to optimize the coverage area. Depending on the mounting height, the medium scale line should be: aligned with the mark on the enclosure (installation at a height of 2.4 m), situated above the mark (installation higher than 2.4 m – example B) or below the mark (installation lower than 2.4 m – example D).

# Start-up

- Switch the detector power on. The LED will start blinking (if the LED ON/OFF pins are shorted).

- When the detector is ready to work (the LED will stop blinking), carry out the detector range test, i.e. check that movement within the coverage area will activate the alarm relay and lighting of the LED.

- If necessary, change the detector sensitivity (pins PIR SENS.).

# Specifications

Supply voltage	12 V DC 15%

Standby detector current consumption	10 mA

Maximum detector current consumption	12 mA

Maximum current consumption by lighting	28 mA

Relay contacts rating (resistive load)	40 mA / 16 V DC

Alarm signaling time	2 s

Detectable speed	0.3...3 m/s

Standards complied with	EN50130-5, EN50131-1, EN50131-2-2, EN50130-4

Security grade according to EN50131-2-2	Grade 2

Environmental class according to EN50130-5	II

Operating temperature range	-30...+55 °C

Dimensions	63 x 96 x 49 mm

Recommended installation height	2.4 m

Weight	92 g

The declaration of conformity may be consulted at www.satel.eu/ce

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl