|  | CABLE SET FOR PROGRAMMING DEVICES WITH RS-232 TTL PORT DB9FC/RJ-KPL |
| --- | --- |

db9fcrj_en 08/08

The DB9FC/RJ-KPL cable set includes the DB9FC/RJ main cable, RJ/PIN3 adapter, PIN3/RX adapter and connector with two RJ (6-pin) sockets. The first two cables are marked by yellow cable flag labels with suitable symbol printed on them.

This set replaces the two cables manufactured earlier under the name of DB9FC/PIN3 (or RS-CA5/6/R-2/4) and DB9FC/RJ. It enables computer to be connected to devices with RS-232 TTL port, irrespective of what type of socket is used in them (PIN3 or RJ).

The DB9FC/RJ cable has a built-in data converter from RS-232 (-12V, +12V) into RS-232 TTL (0V, +5V) standard.

The set is designed for use with the following devices:

- CA-6, CA-5 alarm control panels (all electronics board versions);

- RX-2K, RX-4K, RE-4K radio controllers;

- INT-RX 433MHz keyfobs receiver expansion module

- ACCO-KP, ACCO-KP-PS access control modules.

Note:	The cables designated DB9FC/RJ, manufactured up to 2007 (including 2007) and sold individually (without adapters), do not allow programming the CA-5, CA-6 control panels with PIN3 socket, as well as the radio controllers (even when using the adapters described herein).

The figures below show connection diagrams.

Figure 1. Connection diagram – DB9FC/RJ cable

Figure 2. Connection diagram – RJ/PIN3 adapter

Figure 3. View of PIN3/RX adapter (for programming radio controllers)

Figure 4. Method of making cable connections

| The latest EC declaration of conformity and product approval certificates are available for downloading on website www.satel.pl |  |
| --- | --- |

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl

druk:

2,1,2,1

# Text boxes

to computer

to control panel

DB9F

to radio controller

to RJ/PIN3 adapter

2xRJ connector

1

1

2

3

4

5

654321

(view of RJ plug )

(view of converter board located in DB9F female connector)

cable

adapter

DB9FC/RJ

1

RJ/PIN3

device with 
PIN3 type socket

COMPUTER

COM (black)

LV (white)

AL (green)

3  2  1

view of RJ plug

654

view of PIN-3 plug

3  2  1

to RJ connector

to device with PIN3 socket