|  | CABLE SET FOR PROGRAMMING DEVICES WITH RS-232 PORT DB9F/RJ-KPL |
| --- | --- |

db9frj_en 08/08

The DB9F/RJ-KPL cable set includes the DB9F/RJ main cable, RJ/PIN5-LCD adapter and connector with two RJ (6-pin) sockets. Both cables are marked by green cable flag labels with suitable symbol printed on them.

This set replaces the two cables manufactured earlier under the name of DB9F/PIN5 (or RS-CA64/CA10) and DB9F/RJ. It enables computer to be connected to devices with RS-232, port, irrespective of what type of socket is used in them (PIN-5 or RJ).

The set is designed for use with the following devices:

- INTEGRA, CA-64, CA-10 alarm control panels ;

- LCD keypads for INTEGRA, CA-64 and CA-10 control panels ;

- GSM-4S, GSM LT-2S, GSM LT-1S communication modules;

- ACU-100 controller for ABAX wireless system.

The figures below show connection diagrams.

Figure 1. Connection diagram – DB9F/RJ cable

Figure 2. Connection diagram – RJ/PIN5-LCD adapter

Figure 3. Method of making cable connections

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl

druk:

2,1,2,1

# Text boxes

TO COMPUTER

TO CONTROL PANEL

DB9F

5

4

8

3

2

6543 1

(view of RJ plug )

(view of DB9F female plug from the side of soldering points )

to device with PIN5 socket

to RJ connector

5    4     3    2    1

6543 1

(view of PIN-5 plug)

(view of RJ plug )

COMPUTER

2xRJ connector

DB9F/RJ

adapter

RJ/PIN5-LCD

device with 
PIN5 type socket

1

1

cable