CHANGES MADE TO INTEGRA CONTROL PANEL FIRMWARE VERSION 1.10

errata_integra_en 12/11

# LCD keypads

Recommended version of the keypad, if the system is to meet the EN 50131 standard requirements for Grade 2:

INT-KLCD / INT-KLCDR – 1.08 or newer;

INT-KLCDK / INT-KLCDL / INT-KLCDS – 6.08 or newer;

INT-KSG – 1.01 or newer.

New option:

Show arm messages – after arming the system, armed mode messages can be displayed on the keypad display. The messages will be displayed regardless of how the system has been armed.

# Expansion modules

Partition keypads (INT-S, INT-SK), multifunctional keypad with proximity card reader (INT-SCR) and readers connected to reader expanders (INT-R, CA-64 SR, CA-64 DR) can be used by users with the Access to cash dispenser type of code.

Code locks (INT-SZ, INT-SZK) allow you to:

activate the 24. MONO switch type outputs, using the MONO outputs type of code;

change the status of 25. BI switch type outputs, using the BI outputs type of code;

temporarily block the partition to which the expander is assigned, using the Temporary partition blocking type of code (partition can only be blocked when armed).

Support for new modules:

INT-KNX – KNX integration module.

INT-VG – voice module.

# ABAX wireless system

Support for new wireless devices:

AMD-103 – wireless magnetic contact;

ASD-110 – wireless smoke and heat detector.

# System options

New options have been added:

Grade 2 – the system operates as required by the EN 50131 standard for Grade 2, i.e.:

starting the arming procedure may be impossible, or, if started, the arming procedure may fail, if some zones are violated in the partition, or there is a trouble in the system;

LCD keypads, partition keypads, proximity card arm/disarm devices and reader expanders do not signal alarms;

the  LEDs in keypads indicate alarms only when code has been entered and confirmed with the [*] key;

the blinking  LED in keypads means that there is a trouble in the system, some zones are bypassed, or there has been an alarm;

new access codes in the system must be composed of at least 5 characters (User code min. length parameter);

the following global options have been enabled (cannot be disabled):

Trouble memory until review;

Do not show alarm if armed;

Block keypad after 3 wrong codes;

Warn while arming if trouble;

Display violated/bypassed zones on arming;

the following global options have been disabled (cannot be enabled):

Do not arm if tampered;

Do not arm if battery trouble;

Required system reset after verified alarm;

Do not arm if trouble;

Do not arm if outputs trouble;

Do not arm if reporting trouble;

the Always loud tamper alarm option has been disabled for all zones, keypad and expander buses (the option cannot be enabled);

the Valid within 60 sec option has been enabled for all partitions (cannot be disabled);

the entry delay time (global and for individual zones) can be up to 45 seconds (if longer, it will be automatically reduced);

the Reporting delay option will be enabled for the 4. Perimeter, 5. Instant, 6. Exit, 7. Day/Night and 64...79 Bypassing – group: 1...16 zone types (the option cannot be disabled);

the Abort delay option will be enabled for the 0. Entry/Exit, 1. Entry, 2. Delayed with delay signaling, 3. Interior delayed, 85. Entry/Exit - conditional and 86. Entry/Exit - final zone types (the option cannot be disabled);

the Auto-reset 3 and Auto-reset 1 options will be disabled for the 12. Panic audible and 13. Panic silent zone types (the options cannot be enabled);

AC loss report delay (for the control panel and all modules with power supply units) can be up to 60 minutes (if longer, it will be automatically reduced);

the quick arming is not possible (relevant parameters in keypad settings are automatically modified);

the Show arm messages option has been enabled in all keypads (it cannot be disabled);

the following options have been disabled in all keypads (they cannot be enabled):

Signaling troubles in partially arm;

Signal new trouble;

Alarm messages: Partitions;

Alarm messages: Zones;

Show violated zones;

Display mode switching;

it is not possible to view the status of zones, partitions, alarms, trouble memory and current troubles by pressing and holding down the dedicated keypad keys (the corresponding options are disabled and cannot be enabled);

it is not possible to present information on partition status in the bottom line of keypad display (relevant parameters in the keypad settings will be automatically modified);

after entering the user menu by means of the service code, you will get access in the Events submenu to the Grade 2 function, which enables viewing the events required by EN 50131 for Grade 2;

the System state user function provides information about alarms, bypassed zones, troubles and partition status (disarmed or type of armed mode).

Answering – ETHM/GSM – if enabled, it is possible to initiate communication with the alarm control panel from outside, by means of the ETHM-1 or GSM module. The option is not available, when the Answering - modem option is enabled.

The options Do not arm if tampered, Do not arm if battery trouble, Do not arm if trouble, Do not arm if outputs trouble and Do not arm if reporting trouble are available, when the Warn while arming if trouble option is enabled.

# Partitions

The Arming control time will no longer be programmed for the partition for which the Infinite exit delay option is enabled, because this time duration will always be 260 seconds. Unless the partition is armed before 260 seconds have elapsed, the "Arming failed" event will be recorded into the control panel memory.

For the partition for which the Infinite exit delay option is enabled, you can program the Partition exit delay. This time will be taken into account, if the partition is armed by means of a zone or timer.

# Zones

A new zone type has been added:

Outputs group off – the zone allows you to deactivate a selected group of outputs.

# Outputs

The 23. Arm/Disarm Acknowledge output type indicates additionally the inability to start arming procedure and the failure of started arming procedure (7 pulses).

# Reporting

The control panel will send an event code to inform about arming failure, when the arming procedure has been terminated because of occurrence of some circumstances that prevent the arming. A suitable event code must be programmed for pulse and Ademco Express formats.

# Messaging

The control panel can notify about arming failure (when the arming procedure has been terminated because of occurrence of some circumstances that prevent the arming).

# Event log

A separate event log is allocated to store events required by the EN 50131 standard for Grade 2.

# Timers

The number of timers in the INTEGRA 32 control panel has been reduced to 28.

# Alarms

A warning alarm has been introduced, whose function is to delay the audible alarm and reporting in case of any errors made when entering the protected premises. It is triggered by the zones with enabled Reporting delay option which will be violated during the entry delay countdown. The warning alarm will be signaled by the 9. DAY alarm, 12. Silent alarm and 116. Internal siren output types.

# User functions

The Troubles user function name has been changed to System state.

The Temperatures function has been added to the Tests submenu to check the temperature measured by the ATD-100 wireless temperature detectors.

druk (2 na 1):

4,1,2,3