CHANGES MADE TO INTEGRA CONTROL PANEL FIRMWARE VERSION 1.09

errata_integra_en 05/11

# LCD keypads

The way of blocking CHIME signals in keypads has been modified: the blocking period is counted from the zone restore.

# Wireless devices

The control panels support the ATD-100 wireless temperature detector.

In case of some wireless devices it is possible to select whether the device will take one or two places (channels) on the list of devices. Depending on the device, if you select one channel:

AMD-102 – only additional inputs (roller shutter and NC) will be supported;

ATD-100 – it will only be possible to preset one temperature threshold;

AVD-100 – only vibration detector will be supported.

Selection of the number of places (channels) is performed during the device adding procedure. The selection is possible in case of INTEGRA 128-WRL control panel and ACU-100 controllers with firmware version 3.0 or newer.

# GSM telephone only INTEGRA 128-WRL

New parameter has been added:

GSM auto-restart after – duration of the GSM telephone idle state after which it will be restarted. Defined in hours.

# System options

New parameter has been added:

Default partition block time – the time period during which the With temporary block type partitions with enabled Default block time option will be blocked.

# Partitions

New type of partition has been added:

Bank vault – the partition can be armed / disarmed by the user. Disarming may be delayed by a defined period of time (Disarm delay). After it has been disarmed, the partition can be automatically re-armed after a defined period of time elapses (Time to re-arm).

New parameters relating to the Bank vault type of partition have been added:

Disarm delay – the partition will only be disarmed after a defined period of time has elapsed since the code (proximity card, DALLAS chip, etc.) was used by the user. If the time is equal to 0, the partition will be disarmed immediately.

Time to re-arm – after disarming, the control panel will be analyzing for a defined period of time whether a door in the partition will be opened by means of an access control module (partition keypad, code lock, etc.). If the door is not opened, the partition will be automatically re-armed (the partition exit delay countdown will not be running). If the time value is equal to 0, the partition will not be re-armed. Irrespective of the preset value, if the Disarm delay parameter is 0, the partition will not be re-armed.

New options relating to the With temporary block type partition have been added:

Default block time – if the option is enabled and the Default partition block time is preset, the partition will be blocked on arming for a default time period, as defined by the installer (the blocking time cannot be programmed by the user).

Alarm – disarm allowed – if the option is enabled, the partition can be disarmed in case of alarm by the users who do not have the Access to temporary blocked partitions right.

# Messaging

The control panel can notify about restoration of mainboard AC power supply.

# SMS control only INTEGRA 128-WRL

An option has been added to define the telephone number from which the service technician will send SMS messages containing the alarm system control commands (additional number from which the control panel will accept the control commands in case the SMS control is to be effected only from defined telephone numbers).

# Arming

When arming a partition of With temporary block type, the user can permanently block the partition by entering the blocking time equal to 9 days 99 hours 99 minutes. Only a user having the Access to temporary blocked partitions right will be able to disarm the partition.

# Event log only INTEGRA 128-WRL

The contents of SMS messages received by the control panel is recorded in the event log.

druk (2 na 1):

2,1,2,1