MAGENTA

DIGITAL GLASS-BREAK DETECTOR

magenta_en 06/15

The MAGENTA detector enables detection of plate, tempered or laminated glass breaking. This manual applies to the detector with electronics version 1.1 (or newer).

# Features

Advanced dual path signal analysis.

Stepless regulation of detection sensitivity.

Supply voltage control.

LED indicator.

Tamper protection in 2 ways – cover removal and tearing enclosure from the wall.

# Description

The detector will report the alarm when a low frequency sound (impact) followed by a high frequency sound (glass-break) are registered. The high-frequency channel is analyzed for four seconds from receiving the low-frequency sound wave, caused by the impact.

## Supply voltage control

In the event of a prolonged voltage drop below 9 V (±5%), the detector will signal a trouble. The trouble is indicated by the activation of alarm relay and the steady light of LED indicator. The trouble signaling will continue as long as the trouble persists.

## Electronics board

terminals:

+12V	-	power input +12 V DC (15%),

COM	-	common ground,

TMP	-	tamper output (NC),

NC	-	alarm output (NC).

tamper contact.

red color LED to indicate:

- detection of low-frequency sound – ON for 0.5 seconds,

- alarm – ON for 2 seconds,

- test mode – short flash every 3 seconds,

- low supply voltage – ON.

detector configuration pins:

TEST – enabling/disabling the test mode. In the test mode, the detector reports an alarm when it detects a high frequency sound. The INDIGO TESTER is recommended to test the detector. The test mode is enabled when the jumper is set in ON position (Fig. 2).

LED – enabling/disabling the LED indicator. The LED indicator is enabled when the jumper is set in ON position (Fig. 3).

potentiometer for the adjustment of detection sensitivity (Fig. 4).

# Installation

Curtains, drapes, furniture upholstery, acoustic tiles, etc. absorb the sound and adversely affect the detection range.

Disconnect power before making any electrical connections.

The detector should be installed indoors, in spaces with normal air humidity. The protected glass surfaces must be within the detector operating range. Please note that shades, curtains, furniture upholstery, acoustic tiles, etc. absorb the sound and adversely affect the detector operating range.

- Open the detector enclosure (Fig. 5).

- Make the opening in the enclosure base for the cable.

- Pass the cable through the prepared opening.

- Using wall plugs (screw anchors) and screws, fasten the enclosure base to the mounting surface (Fig. 7). Wall plugs (screw anchors) and screws are included in the detector delivery set.

- Configure the detector using jumpers and the potentiometer.

- Connect the wires to the corresponding terminals on the electronics board.

- Configure the detector using jumpers and the potentiometer.

- Close the detector enclosure.

# Specifications

Supply voltage	12 V DC 15%

Standby current consumption	5 mA

Maximum current consumption	10 mA

Relay contacts rated load (resistive)	40 mA / 16 V DC

Alarm signaling time	2 s

Detection range	up to 6 m

Environmental class according to EN50130-5	II

Operating temperature range	-10...+55 °C

Enclosure dimensions	26 x 112 x 29 mm

Weight	40 g

The declaration of conformity may be consulted at www.satel.eu/ce

SATEL sp. z o.o. • ul. Budowlanych 66 • 80-298 Gdańsk • POLAND tel. 58 320 94 00 www.satel.eu

druk (4 na 1)

4,1,4,1,2,3,2,3