MMD-300

WIRELESS MAGNETIC CONTACT

mmd300_en 04/17

The MMD-300 magnetic contact can detect opening of a door, window, etc. The magnetic contact is supported by:

PERFECTA 16-WRL and PERFECTA 32-WRL control panels,

MICRA alarm module (firmware version 2.02 or newer),

VERSA-MCU controller,

MTX-300 controller.

This manual applies to the device with electronics version 1.4 or newer.

# FEATURES

Two reed switches allowing to select the magnet installation manner.

Input for connecting an NC type hardwired detector.

LED indicator enabled in test mode.

Battery status control.

Tamper protection against cover removal and tearing enclosure from the wall.

# DESCRIPTION

## Alarms

The magnetic contact reports alarm in the following cases:

opening reed switch contacts after removal of magnet,

opening the NC type input,

opening the tamper contact (tamper alarm).

## Operating modes

Normal – each alarm results in sending a radio transmission.

Energy save – after sending information about the alarm caused by opening the reed switch contacts or opening the additional input, the next transmission containing information on this alarm will be sent after 3 minutes at the earliest. Tamper alarms are always sent.

To select between normal mode and energy saving mode, use the E-SAVE MODE pins (Fig. 1).

## Test mode

The test mode is turned on for 20 minutes after inserting the battery or opening the tamper contact. When the test mode is active, the LED is working and the magnetic contact operates like in the normal mode.

## Periodic transmissions

Every 15 minutes, the magnetic contact sends a transmission containing information on the current status of the active reed switch, input, tamper contact and battery. Periodic transmissions are used to monitor presence and operation of the magnetic contact. In the test mode, this transmission is indicated by the LED lighting for 80 milliseconds.

## Electronics board

CR123A lithium battery.

tamper contact.

detector configuration pins:

E-SAVE MODE	-	operating mode selection:

pins shorted – energy save mode;

pins open – normal mode.

SIDE SWITCH	-	selection of active reed switch:

pins shorted – side reed switch;

pins open – bottom reed switch.

terminals:

M	-	NC type input (if no detector is connected to the input, connect the input to common ground).

COM	-	common ground.

The LED and reed switches are placed on the other side of the electronics board.

## LED

The LED is working in the test mode and indicates:

periodic transmission – short flash (80 milliseconds),

alarm – ON for 2 seconds.

## Battery status control

When the battery voltage is below 2.6 V, information about low battery is sent during each transmission.

# INSTALLATION

There is a danger of battery explosion when using a different battery than recommended by the manufacturer, or handling the battery improperly.

Be particularly careful during installation and replacement of the battery. The manufacturer is not liable for the consequences of incorrect installation of the battery.

The used batteries must not be discarded, but should be disposed of in accordance with the existing rules for environment protection.

The device is designed for indoor installation. The detector should be mounted on a fixed surface (e.g. window or door frame), and the magnet on a movable surface (e.g. window or door). Mounting the magnetic contact on ferromagnetic surfaces and/or near to strong magnetic and electrical fields is not advisable, because it can result in malfunctioning of the device.

- Open the enclosure (Fig. 2).

- Configure the magnetic contact by means of jumpers.

- Install the battery in the magnetic contact.

- Enroll the detector in the system (see the PERFECTA / VERSA / VERSA IP / VERSA Plus control panel installer manual, MICRA module manual or MTX-300 controller manual).

- Close the enclosure.

- Put the magnetic contact at the place of its future installation.

- Close and open the tamper contact. If the alarm transmission is received, continue with the installation. If the alarm transmission is not received, select a different mounting location and repeat the test.

- Open the enclosure (Fig. 2).

- If a detector is to be connected to the additional input terminals, make a hole in the enclosure base, run the wires through the hole and fasten them to screw terminals. The maximum permissible length of wires: 3 m.

- Using wall plugs (screw anchors) and screws, fasten the enclosure base to the mounting surface (Fig. 4).

- Secure the magnet, taking into account the maximum permissible distance from the reed switch (Fig. 5). The distance indicated applies to the magnet located at the reed switch height. Location of the reed switches in the enclosure is shown in Fig. 3.

- Close and open the tamper contact to activate the test mode.

- Close the enclosure.

- Check whether the LED lights up:

after moving the magnet away (opening the window / door),

after violation of a detector connected to the additional input.

# SPECIFICATIONS

Operating frequency band	433.05 ÷ 434.79 MHz

Radio communication range (in open area)

MICRA / VERSA-MCU / MTX-300	up to 200 m

PERFECTA	up to 400 m

Battery	CR123A 3 V

Battery life expectancy (energy save mode)	up to 3 years

Additional input sensitivity	312 ms

Standby current consumption	80 µA

Maximum current consumption	27 mA

Environmental class according to EN50130-5	II

Operating temperature range	-10 °C...+55 °C

Maximum humidity	933%

Detector enclosure dimensions	26 x 112 x 29 mm

Surface mounted magnet enclosure dimensions	26 x 13 x 19 mm

Surface mounted magnet spacer dimensions	26 x 13 x 3.5 mm

Flush mounted magnet enclosure dimensions	28 x 10 x 10 mm

Weight	80 g

Hereby, SATEL sp. z o.o., declares that this detector is in compliance with the essential requirements and other relevant provisions of Directive 1999/5/EC. The declaration of conformity may be consulted at www.satel.eu/ce

SATEL sp. z o.o.

ul. Budowlanych 66

80-298 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl

druk (4na1):

4,1,4,1,2,3,2,3