MPT-350

REMOTE CONTROL KEYFOB

mpt-350_en 10/17

The MPT-350 keyfob allows you to remotely control the alarm system or automation devices. The keyfob is supported by:

PERFECTA control panels,

MICRA alarm module (firmware version 3.03),

INT-RX-S expansion module (firmware version 1.04),

VERSA-MCU controller (firmware version 1.04),

MTX-300 controller (firmware version 1.01).

For information on how to add the keyfobs and what functions can be executed by using them, please see the manuals of devices that support the MPT-350 keyfobs.

# Features

Encrypted radio communication in the 433 MHz frequency band.

5 buttons to run up to 6 selected functions.

Key press LED indicator.

# Specifications

Operating frequency band	433.05 ÷ 434.79 MHz

Radio communication range (in open area)	up to 400 m

Battery	CR2032 3V

Environmental class according to EN50130-5	II

Operating temperature range	-10 °C...+55 °C

Maximum humidity	933%

Enclosure dimensions	38 x 78 x 16 mm

Weight	30 g

Hereby, SATEL sp. z o.o., declares that this keyfob is in compliance with the essential requirements and other relevant provisions of Directive 2014/53/EU. The declaration of conformity may be consulted at www.satel.eu/ce

# Battery replacement

There is a danger of battery explosion when using a different battery than recommended by the manufacturer, or handling the battery improperly.

Be particularly careful during installation and replacement of the battery. The manufacturer is not liable for the consequences of incorrect installation of the battery.

The used batteries must not be discarded, but should be disposed of in accordance with the existing rules for environment protection.

The battery life depends exclusively on how the keyfob is used. The more frequently the buttons are pressed, the faster the battery drains. Each transmission sent from the keyfob contains information on the battery status. If the battery is low, pressing the button will make the LED flash once only (normally, the LED is flashing until the button is pressed, but not longer than for 30 seconds).

The keyfob battery replacement is shown in the figures.

SATEL sp. z o.o. • ul. Budowlanych 66 • 80-298 Gdańsk • POLAND

tel. +48 58 320 94 00

www.satel.eu

druk (4na1):

2,1,2,1,2,1,2,1