S-4

MAGNETIC CONTACT

s4_en 07/11

# Features

Surface mounted magnetic contact.

Screw terminals eliminate wires splicing and soldering.

Extra terminal for easy installation of EOL resistor inside the enclosure.

Tamper contact.

Spacers included.

# Installation

The magnetic contact is designed for indoor installation. The switch should be mounted on a fixed surface (e.g. window or door frame), and the magnet on a movable surface (e.g. window or door). Mounting on ferromagnetic surfaces and/or near to strong magnetic and electrical fields is not advisable, because it can result in malfunctioning of the contact.

- Open the enclosure containing the reed switch (undo the screw and remove the cover).

- Make a hole for wires in the base. If a spacer is to be used, the same hole must be made in it as well.

- Screw the wires (and optional resistor) to the appropriate terminals. Description of the terminals:

NC	-	reed switch;

M	-	terminal to facilitate EOL resistor mounting;

TMP	-	tamper contact.

Fig. 1. Ways to connect the wires and resistors for EOL and 2EOL configuration.

- Using screws, attach the base of reed switch enclosure (and, optionally, a spacer) to a flat surface at the selected mounting location. It is advisable that the reed switch mounted in the base be located on the same side on which the magnet will be installed (after the enclosure is closed, the arrow on the cover should point towards the magnet).

- Close the enclosure with the reed switch (replace the cover, insert and tighten the screw).

- Open the enclosure containing the magnet (undo the screw and remove the cover).

- Using screws, attach the base of magnet enclosure (and, optionally, a spacer) to a flat surface opposite the reed switch. The magnet must be located within the operating gap (make distance).

- Close the enclosure with the magnet (replace the cover, insert and tighten the screw).

# Specifications

Contact type	NC

Maximum switching voltage	20 V

Maximum switching current	20 mA

Contact resistance	150 mΩ

Life expectancy (20 V, 20 mA)	min. 360 000 cycles

Contact material	Ru (Ruthenium)

Make distance	18 mm

Break distance	28 mm

Operating temperature range	-30...+55 °C

Maximum humidity	933%

Dimensions:

reed switch enclosure	58,5 x 16,5 x 15,2 mm

reed switch spacer	58,5 x 16,5 x 3,3 mm

magnet enclosure	58,5 x 14,7 x 8,3 mm

magnet spacer	58,5 x 14,7 x 3 mm

Weight	24 g

The declaration of conformity may be consulted at www.satel.eu/ce

SATEL sp. z o.o.

ul. Schuberta 79

80-172 Gdańsk

POLAND

tel. + 48 58 320 94 00

info@satel.pl

www.satel.pl

druk (4 na 1):

2,1,2,1,2,1,2,1