Wired motion detector

for outdoor use

Quick installation guide

outdoor_detector_en 02/20

Full manuals are available on www.satel.eu

The device should be installed by qualified personnel.

Before installation, please read the full manual thoroughly.

Changes, modifications or repairs not authorized by the manufacturer shall void your rights under the warranty.

Do not touch the pyroelectric sensor, so as not to soil it.

Disconnect power before making any electrical connections.

# Selecting a mounting location

The detector can be installed outdoors (1) as well as indoors, in spaces with harsh environmental conditions (high dustiness, high humidity, low or high temperatures, etc.).

Install the detector at the recommended height (2).

Install the detector at a roofed location (2) or under a protective roof (3), where streams of water from rain or melting snow will not run down the enclosure

When choosing the installation location, keep in mind that the detector performance will be the best where the expected direction of the intruder movement will be across the coverage pattern (4).

Don’t install the detector closer than 3 meters from the moving objects (eg. tree branches, bushes, laundry etc.) (5).

Do not install the detector in places where it will be exposed to direct sunlight (6) or light reflected from other objects (7).

Do not point the detector towards fans or heat sources (8).

# Installation

- Open the detector enclosure.

- Remove the electronics board.

- Make holes for screws and wires in the base of the detector enclosure.

To ensure tightness of the enclosure, make the holes only at places specially intended for this purpose, which are provided with sealing material around the inner side of the base.

- Run the wires through the hole made.

When putting two or more cables into the enclosure, it is advisable to place them in heat shrink tube. It reduces the risk of getting water into the enclosure.

- Using wall plugs (anchors) and screws, attach the enclosure base to the mounting surface or to the bracket. The type of wall plugs (anchors) must be suitable for the mounting surface.

- Fasten the electronics board.

- Connect the wires to the appropriate terminals.

If the detector with active IR anti-mask feature has been installed outdoors, do not connect the anti-masking output to the control panel. Harsh weather conditions such as rain, fog or frost can be interpreted by the anti-mask system as an attempt to mask the detector.

- Configure the detector settings (see full detector manual).

- Close the detector enclosure.

# Start-up and walk test

If you start the detector with the active IR anti-mask feature, keep in mind that the detector enclosure must be closed and the detector must be in no way obstructed.

The detector LED(s) should be enabled during walk test.

- Power on the detector. Warm-up of the detector will be indicated by flashing of the LED(s).

- When the warm-up indication is finished, check that movement within the detector coverage area will make the LED(s) turn on.

- If necessary, change the sensitivity of the detector sensor(s).

The declaration of conformity may be consulted at www.satel.eu/ce

SATEL sp. z o.o. • ul. Budowlanych 66 • 80-298 Gdańsk • POLAND

tel. +48 58 320 94 00

www.satel.eu