SX6-TO

OPTICAL ANTI FOAM DETECTOR

sx6-to_en 10/14

The SX6-TO anti foam detector detects an attempt of damping the siren with acoustical signaling with PUR foam. The detector is dedicated to be mounted in Satel's SD-6000 outdoor siren.

Note:	The SX6-TO detector can only be installed in the SD-6000 sirens manufactured after 1 August 2014.

# Electronics board

Fig. 1. Electronics board of SX6-TO detector.

transmitter and receiver diodes.

LED (red). The LED is ON when there is no communication between the transmitter and receiver diodes. It goes on about 2 seconds after the infrared beam is broken, and goes off immediately after the obstacle is removed.

relay.

terminals:

TMP	-	tamper output (relay output).

COM	-	common ground.

12V	-	power input.

# Installation

Disconnect power before making any electrical connections.

- Insert the SX6-TO board into its holders in the enclosure base of the siren.

- Connect power cables to the 12V and COM terminals.

- Connect the TMP terminals in series with the tamper switch of the siren.

Fig. 2. Installation of the SX6-TO detector in SD-6000 siren enclosure.

# Specifications

Supply voltage	12 V DC 15%

Standby current consumption	35 mA

Maximum current consumption	45 mA

TMP output rating	40 mA / 16 V DC

Environmental class according to EN50130-5	III

Operating temperature range	-25(C …+55(C

Maximum humidity	933%

Dimensions	97x53 mm

Weight	12 g

The declaration of conformity may be consulted at www.satel.eu/ce

SATEL sp. z o.o. • ul. Budowlanych 66 • 80-298 Gdańsk • POLAND tel. + 48 58 320 94 00 info@satel.pl • www.satel.eu

druk (4 na 1):

2,1,2,1,2,1,2,1