Page 4

integration with KNX standard (with INT-KNX-2 module)

page 9

ACU-120 / ACU-270

Wireless system controllers

compatible with INTEGRA and VERSA control panels

operating range up to 500 m open space

support for up to 48 wireless devices

support for up to 8 wireless keypads

support for up to 248 wireless APT-100 keyfobs

programming controller settings via control panel service menu and DLOADX program

firmware update without dismantling of device

antenna diversity – automatic antenna selection, depending on received signal strength – only RX reception (ACU-120)

tamper protection

page 14

touchscreen keypads, LCD vagy LED kezelők (up to 6)

mobile application

proximity tags/cards

helyi – LCD keypad or computer (with DLOADX program), connected to RS-232 TTL port

távoli – vezérlőpanelhez modem vagy Ethernet hálózat segítségével csatlakozó számítógép

távoli – computer connecting to the control panel via GPRS (VERSA Plus)

Characteristic features of VERSA Plus control panel:

built-in Ethernet, GSM / GPRS, voice and acoustic alarm verification modules:

Ethernet (mobile application, PUSH notifications, e-mail messages, reporting to monitoring station)

GSM/GPRS (SMS, CLIP, reporting to monitoring station)

PSTN (voice messaging, reporting to monitoring station)

USB communication port

remote service access via TCP/IP, GSM/GPRS and PSTN

one potential-free relay output

efficient 2 A power supply

built-in audible signaling

APPLICATION FOR OPERATING VERSA SYSTEMS

VERSA CONTROL

Application for remote control of the VERSA system by using smartphones and tablets

available in versions for Android, iOS, Windows Phone systems

allows you to:

check the system status

check the zone status

check the output status

view the current troubles

view all system events

use instant PUSH notifications of system events

Page 15

fully wireless communication with VERSA control panel (VERSA-LCDM-WRL)

ACU-120 or ACU-270 controllers required for operation (VERSA-LCDM-WRL)

proximity card reader (VERSA-LCDM-WRL)

power: two lithium batteries 3 V CR123A (VERSA-LCDM-WRL)

Page 23

Built-in communicator: PSTN / GSM / ETHERNET

Operation via web browsers / mobile applications

Page 26 – text from page 9

Page 55

CZ-USB-1

Proximity card reader

operation in Windows environment

operation at 125 kHz frequency

Page 64

USB-RS

USB-RS converter

appropriate for the SATEL devices provided with the following port:

RS-232 – PIN5 or RJ type connector

RS-232 (TTL) – PIN3 or RJ type connector

suitable for programming SATEL radio controllers

4 cables terminated with appropriate plugs

USB type B socket for connecting the converter to the computer

delivered with a USB cable (1.8 m)

RJ/PIN5-LCD

RJ to PIN-5 adapter

dedicated to work with LCD keypads for INTEGRA and CA-10 control panels

designed for use with: GSM-4, GSM-5, GSM LT-1, GSM LT-2, ACU-100, VIVER

RJ/PIN3

RJ to PIN-3 adapter

designed for use with: ACTIVA, GPRS-T1, GPRS-T2, GPRS-T4, GPRS-T6, MICRA

PIN5/RJ-TTL

RS-232 TTL cable

cable for connecting of ETHM-1 and ETHM-1 Plus module with VERSA

PIN5/PIN5

RS-232 TTL cable

cable for connection of RS Ports of INTEGRA and CA-64 panels equipped with PIN5 connector and modules equipped with PIN5 connector: MDM56 BO, GSM-4, GSM-5, GSM LT-1, GSM LT-2, ISDN-MOD, ETHM-1, ETHM-1 Plus

RJ/PIN5

RS-232 cable

cable for connection of RS Ports of INTEGRA panels equipped with RJ connector and modules equipped with PIN-5 connector: MDM56 BO, GSM-4, GSM-5, GSM LT-1, GSM LT-2, ISDN-MOD, ETHM-1, ETHM-1 Plus

ANT-900/1800

GSM antenna

900/1800 MHz antenna for modules: GSM-4, GSM-5, GSM LT-1, GSM LT-2, GPRS-T1, GPRS-T2, GPRS-T4, GPRS-T6, MICRA, INTEGRA 128-WRL, VERSA Plus

ANT-OBU-Q

GSM antenna

GSM quad-band antenna for following modules: GSM-4, GSM-5, GSM LT-1, GSM LT-2, GPRS-T1, GPRS-T2, GPRS-T4, GPRS-T6, MICRA, INTEGRA 128-WRL, VERSA Plus