GPRS-A

Universal monitoring module

GPRS-A is a universal monitoring module, provided with GSM telephone, supporting data transmission in 2G technology. The device is an extension for intruder alarm systems as well as for automation systems.

It provides effective reporting from the alarm control panel to the monitoring station and notifies the concerned parties about selected events. Thanks to its configurable inputs that support digital and analog signals, it can be used to supervise operation of any sensors measuring different physical quantities and report instances when the set thresholds are exceeded.

To allow the module to interact with prepaid SIM cards, it has been provided with functions required for checking the account balance and setting notifications about exceeding the minimum amount.

Full flexibility

The module is capable of monitoring any intruder alarm or automation system. It can be successfully used in many existing, as well as newly built systems. When working in conjunction with the alarm control panel, it can receive information about events, thus simulating the monitoring station. When used with simpler models of control panels or when supervising processing lines etc., it will track changes in the status of its inputs. The received information is transmitted by the module to security agency monitoring stations or any parties concerned.

GPRS-A can be used as a stand-alone device, e.g. as a controller intended to supervise processing lines, automation systems, etc.

Event reporting

As regards reporting, information can be effectively transmitted via:

- GPRS – using TCP or UDP protocols

- SMS messages.

Where events are being shared in GPRS technology, the module supports two transmission formats:

- SIA-IP (when working with any monitoring station)

- SATEL (when working with SATEL made devices: STAM-2 monitoring station or TCP/IP to audio formats reporting converter SMET-256).

Notification messaging

The GPRS-A module can send notifications to up to 8 telephone numbers. This function can be implemented by using:

- SMS messages

- PUSH messages

- CLIP service.

The device can send notifications to the recipient through several independent paths. Since the event alert will be transmitted via all of the preprogrammed channels, the information will reach the recipient even when one of them turns out to be unavailable.

[Podpis: An easy and reliable way to deliver information.]

Remote control

GPRS-A has 4 outputs that can be remotely controlled and activated from practically any location in several ways:

- via SMS messages (from 8 numbers)

- from GX CONTROL mobile application

- from a computer with GX Soft program installed

- using CLIP service (from 64 numbers or with no limitations).

In addition to alarm systems, the GPRS-A module will be a perfect choice to implement automation functions, including control of lighting, gates, wickets, roller shutters, solenoid valves, etc. If needed, it will turn on heating, air conditioning, smoke extraction, watering and many other systems.

Interaction with detection, measuring and other devices.

GPRS-A can be used in conjunction with a number of devices having normally open (NO) or normally closed (NC) connectors. Signals from analog sensors and digital-to-analog converters can be fed into the inputs of the module, which offers a great many possibilities for its use.

Whenever needed, the module will convert (rescale) the received signal to any unit of measure, including temperature or other physical quantities. Exceeding one of the thresholds set by the installer (either lower or upper) will result in:

- sending a report to monitoring stations

- sending a notification to selected people

- automatic response of the module i.e. execution of the preset action.

Digital data collection

The device is provided with a digital 1-Wire sensor bus. This allows up to 8 detectors to be connected, the maximum bus length being up to 30 m. For example, using the SATEL DS-T1 or DS-T2 sensors will enable the GPRS-A module to perform very well in any location where the temperature measurement is crucial.

Monitored logistics

GPRS-A is powered with 12 V DC voltage, so it will find its use as a stand-alone device in passenger cars, trucks, caravans, yachts, etc. The module will protect the interior of the given object by sending remote notification that the door has been opened or an attempt has been made to start the engine.

As it can work e.g. with temperature and humidity sensors, the module will easily do its job monitoring environmental conditions during transportation of food, medicines, etc. by:

- sending information about selected parameters in real time

- triggering alarm when preset limits are exceeded or input state changes

- responding to specific events.

IoT - Internet of Things

A solution that has never been used before is interaction of the universal communication module with automation and data acquisition systems. It consists in transmission of the measurement data via GPRS, using open communication protocols. Thus, operation of GPRS-A becomes part of the Internet of Things concept.

The IoT function, available in the GX Soft configuration program, allows sending data from multiple devices to one point (central server), from which it is also possible to remotely control the outputs of all connected modules. The system built in this way is scalable, and the number of integrated GPRS-A modules depends only on the capabilities of the server itself.

Collecting information from many modules in one place makes it possible to create a tool to supervise, for example, a fleet of vehicles.

Interface and integration

GPRS-A supports three non-proprietary, open communication protocols: MQTT, JSON and MODBUS RTU. Consequently, the users gain a very wide range of possibilities of using, processing, collecting and visualization of data. Information sent by the module can be processed both in programs available on the market and in applications created from scratch.

Mobile access

Mobile applications designed for remote operation of various devices are becoming an increasingly popular solution, valued for convenience of use. GX CONTROL is a program created for the needs of SATEL communication modules and intended for Android and iOS platforms. Its tasks include:

- verification of the status of inputs and outputs (of connected sensors and devices)

- display of indications from analog inputs and digital sensors

- viewing troubles with trouble memory clearing option

- viewing event memory with filtering capability

- remote control of module outputs (devices connected to them).

PUSH messages give the user permanent access to notifications. Importantly, configuration of the application is very simple, and so is connection with the module. Just send an SMS from the application level to the device and receive the configuration data in response. Another, equally convenient way is to scan the QR code that is generated in the GX Soft program.

[grafika: telefon i kilka ekranów z aplikacji; zaznaczenie dostępności dla dwóch platform: Android i iOS]

Functional software

GX Soft is a versatile tool with a friendly and clear interface, intended for configuration as well as diagnostics of SATEL communication modules. It gives the installer access to all functions of the device and enables him to program operation of the module so that it can meet requirements of the specific system, as well as expectations of the system users. The module and the program can interact locally (via RS-232 (TTL)) or remotely (via GPRS).

[grafika: komputer z GX Soft]

Easy and secure connection

Connecting the GX CONTROL application and the GX Soft configuration program to the GPRS-A module takes just a few moments. The process requires neither external IP address nor advanced network configuration. The SATEL connection set-up service provides a simple way to enjoy many GX CONTROL and GX Soft functionalities. When being sent, the data are encrypted using a sophisticated algorithm to ensure security of the transmission.

Remote software update

GPRS-A is compatible with the UpServ program, which enables the device to be remotely updated. Thus you can quickly and easily add new functionalities from any location and at any moment without having to physically visit the premises where the communication modules are installed.

Reporting events

- reporting sources:

  - control panel audio reporting

  - internal events

  - input violation

  - output status change

- reporting paths:

  - SMS

  - GPRS (TCP / UDP)

Notification messaging

- notification sources:

  - control panel audio reporting

  - internal events

  - input violation

  - output status change

- notification options:

  - SMS

  - PUSH

  - CLIP

Remote output control

- SMS

- CLIP

- GX CONTROL mobile application

- GX Soft configuration program

Interaction with all control panels

- programmable inputs

- outputs with remote control capability

- converting audio reporting (PSTN) into SMS, TCP / UDP formats

Input types:

- digital (NO, NC)

- analog

- 1-Wire digital sensor bus

Interaction with central server - IoT function:

- receiving and collecting data from multiple devices

- using transmitted information in any data acquisition systems

- remote control of integrated module outputs

Support for open communication protocols (via GPRS):

- MQTT

- JSON

- MODBUS RTU

GX CONTROL mobile application for Android and iOS

- checking input status with bypassing capability

- displaying indications from analog inputs

- presentation of readings from connected digital sensors

- controlling and checking output status

- viewing troubles with memory clearing capability

- viewing event memory with filtering capability

- PUSH notifications

GX Soft configuration program

- intuitive interface

- full module configuration

- viewing event log

- fault diagnostics

# Text boxes

NOTIFYING  SELECTED PARTIES OF EVENTS

INTERACTION WITH  1-WIRE DIGITAL SENSORS

AUTOMATIC CONTROL

SUPPORT FOR DIGITAL AND ANALOG SIGNALS

IMPLEMENTATION OF REMOTE CONTROL FUNCTION

SENDING INFORMATION TO SECURITY AGENCY MONITORING STATION

REPORTING

output status change

control panel audio reporting

NOTIFICATION

MONITORING STATION

input violation

internal events

OUTPUTS - CONTROL

INPUTS - MEASUREMENTS

OUTPUTS - CONTROL

INPUTS - MEASUREMENTS

OUTPUTS - CONTROL

INPUTS - MEASUREMENTS

VISUALIZATIONS

REPORTS

DATABASES

SATEL CONNECTION SETUP SERVICE