OUTDOOR DUAL-TECH MOTION DETECTORS

OPAL, OPAL Plus, OPAL Pro

OUTDOOR PIR+MW DUAL-TECH MOTION DETECTORS

high resistance to adverse weather conditions

- reliable operation

- active IR anti-masking (OPAL Pro)

- immunity to pets

- tamper protection against removal from mounting surface and opening of enclosure

Reliable detection owing to advanced design

can be used in building automation systems, thanks to built-in dusk sensor

BRACKETS: ANGLE AND BALL TYPE

selectable mounting method, thanks to dedicated ball-type and angle-type brackets

easy remote sensitivity configuration of all detection circuits and dusk sensor using OPT-1 keyfob (OPAL Plus/OPAL Pro)

ADVANCED OUTDOOR DETECTORS

When planning an alarm system, one should not focus solely on detecting the presence of an intruder inside the protected premises. It is equally or perhaps even more important that he be detected before causing any damage to the building. Such an attempt to penetrate the outer zone of protected premises will be detected by the OPAL detectors.

APPLICATION

OPAL, OPAL Plus and OPAL Pro provide excellent outdoor protection in buildings of various types and purpose. These devices will also perform very well as the indoor protection in industrial buildings where difficult or specific environmental conditions prevail (in halls, shelters, sheds etc.). The OPAL series detectors can also be used for the implementation of alarm systems with home automation. This is made possible by a dusk sensor with which OPAL Plus and OPAL Pro are fitted. You can directly control the relays located in electrical distribution board or the automation controllers. These detectors can also interface with the KNX system via an INTEGRA series control panel, which allows you to easily and conveniently control the roller shutters, exterior lighting of the building, garage door, entrance gate, etc. The moment of operation can be selected through fine sensitivity adjustment.

OPERATING RANGE

Detection angle of the OPAL detectors is as high as 100 degrees and their range exceeds 15 m. The look down zone is also protected, so any intruder's attempt to creep up on the device to damage it or tear off the wall will be detected. Additionally, the detector software is designed so as to prevent false alarms from being triggered by the movement of small pets.

maximum range

average range

minimum range

range - top view

range - side view

RESISTANCE TO WEATHER CONDITIONS

The SATEL outdoor detectors offer stable performance regardless of whether they work in rain, in bright sunlight, during strong gusts of wind or in very high or very low temperatures. This functionality is provided by a combination of dual technology of detection and an algorithm of auto-adaptation to environmental conditions with automatic compensation for changes in ambient temperature.

Resistance of the OPAL series detectors to severe weather conditions has been confirmed in comprehensive long-term tests.

TEMPERATURE COMPENSATION

time

sensitivity

temperature (°C)

ANTI-MASKING PROTECTION

OPAL Pro is provided with an active IR anti-masking function, so it will detect any attempt to cover the detector lens with paint or lacquer, or with materials of different thickness, color and texture.

In OPAL and OPAL Plus, the anti-masking function is implemented in the microwave circuit, which enables detection of objects moving around in close proximity to the detectors.

DETECTOR DESIGN

PIR sensor

additional service mode input

independent dusk sensor output

IR receiver for OPT-1 keyfob

manual sensitivity control

anti-masking circuit LEDs

tamper switch

dusk sensor

24 GHz microwave sensor

* The illustration shows OPAL Pro detector design

High quality of the detectors of OPAL series results from combining the latest technology and many years' experience of SATEL specialists in the design and production of devices for intrusion and hold-up alarm systems. This is evidenced by the design of detectors, both their electronics and the enclosure itself.

Enclosures of the detectors are made of a combination of polycarbonate and thermoplastic elastomer using two-component injection technology. The thus obtained design is IP54 rated, which makes the detectors splash-proof and suitable for outdoor applications as well. The enclosure protects electronic circuits of the device against potentially harmful phenomena, such as rain, snow, fog or moisture. Moreover, the detectors are characterized by a high mechanical strength and resistance to UV radiation, so their appearance remains unchanged for many years.

elastomer

polycarbonate

USEFUL FEATURES AND EXTRA COMPONENTS

REMOTE CONFIGURATION OF SENSITIVITY

A big help for the installer is the ability to remotely change the sensitivity of all detection circuits and dusk sensor in OPAL Plus and OPAL Pro detectors by using the OPT-1 IR keyfob. This feature makes the control easy, as you do not need any more to frequently open the device enclosure to do the job. The CR2032 battery powered keyfob ensures several thousand adjustments.

MOUNTING METHODS

Design of the OPAL series detector makes it possible to mount it directly on a flat surface, e.g. where the small pet immunity option is to be used. If, however, for the optimum coverage of the protected area, it is necessary that the detector be mounted at a different angle, you can use the dedicated BRACKET C set of brackets.

The ball-type bracket allows you to control the detector tilt angle in two planes: up to 60°vertically and up to 90° horizontally. This makes it easier to find the optimum position relative to the protected area. If the premises require that the detector be set permanently at an angle of 45° to the wall, you can use the angle-type bracket.

WIRING

In the case of devices installed outdoors, it is extremely important to guarantee the security and reliability of their operation. For this reason, the above mentioned brackets are designed so that the cable which connects the detector to the control panel is running inside them. This makes the whole system both secure and aesthetic.

TAMPER PROTECTION

Regardless of which type of bracket is used, the detectors of OPAL series will always be protected against opening and removing them from the mounting surface. This protection is provided by two tamper switches located on the PCB and a specially designed contact that can be mounted in the ball bracket or at the back panel of the detector (if the angle bracket is used).

AOD-200 - WIRELESS OUTDOOR PROTECTION

Protection can also be provided outside of the building which is to be secured, even where using wired devices is not possible. The AOD-200 outdoor wireless detector, which is designed to work as part of the ABAX two-way system, is ideally suited for such applications.

ABAX

wireless system controller or radio signal repeater

up to 500 m in open area

SUMMARY OF FEATURES AND CHARACTERISTICS

|  | OPAL | OPAL Plus | OPAL Pro | AOD-200 |
| --- | --- | --- | --- | --- |
| Two detection circuits: PIR+MW |  |  |  |  |
| Active IR anti-masking according to EN 50131-2-4 for Grade 3 | - | - | * | - |
| Anti-masking in microwave circuit |  |  | - | - |
| Built-in dusk sensor enabling the detector to be used in automation systems | - |  |  |  |
| Built-in receiver of IR OPT-1 keyfob signal | - |  |  | - |
| Remote sensitivity configuration of detection circuits and dusk sensor with OPT-1 keyfob without having to open detector enclosure | - |  |  | - |
| Sensitivity configuration of dusk sensor by using PCB located buttons | - |  |  | - |
| Sensitivity configuration of detection circuits by using PCB buttons |  |  |  | - |
| Remote sensitivity configuration of detection circuits and dusk sensor from DLOADX | - | - | - |  |
| Reinforced polycarbonate enclosure |  |  |  |  |
| Splash-proof enclosure, IP54 rated |  |  |  |  |
| Digital temperature compensation |  |  |  |  |
| Auto-tuning algorithm for high immunity to false alarms |  |  |  |  |
| Ability to work in adverse weather conditions (rain, snow, fog, strong wind) |  |  |  |  |
| Tamper protection (against opening and removal) |  |  |  |  |
| Low current consumption |  |  |  |  |
| Dedicated angle-type bracket (45°) |  |  |  |  |
| Dedicated ball-type bracket (tilting up to 60° vertically and up to 90° horizontally) |  |  |  |  |
| Wires running inside the bracket for better protection |  |  |  |  |
| Optional installation without any additional bracket |  |  |  |  |
| White enclosure front back |  |  |  |  |
| Gray enclosure front back |  |  |  |  |

* for indoor applications

TECHNICAL PARAMETERS

|  | OPAL | OPAL Plus | OPAL Pro | AOD-200 |
| --- | --- | --- | --- | --- |
| Environmental class | III A | III A | III A | III A |
| Security rating | acc. to Grade 2 | acc. to Grade 2 | acc. to Grade 3* | acc. to Grade 2 |
| Enclosure dimensions | 65 x 138 x 58 mm | 65 x 138 x 58 mm | 65 x 138 x 58 mm | 65 x 138 x 58 mm |
| Operating temperature range | from -40°C to +55°C | from -40°C to +55°C | from -40°C to +55°C | from -35°C to +55°C |
| Recommended installation height | 2.4 m | 2.4 m | 2.4 m | 2.4 m |
| Standby current consumption | 12 mA | 15 mA | 17 mA | 70 µA |
| Maximum current consumption | 20 mA | 20 mA | 30 mA | 30 mA |
| Operating range | 15 m | 15 m | 15 m | 15 m |

* for indoor applications

LIST OF PRODUCTS

OPAL / OPAL GY

Outdoor PIR+MW dual-tech motion detector

OPAL Plus / OPAL Plus GY

Outdoor PIR+MW dual-tech motion detector

OPAL Pro / OPAL Pro GY

Outdoor PIR+MW dual-tech motion detector

AOD-200 / AOD-200 GY

Outdoor wireless PIR+MW dual-tech motion detector

OPT-1

IR keyfob

BRACKET C / BRACKET C GY

Set of wall brackets for mounting outdoor detectors