Customization of the access code

OPERATIONS TO BE MADE ON THE KEYPAD

1.	Key in # +PROGRAMMING CODE+ #

Signalling: 1 BEEP of 1,5 sec. + L1 and 12 on for 1,5 sec.

2.	Key in within a minute the KEY 2 + #

Signalling: 2 BEEP + L2 on

3.	Key in the NUMBER OF THE CHOSEN CHANNEL + #

Signalling: 1 BEEP of 1 sec. + 12 on

4.	Key in the NEW ACCESS CODE + #

Signalling: 1 BEEP of 1 sec. + L2 on

5.	Repeat the NEW ACCESS CODE + #

Signalling:      - 1 BEEP of 3 sec. + LI and L2 on if the operation is correct;

-	short flashes of the LED if incorrect

Disabling a channel

OPERATIONS TO BE MADE ON THE KEYPAD

1.	Key in # 4- PROGRAMMING CODE + #

Signalling: 1 BEEP of 1,5 sec. + LI and L2 on for 1,5 sec.

2.	Key in within a minute the KEY 2 + #

Signalling: 2 BEEP + L2 on

3.	Key in the NUMBER OF THE CHOSEN CHANNEL + #

Signalling: 1 BEEP of 1 sec. + L2 on

4.	Key in the KEY 0 + #

Signalling: 1 BEEP of 1 sec. + L2 on

5.	Repeat the KEY 0 + If

Signalling:      -1 BEEP of 3 sec. + L1 and L2 on if the

operation is correct;

-	short flashes of the LED if incorrect

3. WORKING MODE: ROYAL, 53200 or

PERSONAL PASS

Select the working mode according to the kind of remote controls already used in the system.

OPERATIONS TO BE MADE ON THE KEYPAD

1.   Key in # + PROGRAMMING CODE + #

Signalling: 1 BEEP of 1,5 sec. + LI and L2 on for 1,5 sec.

2.  Key in within a minute the KEY 3 +

Signalling: 3 BEEP + L1 and L2 on

3.  •    Key in the KEY 1 + # to select ROYAL mode

- Key in the KEY 2 + # to select 53200 mode

- Key in the KEY 3 + # to select PERSONAL PASS mode
Signalling: 1 BEEP of 1 sec.

4.  Repeat to confirm (1 + # or 2 + # or 3 + #)

Signalling:      -1 BEEP of 3 sec. + L1 and L2 on if the

operation is correct; - short flashes of the LED if incorrect

4. DIP-SWITCH CODE (only version Royal/53200)

The factory dip-switch code set for channel 1 is 0101010101 00.

If other remote controls are already stored on the receiver, the dip-switch code of the keypad has to be set with the same sequence of the one set on the dip-switch of the remote control.

The dip-switch of the remote control is made up by a series of 12 micro switches set to ON or OFF.

To set the same code on the keypad, it is necessary to key in a code made up of 12 digits: those will be 0 or 1, depending on the position of the micro switches on the remote control

- micro switch set to ON = 1

- micro switch set to OFF= 0

If the transmitter is single channel, the dip-switch to be set coincides with the position of the 12 micro switches.

If the transmitter is two-channel and the key stored is 2, the dip-switch code to be set coincides with the position of the 12 micro switches: If the key stored on the receiver is the key 1; the dip-switch <5&de coincides with the position of the micro switches from 1 to'1Q plus the 2 digit 00.

If the transmitter is four-channel, the dip-switch code to be set coincides with the position of the micro switches from 1 to 10 plus 2 digits, which are:

- 00 if the key stored on the receiver is the key 1
(e.g. 101010101000)

- 10 if the key stored on the receiver is the key 2
(e.g 101010101010)

- 01 if the key stored on the receiver is the key 3
(e.g. 101010101001)

- 11 if the key stored on the receiver is the key 4
(e.g. 101010101011)

If no transmitter has been stored on the receiver, the

dip-switch code can be set entering a random sequence of 12 digits 0 or 1.

OPERATIONS TO BE MADE ON THE KEYPAD

1.	Key in # + PROGRAMMING CODE + #

Signalling: 1 BEEP of 1,5 sec. + L1 and L2 on for 1,5 sec.

2.	Key in within a minute the KEY 4 + #

Signalling: 4 BEEPs + L1 and L2 flashing alternately

3.	Key in the NUMBER OF THE CHOSEN CHANNEL + #

Signalling: 1 BEEP of 1 sec. + L1 and L2 flashing alternately

4.	Key in the CHOSEN DIP-SWITCH CODE + #

gh'sst to ON = 1 Micro switch set to OFF « 0

Signalling:      -1 BEEP of 3 sec. + L1 and L2 on if the

operation is correct; - short flashes of the LED if incorrect

DECLARATION OF CONFORMITY

V2 S.p.A. hereby declare that SIRMO-DIGIT equipment conforms to the essential requirements established in the electromagnetic compatibility directive

93/68/EEC     electromagnetic compatibility 2006/95/EEC electrical safety 99/5/EEC       directive radio

and that the following technical standards have been applied EN 60950, EN 301 489-1, EN 301 489-3, EN 300 220-1

Racconigi, 9 July 2007

Legal representative, V2 S.p.A.

A. Livio Costamagna